| 1030518 75838 |  |
| --- | --- |
| FACILITY: Lantmannen Unibake USA, Inc. | PERMIT ID: 2793 |
| EuroBake | DISTRICT: Southwest |
| ADDRESS: 1927 4th Avenue South | CONTACT PHONE: |
| St. Petersburg, FL | 727-823-1113 |
| ARMS NO: 1030518 005 | PERMIT NO: | Expiration Date: 2/28/2013 Renewal Date: 12/30/2012 |
|  | 1030518-006-AF |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Mecatherm B baking line and associated equipment. Serial No. 500151. bread production capacity of 2.2046 tons/hour and 19,312 tons/year. Total design heat input rate of 4.167 MMBtu/hours |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | September 13, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: File reviewed |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met on site with the responsible official |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: David Leibensperger? |  | Yes |  | No |
|  | Comments: Reviewed records and toured the facility with Mr. Leibensperger The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: David Leibensperger? |  | Yes |  | No |
|  | Comments: Yes The facility contact’s e-mail is: david.leibensperger@lantmannen.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( |  |  | Permitting Note: This permit became effective on11/17/2008. This permit incorporate changes from 1030518-003-AC. This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. - General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. 4. General Visible Emission Limitation - No person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). The facility may add control type devices or work practices to reduce visible emissions below the facility wide opacity limit while baking the seeded breads that contain cheese ingredients. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] Comments: There were no exceedance of the visible emissions limitations observed during survey of outside of building as looking at the flour silos, not loading at time of inspection,. The ovens were in operation. There were no emissions observed from the stack vents. The facility continues to use parchment paper on pans instead of mineral oil to prevent emissions. (see photos) 5. Objectionable Odor - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere that by itself or in combination with other odors is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200, Definitions-(Objectionable Odors), F.A.C., Pinellas County Code Subsection 58-178] Comments: There were no objectionable odors detected off the property. There was mild bread baking odor in the building. 6. Circumvention - No person shall circumvent any air pollution control device, or allow the emission of air pollutants without the applicable air pollution control device operating properly. [Rule 62-210.650, F.A.C.] Comments: there are no pollution control devices for the emissions unit of this facility, and no circumvention evident. 7. Unconfined Particulate Matter - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320(4)(c)., F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions include the following: Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. Landscaping or planting of vegetation. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. Confining abrasive blasting where possible. [Rule 62-296.320(4)(c), F.A.C. and Construction Permit No. 1030518-003-AC] Comments: This facility does not have operations which generate unconfined emissions outside of the building. There are no particulate matter activities associated with the roads, or landscaping requirements. There is no use of hoods inside for the collection of emissions inside the building from the ovens. There is no abrasive blasting performed at this bread making facility. 8. Excess Emissions Startup/Shutdown/Malfunction – Excess emissions resulting from startup, shutdown, or malfunction shall be permitted providing (1) Best operational practices to minimize emissions are adhered to and (2) The duration of excess emissions shall be minimized but in no case exceed two (2) hours in any 24 hour period unless specifically authorized by the Department for a longer duration. Poor Maintenance/Operation, Equipment/Process Failure – Excess emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. Excess Emissions Recordkeeping – The permittee shall maintain records of the occurrence and duration of any startup, shutdown, or malfunction in the operation of this facility which results in excess emissions; any malfunction of the air pollution control equipment; and any periods during which a continuous monitoring system or monitoring device is inoperative. Records shall be maintained at the facility and be available to the Department and/or PCDEM for inspection upon request. [Rules 62-4.070(3) and 62-210.700, F.A.C.] Comments: There were not any excess emissions observed or reported, no shutdown. The facility is clean and well maintenance no malfunctions or upset conditions were noted to have occurred. (see photos) 9. Special Compliance Test – If the Department and/or Pinellas County Department of Environmental Management (PCDEM), after investigation, have good reason (such as complaints, increased visible emissions or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it shall require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emissions unit and to provide a report on the results of said tests to the Department and the PCDEM. [Rule 62-297.310(7)(b), F.A.C.] Comments: There are no special compliance test requirements for this facility. The dept had not received any citizen complaints related to activities performed at this source. 10. Annual Operating Report (AOR) Requirement - On or before April 1 of each year, submit to the Air Compliance Section of the Department's Southwest District Office and the PCDEM (unless otherwise directed by the Department), an Annual Operating Report [DEP Form No. 62-210.900(5)] for the preceding calendar year. Note, the annual operating report for calendar year 2008 shall be submitted by May 1, 2009. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be submitted. [Rule 62-210.370(3), F.A.C.] Comments: The facility submitted the 2010 AOR on 3/6/2011 and completed review 4/6/2011. 11. Records Retention – All monthly records shall be completed by the end of the following month. All records required by this permit shall be maintained at the facility for at least three years, unless otherwise noted, and be made available to the Department and/or PCDEM for inspection upon request. [Rule 62-4.160(14)(b), F.A.C.] Comments: The facility continues to maintain records back to 2007 in hard copy and on Mr. Leibensperger’s personnel office computer. Their records are also maintained through their consultant Marvin Scott of Southern Environmental Engineers. Operation Permit Renewal 12. Permit Renewal Application – A completed application to renew this operation permit shall be submitted to the Air Permitting Section of the Department’s Southwest District Office with a copy sent to the PCDEM no later than 60 days prior to the expiration date of this permit. To properly apply for an operation permit renewal, the applicant shall submit the following: The appropriate operation permit application form (see current version of Rule 62-210.900, F.A.C. and /or FDEP Division of Air Resource management website at: http://www.dep.state.fl.us/air/); The appropriate operation permit application fee (see Rule 62-4.050(4)(a), F.A.C.); Copies of the records specified in Specific Condition No. 14 for the most recent 2 months of operation. [Rules 62-4.070(3), 62-4.090, 62-210.300(2) and 62-210.900 F.A.C.] Comments: the facility permit does not expire until 2/28/13. I reminded Mr. Leibensperger, that the renewal would be due by 2/30/12. He placed a reminder in his work calendar. EMISSION UNIT ID 001, 002, 005 13. Emissions Limits – VOC emissions from emission units 001, 002, and 005 shall not exceed the following limit: E.U. ID No. Annual VOC Emissions (Any consecutive 12-month period) 001 19.3 tons 002 15.5 tons 005 38.6 tons [Rule 62-210.200, F.A.C. – Definitions (PTE) and Permit 1030518-001-AF and Construction Permit 1030518-003-AC] Comments: Review of the records show the facility is well below the emissions limitations of this permit. The limitations were calculated for the facility operating at full capacity continuously for all emissions unit 24/7. This means all ovens would have to be operating continuously to exceed permit limitations. Mr. Leibensperger stated they are making some conversions to the Baking Line #2 (Rheon Line) equipment on 002 to allow them to use it to make the same product as unit 1. This will allow them some flexibility for productions. The highest production month for the Mecatherm B baking line was April 2011 at 734.67 tons of bread baked and 1.47 tons VOC emission per month. The 12 month consecutive total for VOC emissions was 15.14 tons. The unit was below the 38.6 tons limitation of the permit and in compliance. 14. Monthly Recordkeeping – The permittee shall maintain appropriate records to document compliance with the VOC emission limits of Specific Condition No. 13. The records shall include, but are not limited to, the following: Facility Name, Facility Number (1030518), Emission Unit Numbers (001, 002, 005), Month, Year; For each emission unit (001, 002, 005); The total quantity of bread produced (in tons) for the month; The calculated quantity of VOCs emitted (in pounds or tons) for the month as follows; VOC Emissions Equation VOCs emitted = Tons of bread produced x VOC Emission Factor* *VOC Emission Factor = 4 pounds of VOCs / ton of baked bread The sum of VOCs emitted (in tons) for the most recent consecutive 12-month period. [Rule 62-4.070(3), F.A.C.] Permitting Note: The VOC emission factor was determined based upon use of the equation below (ref: EPA document number 453/R-02-017, Alternative Control Technology Document for Bakery Oven Emissions, 12/92) and the worst case parameters supplied by the applicant in the revised permit application dated 4/23/2007. VOC Emission Factor = 0.95Yi + 0.195ti – 0.51S – 0.86ts + 1.90 Where: VOC E.F. = pounds VOC per ton of baked bread Yi = initial baker’s percent of yeast to the nearest tenth of a percent ti = total yeast action time in hours to the nearest tenth of an hour S = final (spike) baker’s percent of yeast to the nearest tenth of a percent ts = spiking time in hours to the nearest tenth of an hour Comments: The monthly records for the ovens are maintained by Mr. Leibensperger as required in this permit condition. He monitors and keeps record through the production of the daily bread batches. There are tons of bread produced in vats and go through the conveyor lines into the ovens , flash frozen and packaged for shipment. The information is transferred to the spread sheet and reviewed by consultant Marvin Scott to maintain accuracy (See Record copies) |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: : there have been no changes to the facility emission units. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The facility recycles cardboard and waste dough goes to animal farm. |
| Closing Conference: I informed Mr. Lenisperger, that the facility appears to be in compliance at this time. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: September 27, 2011 |
| ACCESS? | ( | ARMS? | ( |

Lantmannen Unibake USA, Inc.  EuroBake

1927 4th Avenue South, St. Petersburg

Project Id:	75838	Permit No: 1030518-006-AF	Arms Number: 0518 005

Inspector:	Shea Jackson	Inspection Date / Time: 9/13/2011  /

Source (EU):	Mecatherm B baking line and associated equipment.  Serial No. 500151.  bread production capacity of 2.2046 tons/hour and 19,312 tons/year. Total design heat input rate of 4.167 MMBtu/hours

Description:	[Looking at the front of the facility and to north as observation of the stacks for the Mecatherm B Baking line oven]

Lantmannen Unibake USA, Inc.  EuroBake

1927 4th Avenue South, St. Petersburg

Project Id:	75838	Permit No: 1030518-006-AF	Arms Number: 0518 005

Inspector:	Shea Jackson	Inspection Date / Time: 9/13/2011  / _______

Source (EU):	Mecatherm B baking line and associated equipment.  Serial No. 500151.  bread production capacity of 2.2046 tons/hour and 19,312 tons/year. Total design heat input rate of 4.167 MMBtu/hours

Description:	[Looking inside building of the facility as observation of the stacks vented to roof for the Mecatherm B Baking line oven]