| 1030518 84786 |  |
| --- | --- |
| FACILITY: Lantmannen Unibake USA, Inc. | PERMIT ID: 2852 |
| Lantmannen Unibake | DISTRICT: Southwest |
| ADDRESS: 1927 4th Avenue South | CONTACT PHONE: |
| St. Petersburg, FL | 727-823-1113 |
| ARMS NO: 1030518 001 | PERMIT NO: | Expiration Date: 1/28/2018 Renewal Date: 11/29/2017 |
|  | 1030518-007-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Baking Line #1 (Mecatherm Line) a continuous non-stop baking line. Bread production of 1.1023 tons/hour and 9,656 tons/year. Heat input-1.270 MMBtu/hour. VOCs generated from fermentation. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | July 30, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: yes |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: yes I met with Adrian Cimpean to review records and tour the facility. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: David Leibensperger? |  | Yes |  | No |
|  | Comments: Mr. Leibensperger had retired 2 weeks prior to the inspection; I informed Mr. Cimpean they need to send documentation informing the FDEP and AQ Division of the change. Received notification letter 8/2/13 The Responsible Official/Authorized Representative’s e-mail is: david.leibensperger@lantmannen.com |
| 4. | Is the facility contact still: David Leibensperger? |  | Yes |  | No |
|  | Comments: Mr. Leibensperger had retired 2 weeks prior to the inspection. Mr. Adrian Cimpean, is the QA manager, who will replace. Mr. Leibensperger. The facility contact’s e-mail is: adrian.cimpean@lantmannen.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | General Conditions [62-4.160, F.A.C.] 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any, and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: The facility has not reported any non compliance issues to this date. 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Mr. Leibensperger had kept the permit in his office. Mr. Adrian Cimpean is his replacement. He did not know of its location, because of Mr. Leibensperger’s sudden departure. I sent an email attachment of the permit, until he could locate their copy. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: there are no pollution control devices for the oven emissions units of this facility, and no circumvention evident. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: The facility does not use any organic solvents. The VOC’s are emitted from the bread ding the baking process. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- 0; Wind direction – south easterly Upwind odor level detected-none detected off property 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. Comments: This facility does not typically have operations, which generate unconfined emissions outside of the building. There was a remodel of the front of the building; most of construction activity was inside building. A check later with the Asbestos section verified they had notified and taken proper steps for construction activities. There is no unconfined particulate matter activities associated with the roads; the landscaping is still in place. There is use of hoods inside for the collection of emissions from the ovens. inside the building from the ovens. There is no abrasive blasting performed at this bread making facility. (2). In addition to the standard products, the facility also bakes seeded breads and breads containing cheese ingredients. During the baking of these products, the potential for visible emissions from oven vents (exceeding the facility wide opacity limit of less than 20 %) exists. To reduce visible emissions below the facility wide opacity limit, the facility may utilize exit blowers that will add sufficient volumes of air to the oven vents. The use of baking pans with special surface coatings (parchment paper, silicone coated) may also allow the production of these special products with acceptable visible emissions. Comments: Prior to entering the building while off property, observation of facility roof and oven stacks. There were some stream and heat waves, there was no opacities or have visible emissions observations Permit Administrative Requirements 7. Annual Operating Report - On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year _2012___ was submitted on __ 3/12/13__. 8. Objectionable Odor - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere that by itself or in combination with other odors is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200, Definitions-(Objectionable Odors), F.A.C.; Pinellas County Code Subsection 58-178] Comments: There were no objectionable odors detected during observations and tours of the facility around the outside of inside of the buildings. 10. Operation Permit Renewal Application - A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCAQD (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 1/28/18. An application is required to be submitted no later than 11/29/17. It is not applicable at this time to submit application. This section of the permit addresses the following emissions units (EUs). Performance Restrictions A.2. VOC Emissions Standard – VOC emissions from emission units 001, 002, and 005 shall not exceed the following limit: E.U. ID No. Annual VOC Emissions (Any consecutive 12-month period) 001 19.3 tons [Rule 62-210.200 (Definition of Potential to Emit), F.A.C.; FESOP Permit No. 1030518-001-AF and Construction Permit No. 1030518-003-AC] Comments: The records reviewed from August 2012 through July 2013. The highest production month for EU 001 Mecatherm was August 2012 at 498.5 tons of bread baked with .997 tons VOC emission per that month. The 12 month consecutive total for VOC emissions was 11.84 tons. The unit was below the 19.3 tons limitation of the permit and in compliance. A.3. Monthly Log - The permittee shall maintain appropriate records to document compliance with the VOC emission limits of Specific Condition No. A.2. The records shall include, but are not limited to, the following: Facility Name, Facility Number (1030518), Emission Unit Numbers (001, 002, 005), Month, Year; For each emission unit (001, 002, 005); The total quantity of bread produced (in tons) for the month; The calculated quantity of VOCs emitted (in pounds or tons) for the month as follows; VOC Emissions Equation VOCs emitted = Tons of bread produced x VOC Emission Factor* *VOC Emission Factor = 4 pounds of VOCs / ton of baked bread The sum of VOCs emitted (in tons) for the most recent consecutive 12-month period. Permitting Note: The VOC emission factor was determined based upon use of the equation below (ref: EPA document number 453/R-02-017, Alternative Control Technology Document for Bakery Oven Emissions, 12/92) and the worst case parameters supplied by the applicant in the revised permit application dated 4/23/2007. VOC Emission Factor = 0.95Yi + 0.195ti – 0.51S – 0.86ts + 1.90 Where: VOC E.F. = pounds VOC per ton of baked bread Yi = initial baker’s percent of yeast to the nearest tenth of a percent ti = total yeast action time in hours to the nearest tenth of an hour S = final (spike) baker’s percent of yeast to the nearest tenth of a percent ts = spiking time in hours to the nearest tenth of an hour [Rule 62-4.070(3), F.A.C.; FESOP Permit No. 1030518-001-AF and Construction Permit No. 1030518-003-AC] Comments: The permit limitations calculated for the facility while operating at full capacity continuously 24/7 with all oven emissions units 001, 005 and 006. This means all ovens would have to be operating continuously to exceed permit limitations. Mr. Leibensperger had maintained the monthly records for the ovens in the facility computer. I informed Mr. Cimpean, that they keep record through the production of the daily bread batches. The flour is loaded into the storage silos, it dispenses into the building vats, where mixed batches and bread produced. The dough goes through the conveyor lines. The bread is formed, cut, allowed to rise, baked in the ovens, flash frozen and packaged for shipment. The employees collect the process information as they use flour to make bread batches. These measurements are transferred to the record spread sheets. Mr. Cimpean said he was aware of this and keeping records, but was not able to access the spreadsheet because he did not have password for Mr. Leibensperger’s personal computer. I told Mr. Cimpean he could contact his consultant Marvin Scott to assist them with the permit issues, and recordkeeping, as the facility records for the 2012 AOR had been completed by Southern Environmental Consulting. A.4. Records Retention – Monthly records shall be completed by the end of the following month. All records required by this permit shall be maintained at the facility for at least three years, unless otherwise noted, and be made available to the Department and/or PCAQD for inspection upon request. [Rule 62-4.160(14)(b), F.A.C.] Comments: The records reviewed for 2012 – 2013 were up to date, and recorded as required by permit conditions. The records were available on spread sheet back to 2009. (See spreadsheet Record copies) |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: there have been no changes to the facility emission units. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: The facility recycles cardboard and waste dough goes to animal farms. |
| Closing Conference: I informed Mr. Cimpean the facility compliance is pending review of records, and submittal of notification for change of authorized representative. 8/2/13 - Received notification letter and records spreadsheet. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: August 7, 2013 |
| ACCESS? | ( | ARMS? | ( |

Lantmannen Unibake USA, Inc.  Lantmannen Unibake

1927 4th Avenue South, St. Petersburg

Project Id:	84786	Permit No: 1030518-007-AO	Arms Number: 0518 001

Inspector:	Shea Jackson	Inspection Date / Time: 7/30/2013  / _______

Source (EU):	Baking Line #1 (Mecatherm Line) a continuous non-stop baking line. Bread production of 1.1023 tons/hour and 9,656 tons/year. Heat input-1.270 MMBtu/hour. VOCs generated from fermentation.

# Description:	[No visible emissions observed from the oven stacks during off property observations.]

# Description:	[Records reviewed for 2012 through July 2013]