| 1030528 84583 |  |
| --- | --- |
| FACILITY: Instrument Transformers, Inc. | PERMIT ID: 1005 |
|  | DISTRICT: Southwest |
| ADDRESS: 1907 Calumet Street | CONTACT PHONE: |
| Clearwater, FL | 727-298-2109 |
| ARMS NO: 1030528 001 | PERMIT NO: | Expiration Date: 4/21/2016 Renewal Date: 2/21/2016 |
|  | 1030528-002-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Five (5) varnish dip process areas and a Black W/R (Egyptian Coating) operation |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 24, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Phil Gonzalez? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: Philip.Gonzalez@ge.com |
| 4. | Is the facility contact still: Bruno Truconis? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | General Conditions [62-4.160, F.A.C.] 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: a. A description of and cause of noncompliance; and b. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: There were no periods of noncompliance reported during the compliance year. 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: There were no leaks observed in the Egyptian Coating operation or varnish dip process area. The Egyptian Coating operation and the varnish dip process recycles the spent material. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor level detected- None; Wind direction – E/5 mph Upwind odor level detected-None 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 4/21/16. An application is required to be submitted no later than 2/21/16. 9. Unconfined Particulate Emissions: a. No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. b. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. c. Reasonable precautions include the following: (1) Paving and maintenance of roads, parking areas and yards. (2) Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. (3) Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. (4) Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. (5) Landscaping or planting of vegetation. (6) Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. (7) Confining abrasive blasting where possible. (8) Enclosure or covering of conveyor systems. Comments: There are no unconfined particulate emissions associated with the solvent coating process. There are paved roads around the facility to decrease the presence of unconfined emissions. Permit Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 12’ was submitted on 3/21/13. 10. Volatile Organic Compound (VOC) and Total Hazardous Air Pollutants (THAP) Emission Limitations – VOC and THAP emissions shall not exceed the following: a. 22.2 tons of VOC per any consecutive 12-month period; b. 8.5 tons of THAP per any consecutive 12-month period. [Rule 62-210.200(PTE), F.A.C.; Construction Permit 1030528-001-AC] Comments: The review period 6/1/12 – 5/31/13 Total VOC emissions = 0.96680 tons/yr (95.6% under the limit) Total HAP emissions = 0.26 tons/yr (96.9% under the limit) 11. VOC and THAP Emission Recordkeeping Requirements - In order to document compliance with Specific Condition No. 4., the permittee shall maintain monthly records for all VOC and/or HAP containing materials, which shall contain at a minimum the following: a. Facility ID No. (1030528); b. date (month/year); c. the name/identification of each VOC and HAP containing material used; d. the VOC and/or HAP content in each material used; and e. the amount of each material used for the month. (Note - At the permittee's option the assumption may be made that material purchases equal material usage, provided no materials are used that are not purchased.) f. Calculate and record the monthly VOC emissions from each material (based on amount of material used and VOC content) along with the total emissions, in tons, from all the materials. g. Calculate and record the monthly THAP emissions from each material (based on the total emissions of each individual HAP from the amount of materials used) along with the total emissions, in tons, from all the materials. h. Calculate and record the most recent consecutive 12-month period total of VOC emissions, in tons. i. Calculate and record the most recent consecutive 12-month period total of THAP emissions, in tons. Supporting documentation (MSDS sheets, "As Supplied" sheets, purchase orders, purchase records, inventory records, production records, etc.), which includes sufficient information to determine emissions shall also be kept. The monthly records shall be completed by the 15th day of the following month. These records shall be recorded in a permanent form suitable for inspection by the Department and Pinellas County Air Quality Division upon request and shall be maintained at the facility for the most recent three (3) year period. [Rules 62-4.070(3) and 62-4.160, F.A.C.; Pinellas County Code, Section 58-90; Construction Permit 1030528-001-AC] Comments: The facility meets the recordkeeping provisions of the condition. A copy of the highest monthly emissions total is attached to the compliance file. 12. General Pollutant Emission Limiting Standards: Objectionable Odor Prohibited - The permittee shall not cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An "Objectionable Odor" is defined as any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178; Construction Permit 1030528-001-AC] Comments: There were no objectionable odors detected during the inspection. Additionally, there were no odor complaints filed against the company. 13. General Pollutant Emission Limiting Standards: Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions - The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds or organic solvents without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The permittee shall comply with the following: a. All equipment, pipes, hoses, lids, fittings, etc., shall be operated and maintained in such a manner as to minimize leaks, fugitive emission, and spills of paints and solvent materials that contain VOC's and/or OS's. b. All solvents from solvent washings that contain VOC's and/or OS's shall be directed into containers that prevent evaporation into the atmosphere. [Rule 62-296.320(1), F.A.C.; Construction Permit 1030528-001-AC] Comments: There were no leaks observed in the hoses or fittings associated with the Egyptian Coating operation and varnish dip process. All lacquer containers were closed and sealed. If there are spills of paint associated with each process, the facility disposes spent clean up rags in sealed cans. All washings of brushes and applicators used in the self contained dipping process are directed into sealed containers for recycling. The Control Power Transformers (CPT) varnish dip process is now performed in a small booth with a motorized robot. The robot arm picks up the transformer assembly and sprays varnish in a fine mist from its arm/aperture. This allows for an even coating on the assembly. There were no solvent odors detected with either process. A.1. VOC RACT (Reasonably Available Control Technology) Emission Limitations - No owner or operator of a coating line for miscellaneous metal parts and products shall cause, allow, or permit the discharge into the atmosphere of any volatile organic compounds (VOCs) in excess of: a. 4.3 pounds per gallon of coating, excluding water delivered to a coating applicator that applies clear coatings; b. 3.5 pounds per gallon of coating, excluding water, delivered to a coating application system that is air dried or forced warm air dried at temperatures up to 194 degrees Fahrenheit; c. 3.5 pounds per gallon of coating, excluding water, delivered to a coating applicator that applies extreme performance coatings; or, d. 3.0 pounds per gallon of coating, excluding water, delivered to a coating applicator for all other coating application systems. e. If more than one emission limitation in a., b., c., or d., above applies to a specific coating, then the least stringent emission limitation shall be applied. f. All volatile organic compound emissions from solvent washings shall be considered in the emission limitations in a., b., c., and d. above, unless the solvent is directed into containers that prevent evaporation into the atmosphere. [Rule 62-296.513(2) (Surface Coating of Miscellaneous Metal Parts and Products), F.A.C.; Construction Permit 1030528-001-AC] Comments: The facility only uses clear coating and the limit is 4.3 lbs/gal. At no time during the compliance year was the limit exceeded. A.2. VOC RACT Recordkeeping Requirements - In order to demonstrate compliance with Specific Condition No. A.1., the permittee shall comply with the daily recordkeeping requirements of Rule 62-296.500(2)(b), F.A.C. The records shall be maintained on file at the facility and include at least the following: a. facility name, facility ID, and emission unit number (i.e., 1030528, EU 001 - Varnish Dip Process Areas and a Black W/R (Egyptian Coating) Operation); b. the date for each application of adhesive, coating, and/or solvent: c. the rule number applicable to the operation for which the records are being maintained (i.e., Rule 62-296.513, F.A.C.); d. the application method (e.g., Dip Coating, Egyptian Coating, etc.) and substrate type (e.g., metal); e. the amount and type of adhesive, coatings (including catalyst and reducer for multi-component coatings), solvent, solvent used at each point of application, including exempt compounds; f. the VOC content (pounds per gallon excluding water) as applied in each adhesive coating, and solvent; g. the amount of surface preparation, cleanup, wash-up of solvent (including exempt compounds) used and the VOC content of each; and h. oven temperature (where applicable). The daily logs shall be completed within three (3) business days. The facility shall also maintain documentation, such as all MSD sheets, purchase orders, etc., for all solvents used, which includes sufficient information to determine VOC emissions. All of the above records shall be kept at the facility for the most recent two-year period and made available to the Department and the Pinellas County Air Quality Division upon request. [Rule 62-296.500(2)(b), F.A.C.; Construction Permit 1030528-001-AC] Comments: Air Quality reviewed the daily records, MSD sheets and purchase orders. The daily logs are completed with three business days. The daily records meet the provisions of this condition. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance year. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |