| 1030528 84584 |  |
| --- | --- |
| FACILITY: Instrument Transformers, Inc. | PERMIT ID: 2868 |
|  | DISTRICT: Southwest |
| ADDRESS: 1907 Calumet Street | CONTACT PHONE: |
| Clearwater, FL | 727-298-2109 |
| ARMS NO: 1030528 002 | PERMIT NO: | Expiration Date: 4/21/2016 Renewal Date: 2/21/2016 |
|  | 1030528-002-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : VOC/HAP materials used in assembly; Safety-Kleen, Model 30, parts washer (or equivalent) using Safety-Kleen 105 (or equivalent) non-halogenated solvent of 40CFR63-Subpart T, Halogenated Solvent Cleaning or Rule 62-296.511, F.A.C.- Solvent Metal Cleaning |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 24, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Phil Gonzalez? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: Philip.Gonzalez@ge.com |
| 4. | Is the facility contact still: Bruno Truconis? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( |  |  | B.1. Parts Washer Limitations - The parts washer shall be limited as follows: a. In order to avoid the requirements of 40 CFR 63, Subpart T, Halogenated Solvent Cleaning, the parts washer shall not use*: 1. Methylene Chloride 2, 1,1,1 – Trichloroethane 3. Chloroform 4. Tetrachloroethylene 5. Trichloroethylene 6. Carbon Tetrachloride * Blended cleaning solvents must contain a total regulated solvent content below 5% by weight to be exempt from the regulation. b. In order to avoid the VOC RACT requirements of Rule 62-296.511, F.A.C. – Solvent Metal Cleaning, the parts washer is limited to a maximum VOC emission rate of 200 pounds per any consecutive 12-month period. [Rules 62-4.070(3) and 62-296.500(3)(a), F.A.C.; Construction Permit 1030528-001-AC] Comments: The facility only uses Safety Kleen Solvent 150. The highest total used was Mar, 13’ = 1 gal. Less than 6.7 lbs of material. (6.672 lbs/gal x 1 gallons). At no time during the compliance year did the facility exceed the maximum VOC emission rate. Additionally, the facility never used any of the above referenced solvents in the parts washer. B.2. Parts Washer Recordkeeping Requirements - In order to demonstrate compliance with Specific Condition No. B.1., the permittee shall keep the following records for the parts washer: a. The name of each solvent used. b. The VOC content of each solvent used, by weight (lbs./gal.). c. The amount of each solvent used*, in gallons. d. The amount of VOC emissions*, in pounds. (* Permitting Note - If during a month no solvent has been added to the parts washer, then record for that month zero pounds used and emitted.) e. The most recent consecutive 12-month period total amount of VOC emissions, in pounds. The monthly logs shall be completed by the 15th day following each calendar quarter. Supporting documentation (MSDS sheets, purchase order, etc.) shall be kept for each material which includes sufficient information to determine VOC emissions. These records shall be recorded in a permanent form suitable for inspection by the Department and Pinellas County Air Quality Division upon request and maintained at the facility for the most recent three (3) year period. [Rules 62-4.070(3) and 62-4.160, F.A.C.; Pinellas County Code, Section 58-90; Construction Permit 1030528-001-AC] Comments: A copy of the February 12’ record is attached. The facility meets the provisions of this condition. Additionally, the monthly logs are completed by the 10th day of each month. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance year. |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |