| 1030536 75770 |  |
| --- | --- |
| FACILITY: Modern Silicone Technologies, Inc. | PERMIT ID: 2851 |
|  | DISTRICT: Southwest |
| ADDRESS: 5777 Myer Lake Circle | CONTACT PHONE: |
| Clearwater, FL | 727-507-9800 |
| ARMS NO: 1030536 001 | PERMIT NO: | Expiration Date: 10/21/2014 Renewal Date: 8/22/2014 |
|  | 1030536-002-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Plastic Injection Molding Operation (Priming Process and Mold Cleaning). The facility produces a variety of custom-design gaskets. The facility utilizes silicone, polypropylene and nylon based resins in the molding process. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | April 11, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Matthew Algate? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Matthew Algate? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. - General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. Comments: A copy of the permit was reviewed by AQD 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An "objectionable odor" means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C. .; Pinellas County Code, Section 58-1781 Comments: No objectionable odors detected during the inspection. The molding machines are self contained 8. Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: received on 3/1/11 and reviewed on4/12/11 9. Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to local program name no later than 60 days prior to the expiration date of the operation permit…. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: Expiration Date: 10/21/2014 Renewal Date: 8/22/2014 A.2. VOC Emissions Limitations: VOC emissions from this emissions unit shall not exceed 44.3 tons per any consecutive 12-month period. [Permit Application dated 4/27/2009; Rules 62-4.070(3) and 62-210.200(PTE), F.A.C.] Comments: Highest VOC total = 2 tons/yr (Dec, 10’) A.3. Total HAP Emissions Limitations: Total HAP emissions from this emissions unit shall not exceed 3.0 tons per any consecutive 12-month period. [Permit Application dated 4/27/2009; Rules 62-4.070(3) and 62-210.200(PTE), F.A.C.]] Comments: Highest HAP total = 0.5 tons/yr (Dec, 10’) A.4. VOC and HAP Monthly Log: The permittee shall maintain appropriate records to document compliance with the VOC and HAP emission limits of Specific Condition Nos. A.2 and A.3. The records shall include, but are not limited to, the following: Facility Name, Facility Number (1030536), Emission Unit No. (EU-001), Month, Year. For each raw material (priming solution, cleaning solvent , etc.) used that contains a VOC and/or HAP, record the following: raw material identification/description; raw material density; total quantity of each raw material used for month (in gallons or pounds); concentration (e.g., percent) of VOC and HAP components in each raw material; calculate the VOC and total HAP emissions for the month (in tons) for each raw material; Calculate the VOC and total HAP emissions for the most recent month (in tons). Calculate the VOC and total HAP emissions for the most recent consecutive 12-month period (in tons). All monthly records shall be completed by the end of following month. [Rule 62-4.070(3), F.A.C Comments: Facility name upper left corner, facility ID and EU in upper right corner Raw material ID description; product name eg naphtha, primer,T-123 Raw material density; recorded in lbs/gal Total quantity annual usage in gallons and pounds Concentration in % VOC and HAP emissions calculated and presented in lower right corner of the spreadsheet. Most recent monthly VOC and HAP emissions located in right corner of spreadsheet Most recent 12-mo period VOC and HAP emissions located in right corner of spreadsheet All monthly records are completed by the end of the following month |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: no pollution activities performed during the compliance year |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |