| 1030536 84587 |  |
| --- | --- |
| FACILITY: Modern Silicone Technologies, Inc. | PERMIT ID: 2851 |
|  | DISTRICT: Southwest |
| ADDRESS: 5777 Myer Lake Circle | CONTACT PHONE: |
| Clearwater, FL | 727-507-9800 |
| ARMS NO: 1030536 001 | PERMIT NO: | Expiration Date: 10/21/2014 Renewal Date: 8/22/2014 |
|  | 1030536-002-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Plastic Injection Molding Operation (Priming Process and Mold Cleaning). The facility produces a variety of custom-design gaskets. The facility utilizes silicone, polypropylene and nylon based resins in the molding process. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | June 19, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Matthew Algate? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: malgate@modernsilicone.com |
| 4. | Is the facility contact still: Matthew Algate? |  | Yes |  | No |
|  | Comments: Dave Singer assisted the inspector during this inspection The facility contact’s e-mail is: dsinger@modernsilicone.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [62-4.160 F.A.C. - General Condition 12.] Comments: The facility did did not have a copy of the permit on-site. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An "objectionable odor" means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C. .; Pinellas County Code, Section 58-1781 Comments: There were no objectionable odors detected during the inspection and no complaints filed to Air Quality during the compliance year. 8. Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: received by Air Quality on 3/20/13 and reviewed on 5/16/13 9. Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to local program name no later than 60 days prior to the expiration date of the operation permit…. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: Renewal Date: 8/22/2014 Expiration Date: 10/21/2014 The facility is planning to encompass two existing operations from Virginia and Chicago in two separate buildings near the existing main plant. The Chicago, IL operation performs tooling while the Virginia operation performs molding. Both existing operations will be moving Oct, 12’ – Jan, 13’ and it will be under the company name. Modern Silicone Technologies will need to apply for an Air Construction permit. During a later time, the main operation will move into the buildings that will occupy the VA and Chicago operations. In the meantime, Modern Silicone Technologies will notify FDEP and Air Quality 60 days before the planned move of the operations. Additionally, Modern Silicone Technologies has performed an asbestos survey in the new buildings A.2. VOC Emissions Limitations: VOC emissions from this emissions unit shall not exceed 44.3 tons per any consecutive 12-month period. [Permit Application dated 4/27/2009; Rules 62-4.070(3) and 62-210.200(PTE), F.A.C.] Comments: The highest VOC emissions = 4.9 tons/yr (July, 12’) A.3. Total HAP Emissions Limitations: Total HAP emissions from this emissions unit shall not exceed 3.0 tons per any consecutive 12-month period. [Permit Application dated 4/27/2009; Rules 62-4.070(3) and 62-210.200(PTE), F.A.C.]] Comments: The highest HAP emissions = 0.15 tons/yr (Aug, 12’) A.4. VOC and HAP Monthly Log: The permittee shall maintain appropriate records to document compliance with the VOC and HAP emission limits of Specific Condition Nos. A.2 and A.3. The records shall include, but are not limited to, the following: Facility Name, Facility Number (1030536), Emission Unit No. (EU-001), Month, Year. For each raw material (priming solution, cleaning solvent , etc.) used that contains a VOC and/or HAP, record the following: raw material identification/description; raw material density; total quantity of each raw material used for month (in gallons or pounds); concentration (e.g., percent) of VOC and HAP components in each raw material; calculate the VOC and total HAP emissions for the month (in tons) for each raw material; Calculate the VOC and total HAP emissions for the most recent month (in tons). Calculate the VOC and total HAP emissions for the most recent consecutive 12-month period (in tons). All monthly records shall be completed by the end of following month. [Rule 62-4.070(3), F.A.C Comments: Modern Silicone Technologies meets the provision of this condition. A copy of the monthly log is attached to the compliance file |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: There were no pollution prevention activities during the compliance year |
| Closing Conference: |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |