| 1030543 77979 |  |
| --- | --- |
| FACILITY: Melitta USA, Inc. | PERMIT ID: 3550 |
|  | DISTRICT: Southwest |
| ADDRESS: 3925 58th Street North | CONTACT PHONE: |
| Clearwater, FL | 727-524-4851 |
| ARMS NO: 1030543 002 | PERMIT NO: | Expiration Date: 1/15/2012 Renewal Date: 10/17/2011 |
|  | 1030543-001-AC |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : One Kabey-synchro flexographic printing machine is used to print the company name on the filter paper before it enters the coffee filter machines to be cut and crimped. VOC emissions are emitted to the atmosphere |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | September 7, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
|  | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: this unit was to be installed under this permit. |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I reviewed the records and toured the facility with Mr. Bloedorn |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Matthias Bloedorn? |  | Yes |  | No |
|  | Comments: I met with Mr. Bloedorn The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Matthias Bloedorn? |  | Yes |  | No |
|  | Comments: yes The facility contact’s e-mail is: MBloedorn@melitta.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( |  |  | Inspection note: This initial construction permit became effective on 3/22/11 B.1. VOC/HAP Emission Limitations – a. Emissions of volatile organic compounds (VOCs), as defined in Rule 62-210.200, F.A.C., shall not exceed the following: Pollutant Emission Limits (tons/consecutive 12 month period) Volatile Organic Compounds 2.4 b. The printing operation shall not use any ink that contains any hazardous air pollutant (HAP). Permitting Note: This emission limit is based on an annual usage of 750 gallons of CSL39513 Brown Ink R with a VOC content of 77.0%. The ink contains no HAPS. [Rule 62-210.200, F.A.C. (“Potential to Emit”); as requested in Construction Permit application received 11/08/2010] Comments: The facility had delays for the installation of the filter printer. They were still working on the design for the impressions for the filter. There are no records for emissions for this unit as it has not be installed and put into operation. Mr. Bloedorn stated they had used some about one quart of inks in the lab to test and make samples. B.2. Notification of Operation Commencement - The permittee shall notify the Compliance Authority in writing of the date of commencing operation of EU No. 002, no later than fifteen (15) days after that date. Commencing operation means setting into operation of any emissions unit for any purpose. [Rule 62-4.070, F.A.C., and Rule 62-210.200, F.A.C., (“Commence Operation”)] Comments: I informed Mr. Bloedorn of the notification of operation commencement condition of his permit. He was aware he had to contact us within 15 days of operations. Mr. Bloedorn showed me the location where the printer will be installed on the filter press equipment line #57. The construction permit renewal date is 10/17/2011. Mr. Bloedorn stated they would not be putting this in until November. I informed him the permit expires 1/15/2011 and it appears he would need to get an extension of permit. I told him I would check at PCAQ and determine what action is needed to prevent violation of permit. Mr. Bloedorn stated the equipment should go in November and start operations in December 2011. B.3. VOC Recordkeeping - In order to document compliance with the VOC emission limits in Specific Condition No. B.1., the permittee shall maintain monthly records. The records shall contain, at a minimum, the following: a. facility name, facility ID No., emission unit ID No., and description (i.e., Melitta USA, Inc., 1030543, EU 002, Flexographic Printing); b. total quantity (gallons) and VOC content (lbs/gallon) of all VOC containing materials used during the month; c. calculated monthly total VOC emissions, in pounds or tons per month (based on b. above); and d. cumulative total of all VOC emissions for the most recent consecutive 12 month period (tons per consecutive 12 month period). [Rule 62-4.070(3), F.A.C.] Comments: the facility records are up to date, and meet the specifications a – d for emission unit 001. There are no records for emission unit 002. The records observed are for the Melitta KD blend for use of ethanol/methanol. The monthly usage is typically 880 gallons. There was one month June, where no KD blends was received due to slowing of business. This is the only chemical currently in use which is monitored for pollutants. Mr. Bloedorn stated they are looking to eliminate the usage of methanol. 8 Application for Non-Title V Air Operation Permit - This permit authorizes construction or modification of the permitted emissions units and initial operation to determine compliance with Department rules. A Non-Title V air operation permit is required for continued operation of the permitted emissions units. The permittee shall apply for a Non-Title V air operation permit at least 90 days prior to expiration of this permit, but no later than 180 days after commencing operation of the flexographic printer. Commencing operation means setting into operation of any emissions unit for any purpose... [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit renewal date is 10/17/2011. I advised Mr. Bloedorn, he may need to request extension or go ahead and renew for operational even though they have not started the operation of the flexi printer. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: This is not applicable at this time, as the facility had not installed the printer. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: I gave Mr. Bloedorn the P2 pamphlets and advised him of the program and looking to reduce or eliminate pollutants. He stated they are reviewing the use of methanol and hope to discontinue use. The facility reuses the filter paper back into their filter manufacturing. They also recycle office bulbs, glass, aluminum, and plastic wrap. |
| Closing Conference: I informed him the facility appears to be in compliance. I would check into the permit expiration and renewal of the construction permit in regards to the flexographic printer. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: September 12, 2011 |
| ACCESS? | ( | ARMS? | ( |

Melitta USA, Inc.

13925 58th Street North, Clearwater

Project Id:	77978	Permit No: 1030543-001-AC	Arms Number: 0543 001

Inspector:	Shea Jackson	Inspection Date / Time: 9/7/2011  / _______

Source (EU):	Coffee Filter manufacturer using ethyl alcohol and methanol solvents

# Description:	[This is the line up of the filter presses where are cut and packaged.  The number 57 unit is where they plan to install printer to start testing marketability. ]

Melitta USA, Inc.

13925 58th Street North, Clearwater

Project Id:	77978	Permit No: 1030543-001-AC	Arms Number: 0543 001

Inspector:	Shea Jackson	Inspection Date / Time: 9/7/2011  / _______

Source (EU):	Coffee Filter manufacturer using ethyl alcohol and methanol solvents

# Description:	[The filters will have an ink impression placed on the inside of filter once they install equipment ]

Melitta USA, Inc.

Project Id:	77978	Permit No: 1030543-001-AC	Arms Number: 0543 001

Inspector:	Shea Jackson	Inspection Date / Time: 9/7/2011  / _______

Source (EU):	Coffee Filter manufacturer using ethyl alcohol and methanol solvents

# Description:	[This is one of the filter press machines and the nozzles where the KD Blend is sprayed into the equipment.]