IC INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY High Performance Systems, Inc. TITLE V FACILITY | DISTRICT Southwest | COUNTY Polk |
| --- | --- | --- |
| ADDRESS 1201 American Superior Blvd. Winter Haven, FL 33884 | CONTACT(S) John Taylor, Vice President, (863) 294-5566 |
| AIRS ID# 1050158 | PERMIT # 1050158-002-AV | EXPIRATION DATE 07/18/2002 | ARMS ENTRY DATE June 13, 2002 |
| SOURCE DESCRIPTION Extruded aluminum metal finishing plant. |
| INSPECTION DATE June 12, 2002 | AUDIT TYPE II-CDS | COMPLIANCE STATUS In compliance |
| INSPECTION FINDINGS |
| PARAMETER | ALLOWED VALUE | OBSERVATION |
| 1. Hours of operation Section III, Condition 1 (III-1) | Each emission unit is allowed to operate 8,760 hours per year. | In compliance |
| 2. Fuels & heat rates (III-2) | a. The batch bake-off incinerator, paint bake oven, paint bake oven afterburner, dry-off oven, and Tank 3 heater shall burn natural gas. Propane may be used during gas curtailment. b. Maximum heat input rate is 10.351 MMBtu/hr. | a. In compliance b. 6.21 MMBtu/hr in CY01 (from 2001 AOR) |
| 3. VOC emissions (III-3) | Facility total 193.4 lb/hr (monthly average basis) and 240 tons per consecutive 12-month period, substantiated by record-keeping. | 01 AOR shows 64.88 tons and 62.4 lb/hr annual average. Checked facility records and found operations to be within permit limits. |
| 4. Visible emissions (III-4, 5) | a. Batch bake-off incinerator (stack 9) and Tank 3/ paint bake oven/afterburner (stack 8): 5%, except 20% for 3 minutes per hour. Test annually. b. Paint spray booths: 20%; however, to provide reasonable assurance that filters are working, VE shall not exceed 5%. If >5%, not a violation, but an indicator that stack testing or additional controls may be required. Test 180 days prior to permit expiration. | a. In compliance b. In compliance |
| 5. Afterburner operation (III-6) | Whenever possible, operated whenever bake oven is in operation. Temperature 1340ºF (1050ºF indicated) | In compliance |
| 6. Bake oven operation (III-7) | At minimum temperature specified by manufacturer of paint in use, but not >525ºF | In compliance. |
| 7. Temperature controls (III-8) | a. Afterburner shall have a circular chart recorder to continuously monitor and record temperature. b. Batch bake-off incinerator will have a temp controller to maintain primary chamber at approx. 800ºF and secondary chamber at approx. 1600ºF, with a minimum of 1400ºF. c. Paint bake oven shall have a controller, be visually monitored, and manually adjusted. d. Dry-off oven is temperature-controlled at approximately 250ºF. | a. In compliance b. In compliance. c. In compliance d. In compliance |
| COMMENTS Emission units: 001: Conveyor paint line (booths 1-4) Touch-up spray booth (booth 5) Paint mix room 002: Paint bake oven/afterburner Tank #3 heater Dry-off oven 003: Batch bake-off incinerator Exempt emission units and/or activities: Miscellaneous maintenance painting activities. |
| INSPECTOR(S) NAME(S) J. Cox |
| SIGNATURE(S) | DATE June 13, 2002 |