| AIR POLLUTION SOURCE INSPECTION REPORT FORM DEPARTMENT OF ENVIRONMENTAL PROTECTION |
| --- |
| FACILITY: American Environmental Container Corp | PAGE: 1 OF 1 |
| FACILITY ADDRESS: 2302 Lasso Lane | CITY: Lakeland, FL 33801 | COUNTY: Polk |
| MAILING ADDRESS: 2302 Lasso Lane | CITY: Lakeland | STATE: FL | ZIP: 33801 |
| INSP. DATE: 9/18/2009 | TIME IN: n/a | TIME OUT: n/a | INSP TYPE: INS2 | STATUS: IN |
| IDENTIFICATION NO: 1050250 | EU ID # Facility Wide |
| SOURCE/FACILITY DESCRIPTION: Fiberglass Product Manufacturer |
| CONTACT(S): Mr. Kirk Sullivan, President; Mr. Ken Butler, facility manager |
| I, James Burkholder (JB), went to American Environmental Container Corporation d/b/a San Juan Pools on September 18, 2009 for an on-site inspection as part of a full compliance evaluation for the Title V fiberglass pool manufacturing facility. When I arrived on site I met with Mr. Kirk Sullivan and Mr. Ken Butler of American Environmental Container Corp. We went through the 2008 and 2009 VOC and HAP emission records first before the facility walk through. In June of 2008, the facility was manufacturing approximately 4 pools a day. At the time of my inspection in September of 2009, the facility was currently averaging 1 to 2 pools a day. The emissions records verified the stated facility production rates. This following emissions occurred at the facility: June 2008 August 2009 Permitted Limit HAPS 48.34 tons ~ 23 tons 180 tons VOCS 49.02 tons ~ 24 tons 180 tons The 2009 emissions reflect that production has decreased by about half of the 2008 production. The emissions have been steadily declining since 2006. In 2006 97.26 tons of HAPS were emitted and in 2007 68.72 tons were emitted. The VOC and HAP emissions are well under the 180 ton limit. The building is ventilated by exhausting the indoor HAP or VOC laden air through six (6) exhaust stacks with 35,000 acfm fans. The facility showed good housekeeping practices inside the building and no objectionable odor was detected. Resin or Gelcoat applications were not in process at the time of inspection. The only project currently in process on the date of the inspection was a custom built pool that was going to be installed on the roof of a hotel in Toronto, Canada. The pool was outside of the building getting the finishing touches. The solvents, resins, and gelcoats were all kept sealed in containers and all records were produced upon demand. At the time of inspection, the facility appeared to be in compliance. |
| INSPECTOR(S): James Burkholder (JB) | TIME EXPENDED: JB – 240 mins | REPORT DATE: 10/8/2009 |