| AIR POLLUTION SOURCE INSPECTION REPORT FORM DEPARTMENT OF ENVIRONMENTAL PROTECTION |
| --- |
| FACILITY: Amerimix Industries, Inc. | PAGE: 1 OF 1 |
| FACILITY ADDRESS: Alabama Lane & 1st Street West | CITY: Auburndale, FL 33823 | COUNTY: Polk |
| MAILING ADDRESS: 2941 5th Avenue North | CITY: St. Petersburg | STATE: FL | ZIP: 33713 |
| INSP. DATE: 9/30/2009 | TIME IN: 1:15 pm | TIME OUT: 2:15 pm | INSP TYPE: INS2 | STATUS: IN |
| IDENTIFICATION NO: 1050377 | EU ID # Facility Wide |
| SOURCE/FACILITY DESCRIPTION: Mineral Processing Plant |
| CONTACT(S): George Chiappo, President; Arnie Cummings, Vice President |
| I, James Burkholder (JB), and Malik Pickering (MP) went to Amerimix Industries, Inc. Auburndale Plant on September 30, 2009 to perform an onsite compliance inspection as part of a full compliance evaluation and to discuss the most recent visible emissions testing. We arrived on site and met with Mr. Arnie Cummings who escorted us through the facility. The facility yard is unpaved, but was being watered down with a portable sprinkler in order to prevent fugitive particulate emissions. Wet sand is transported to the facility by dump truck and piled in the yard. A front end loader loads the rotary dryer, and the sand is heated up to evaporate out the moisture. It is cheaper to run the rotary dryer to dry wet sand than to truck dry sand in. There are eight (8) 120 ton silos that are used for storing materials used for the stucco and mortar mixtures. Emissions from the silos and bagging operations are controlled by a central dust collector and the rotary dryer emissions are controlled by a baghouse. MP and I (JB) inspected the baghouse, CDC, and all of the ductwork. A cement tanker was loading cement into one of the silos while the manual bagger was in operation. The central dust collector was properly operating and no visible emissions or leaks in the ducts were observed. The ductwork for the rotary dryer baghouse also appeared to be in great working condition. The facility keeps daily records that show the dryer run time, tons produced, tons per hour, and fuel usage. Daily baghouse and CDC pressure drops are recorded along with the tons of cement loaded into each silo and the amount of stucco produced on a daily basis as well. I informed Mr. Cummings that the most recent VE test on 8/21/2009 sets their limits for operating until the next VE is performed. On 8/21/2009 the following parameters were established: Permitted Limits Tested Capacity New Limited Capacity Sand Silos from Dryer 60 TPH 50 TPH 55 TPH Cement Truck Loading* 50 TPH 17.72 TPH** 19.49 TPH** Bagging Operations 110 TPH 30.17 TPH 33.2 TPH * Truck loading rate is for two trucks loading at a maximum combined rate of 50 tph. ** Visible Emissions testing conducted while only loading one truck at 17.72 tph. |
| INSPECTOR(S): James Burkholder (JB); Malik Pickering (MP) | TIME EXPENDED: JB – 180 mins MP – 120 mins | REPORT DATE: 10/9/2009 |

| DEPARTMENT OF ENVIRONMENTAL PROTECTION CONTINUATION PAGE 2 OF 2 |
| --- |
| FACILITY: Amerimix Industries, Inc. Auburndale | INSPECTION DATE: 9/30/2009 |
| I informed Mr. Cummings that 110% of the tested rates would be the new maximum capacity that the facility was allowed to operate. He stated that they were unaware of that requirement, but they tested at their average capacity. A detailed record check from 8/21/2009-9/29/2009 showed that the facility was operating daily at the same throughputs as the day of the visible emissions test. Since the facility only loaded one cement tanker during the test I recommended that only one tanker be loaded at a time. If the facility needs to unload two tankers they must stay under the 19.49 TPH combined, or the facility will be in violation. I explained that Amerimix cannot exceed these rates in the future or they will be in violation of their permit, but they may retest at a higher rate given the proper notification to the Department. A spot check of records dating back to July of 2008 was performed and the facility appeared to be in compliance with their previous operating rates. At the time of the inspection, the facility appeared to be in compliance with all of their permit conditions. |
| INSPECTOR: James Burkholder (JB) and Malik Pickering (MP) | REPORT DATE: 10/9/2009 | FACILITY ID NUMBER: 1050377 |