September 9, 2005

Mr. Gene Strickland

Anderson Columbia

2316 Highway 71

Marianna, Florida 32448

Dear Mr. Strickland:

Enclosed is a copy of the report completed by Mr. Richard S. Brookins Jr. describing his inspection of your facility on Thursday, September 8, 2005.  The cooperation and assistance of Mr. John Weigel during the inspection is greatly appreciated.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates a state of compliance with permit conditions at the time of inspection for those sources specifically listed on the inspection report.  However, please note the Recommendation section of this report.

If you have any questions, please contact Mr. Richard S. Brookins Jr. at (850) 872-4375 x108 or e-mail at Richard.Brookins@dep.state.fl.us.

Sincerely,

Josie Penton

Environmental Manager

INSPECTION REPORT

AIR POLLUTANT EMISSION SOURCES

| FACILITY: | Anderson Columbia #3 | DISTRICT: 10 | COUNTY: 32 |
| --- | --- | --- | --- |
|  | 2316 Hwy. 71 | CONTACT: Mike Miller |
|  | Marianna, FL 32405 | TELEPHONE: (850) 526-4440 |
| Email Address: |

| AIRS ID#: 7775064 | PERMIT#: 7775064-003-AO | EXPIRATION DATE: 08/28/2008 |
| --- | --- | --- |
| Permit Renewal Application/Notification Due Date: 06/29/2008 |

| INSPECTION DATE | AUDIT TYPE | COMPLIANCE STATUS |
| --- | --- | --- |
| 9/08/2005 | II | In Compliance |
| SKY | WIND | TEMPERATURE |
| Clear | 3-5 mph | Low 90’s |

SOURCE DESCRIPTION: This facility is an Asphalt Concrete Drum Plant.  Particulate emissions are controlled by a baghouse.

INSPECTION COMMENTS:

I arrived at the facility and was greeted by Mr. John Weigel.  Mr. Weigel showed me the operations logbook which contains all permits for the facility, along with the information required under the permit conditions.  Mr. Weigel provided copies of requested records.  I was allowed unescorted access to the facility.  The facility was not actively producing asphalt at the time of inspection.

According to the information provided, the facility has produced 97,425.36 tons of asphalt cement in the 12-month period ending August 31, 2005.  This is within the permit limit of 500,000 tons in any consecutive 12-month period.  [Specific Condition A.2]

According to the information provided, the facility has operated for a total of 617.75 hours during the 12-month period ending August 31, 2005.  The facility is allowed unlimited hours of operation.  [Specific Condition A.3]

Since the facility was not operating at the time of inspection there were no visible emissions.  This is within the facility’s limit of 20% opacity.  [Specific Condition A.5]

Information in the operations logbook includes tons of asphalt produced, hours of operation, baghouse differential pressures, and fuel oil used in both the burner and asphalt heater.  [Specific Condition A.10]

There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

There were minor fugitive emissions greater than 20% opacity noticed during the inspection.  These emissions were confined within the facility’s boundary.  [Facility-wide Condition 3]

VOC control appeared adequate at the facility at the time of inspection.  [Facility-wide Condition 4]

Reasonable precautions continue to be difficult at this facility.  Even though the facility has a water truck, excessive amounts of fugitive dust was noticed coming from the “off road” areas as the mobile equipment operated in their normal manner.  [Facility-wide Condition 6]

As mentioned above, the operations logbook also contains information regarding the fuel oil used each day in both the burner and asphalt heater.  According to records provided the facility has used 25,146 gallons of fuel oil for the heater and 184240 gallons of fuel oil for the burner during the 12-month period ending August 31, 2005.  Records of fuel oil deliveries including percent sulfur content are maintained as required.  [Facility-wide Condition 9]

RECOMMENDATIONS:

Utilize the water truck as needed to maintain fugitive emissions below permitted limits during the dry months of the year.  Consider utilizing either a street cleaning service or other means to help maintain facility roadways clear of dirt and other material tracked from the unpaved areas of the facility.  Continue to investigate the use of organic dust suppressants.

| INSPECTOR’S NAME | SIGNATURE | DATE |
| --- | --- | --- |
| Richard S. Brookins Jr. |  |  |
| Environmental Specialist |  | September 9, 2005 |