February 2, 2006

Mr. Brian Schreiber

Secretary

Anderson Columbia Company, Inc.

Post Office Box 1829

Lake City, Florida 32056

Dear Mr. Schreiber:

A Department representative recently inspected your facility.  A copy of the inspection report is enclosed.  Please note the permit expiration date and renewal application due date shown on the report.

This letter applies only to activities covered by the Air Resources Management Program.  It indicates compliance at the time of inspection for those sources specifically listed on the inspection report.

If you have any questions, please contact Richard Brookins at 850/872-4375, extension 108 or Richard.Brookins@dep.state.fl.us.

Sincerely,

Marlane Castellanos

Branch Office Manager

FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION

INSPECTION REPORT FORM

AIR POLLUTANT EMISSION SOURCES

| FACILITY: Anderson Columbia Plant #4 | DISTRICT: Northwest | COUNTY: Bay |
| --- | --- | --- |
| ADDRESS: 1310 Redwood Avenue | PHONE: (850) 527-9408 | CONTACT: Vic Keisker |
| CONTACT OR FACILITY EMAIL ADDRESS: |
| ARMS I.D. #: 7775294 | PERMIT: 7775294-001-AC | EXPIRES: 10/04/2007 |
| RENEWAL APPLICATION/NOTIFICATION DUE DATE: 75 days from initial operation |
| SOURCE DESCRIPTION: Double drum mix asphalt plant |
| INSPECTED BY: Richard Brookins INSPECTION DATE: 02/01/2006 | AUDIT TYPE: Ins2 | COMPLIANCE STATUS: In Compliance |

INSPECTION COMMENTS

I arrived at the facility and was greeted by Mr. Vic Keisker.  Mr. Keisker accompanied me during the inspection of the facility and provided copies of requested records for review.  The facility was operating at the time of the inspection and Mr. Donnie Leeper of Astech Environmental Services was performing the required initial stack testing.

A review of the Method 5 sampling train was conducted and compliance with the published test method was verified.  Approximately 15 minutes into the third test run the unit was secured due to lack of silo storage space.  Since it was unknown when the testing would resume the initial inspection of the facility was conducted.

There were no objectionable odors noticed during the inspection.  [Facility-wide Condition 2]

There were no fugitive emissions in excess of 20% opacity noticed during the inspection.  [Facility-wide Condition 3]

There were no open containers of VOC’s or other Organic Solvents noticed during the inspection.  [Facility-wide Condition 5]

Reasonable precautions to prevent fugitive emissions were judged to be adequate at the time of the inspection.  Millled asphalt has been laid down for the facility roadways.  This should help alleviate some of the fugitive dust issues associated with the former plant.    [Facility-wide Condition 6]

A copy of the facility’s Operation and Maintenance Plan was available for review at the time of inspection.  [Facility-wide Condition 12]

EU001	ASPHALT PLANT

According to records provided the facility began initial operations on January 7, 2006 and produced 18,052.36 tons of asphalt concrete during the month of January 2006.  This is within the facility’s permitted limit of 500,000 tons in any consecutive 12-month period.  [Specific Condition A.2]

According to the records provided, the facility used 4,545 gallons of fuel oil for the burner during the same period.  This is within the facility’s maximum permitted limit of 1.2 million gallons total fuel oil usage by all sources (burner, heater, and RAP crusher) during in any consecutive 12-month period.  Information is maintained which shows fuel oil deliveries to be less than .0.5 % sulfur.  [Specific Condition A.3.(a)]

### According to the records provided, the facility operated for 91 hours during the month of January 2006.  The facility is allowed unlimited hours of operation.  [Specific Condition A.4]

Visible emissions were 0 % opacity at the time of the inspection.  [Specific Condition A.5]

### Scale calibration records are maintained and are available for review.  [Specific Condition A.8]

Monthly and 12-month rolling totals of asphalt concrete produced, fuel oil used, and hours of operation are maintained and were available for inspection.  [Specific Condition A.10]

RECOMMENDATIONS:

Submit the required Professional Engineer certification and Air Operating permit application within 75 days of initial operation as specified in the permit.