| INSPECTION REPORT FORM ENVIRONMENTAL PROTECTION COMMISSION OF HILLSBOROUGH COUNTY |
| --- |
| FACILITY: Tampa Amalgamated Steel Corp. | PAGE: 1 OF 2 |
| FACILITY ADDRESS: 5215 St. Paul St. | CITY: Tampa |
| MAILING ADDRESS: Same as above | CITY: Tampa | ST: FL | ZIP: 33601 |
| INSPECTION DATE: 07/23/07 | TIME IN: 10:00 AM | TIME OUT: 11:00 AM | INSPECTION TYPE: FCE Insp. | STATUS: IN |
| NEDS NO.: 0570358-003-AF |
| SOURCE DESCRIPTION: Spray Coating Operation. |
| CONTACT: Bill Updike, Project Coordinator |
| The purpose of this visit was to perform an FCE inspection. I was escorted on my walkthrough by Bill Updike, an architectural draftsman and project coordinator at the facility. There is a Wheelabrator machine maintained on site, however it has been inspected and deemed insignificant for PM emissions. The unit was in operation at the time of my inspection and no visible emissions were noted. All steel waste from the blasting operation was collected in a 55-gallon drum attached to the machine. The baghouse serving the Wheelabrator machine vents inside the building. The baghouse magnahelic reading was 1.5 in of H2O. No open air blasting or wire brushing is done at the facility. No unreported paints were in use at the facility at the time of the inspection. The facility maintains MSDSs for all paints in use. I inspected the storage area and noted that tightly fitting lids were maintained on all the paint drums. No spills were noticeable. No coatings containing lead are used. Primers, mineral spirits, and cleanup solvents are used, and they are accounted for in the facility’s recordkeeping system. The facility does not mix their paints with any thinners. I inspected the facility’s record keeping system and made copies before I left. I verified that the VOC contents of the paints used by the facility were under 3.5 lbs/ gal. I found the facility to be in compliance. Wheelabrator Grit Blasting Machine. |
| INSPECTORS: Jason Golden | REPORT DATE: 07/23/07 |