MARTIN COMBUSTION TURBINE UNIT 8 REFERENCE METHOD TEST PROTOCOL

Reference

Method		Parameter	Principle				Duration

EPA 3A		O2		Paramagnetic – continuous sampling	Continuous sampling with

using a heated stainless steel probe,	method 7E & 10

Teflon line and a moisture removal

system.

EPA 3A		CO2		Non-Dispersive infrared – continuous	Continuous sampling with

sampling using a heated stainless 	method 7E & 10

steel probe, Teflon line and a moisture

removal system.

EPA 7E		NOx 		Chemiluminescence – continuous	3 - 66 minute runs

sampling using a heated stainless 	&  9 – 22 minute

steel probe, Teflon line and a moisture	RATA runs

removal system.

EPA 9		Opacity		Visual Opacity				1 – 1 hour run

EPA 10		CO		Gas filter correlation, NDIR -		3 - 66 minute runs

continuous sampling using a heated 	&  9 – 22 minute

stainless steel probe, Teflon line and	RATA runs

a moisture removal system.

CTM-027	NH3		Isokinetic impinger absorption – 		3 - 1 hour runs

Using Ion Chromatography or

EPA 350.1 (Automated Colorimetric

Procedure) for analysis.

Please note that the relative accuracy test audit (RATA) and gas compliance tests are done simultaneously.

If you have any questions I can also be reached at the below listed numbers.

John Mirino

Florida Power & Light

Senior Emission Technician

office 305-242-3895

cell 786-236-9742