| 1030118 003 66750 |
| --- |
| FACILITY: Schneller, LLC | PERMIT ID: 172 |
|  | DISTRICT: Southwest |
| ADDRESS: 6200 49th St. No. | CONTACT PHONE: |
| Pinellas Park, FL | 727-521-2393 |
| ARMS NO: 1030118 003 | PERMIT NO: | Expiration Date: 2/12/12 Renewal Date: 7/2/11 |
|  | 1030118-011-AV |  |
|  |  | Test Due Date: 11/23/09 |
| EMISSION UNIT DESCRIPTION : Coating Line:(Building No. 2) Liberty Machine Co. coating machine with a combination reverse roll and knife-over-roll; 4.5 MMBtu/hour drying oven; with emission controlled by a Grehnrich & Grehnrich, Model HDFT-40H thermal incinerator at 1200° F |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  |  |  |  | INS1 |  | INS2 |  | INS3 |  | FUI |  | IN |  | MNC |  | SNC |
| INSPECTION TYPE: |  | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: Mssrs. Will Jones and Tom Pfeiffer greeted me, answered the administrative questions re: the facility, provided the VOC Logs, Maintenance Log, the Continuous Monitoring System Logs and Charts and provided answers in my walk through the facility re: the Emission Units. |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Mark Stewart? |  | Yes |  | No |
|  | Comments: |
| 4. | Is the facility contact still: Harold (Hal) Hudson? |  | Yes |  | No |
|  | Comments: |
| IN | MNC | SNC | B. Specific Conditions: |
|  |  |  | This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-6, TITLE V CONDITION 12(12)] Comments: Annual Operating Report for Air Pollutant Emitting Facility. (a) The Annual Operating Report for Air Pollutant Emitting Facility (DEP Form No. 62-210.900(5)) shall be completed each year. (b) The annual operating report shall be submitted to the appropriate Department of Environmental Protection (DEP) division, district or DEP-approved local air pollution control program office by March 1 of the following year. (c) Beginning with 2007 annual emissions, emissions shall be computed in accordance with the provisions of Rule 62-210.370(2), F.A.C., for purposes of the annual operating report. [APPENDIX TV-6, TITLE V CONDITION 24(3)] Comments: Renewals. Prior to one hundred eighty (180) days before the expiration of a permit issued pursuant to Chapter 62-213, F.A.C., the permittee shall apply for a renewal of a permit using forms incorporated by reference in the specific rule chapter for that kind of permit. [APPENDIX TV-6, TITLE V CONDITION 5] Comments: The permit application is due to be submitted on, or before xxxx. 2. General Pollutant Emission Limiting Standards: Objectionable Odor Prohibited - No person shall cause, suffer, allow or permit the discharge of air pollutants which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200, and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: 3. General Particulate Emission Limiting Standards: General Visible Emissions Standard - Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1 & 62-296.320(4)(b)4, F.A.C.] Comments: 4. Prevention of Accidental Releases (Section 112(r) of CAA)- a. The permittee shall submit its Risk Management Plan (RMP) to the Chemical Emergency Preparedness and Prevention Office (CEPPO) RMP Reporting Center when, and if, such requirement becomes applicable. b. The permittee shall submit to the permitting authority Title V certification forms or a compliance schedule in accordance with Rule 62-213.440(2), F.A.C. [40 CFR 68] Comments: 5. Insignificant Emissions Units and/or Activities - Appendix I-1, List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6), and 62-4.040(1)(b), F.A.C.] Comments: 6. Unregulated Emissions Units and/or Activities - Appendix U-1, List of Unregulated Emissions Units and/or Activities, is a part of this permit. [Rule 62-213.440(1), F.A.C.] Comments: 7. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. (a) Ensure all lids, caps, covers on cans and other containers are properly fitted and maintained such that vapor emissions are minimized. (b) Repair all leaks in piping, process equipment, and storage containers immediately and/or removing solvents to secure containers until repairs can be effected. (c) All VOCs from solvent washing (equipment cleanup) shall be directed into containers that prevent evaporation into the atmosphere. (d) For each parts cleaner, comply with each of the following requirements: 1. Equip the cleaner with a cover. The cover shall be so designed that it can be easily operated with one hand. 2. Equip the cleaner with a facility for draining cleaned parts. The drainage facility shall be constructed internally so that parts are enclosed under the cover while draining if the solvent volatility is greater than 0.6 pounds per square inch (31 millimeters of mercury or 4.1 kilopascals) measured at 100 degrees Fahrenheit (38 degrees Celsius), except that the drainage facility may be external for the applications where an internal type cannot fit into the cleaning system. 3. Provided a permanent, conspicuous label summarizing the operating requirements. 4. Store waste solvent only in covered containers. 5. Close the cover whenever parts are not being handled in the cleaner. 6. Drain the cleaned parts for at least 15 seconds or until dripping ceases. 7. If used, supply a solvent spray that is a solid fluid stream (not a fine, atomized, or shower-type spray) at a pressure which does not cause excessive splashing. [Rule 62-296.320(1)(a), F.A.C., previous Title V permit 1030118-010-AV] (Permitting Note: The volatility of MEK is greater than 0.6 pounds per square inch measured at 100 degrees Fahrenheit. The volatility of kerosene is less than 0.6 pounds per square inch measured at 100 degrees Fahrenheit). Comments: 9. Statement of Compliance – The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C. shall be submitted to this office, the EPA, and the Air Program of the Pinellas County Department of Environmental Management (PCDEM), within 60 days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-4.070(3), 62-213.440(3), and 62-213.900(7), F.A.C.] Comments: A.1. Methods of Operation - (Permitted Fuels) - The drying oven shall be fired with natural gas only. [Rule 62-213.440, F.A.C.] Comments: B.3. Federal NESHAPs Requirements - This emissions unit shall comply with the applicable provisions of 40 CFR 63, Subparts A (General Provisions to 40 CFR 63) and JJJJ (Paper and Other Web Coating) as adopted and incorporated by reference in Rule 62-204.800(11)(b), F.A.C., and referenced below*. The complete MACT standard is in the attached Appendix 40 CFR 63, Subpart JJJJ, which is a part of this permit. 40 CFR 63 Subpart JJJJ Applicable Provision References * 63.3280 What is in this subpart? 63.3290 Does this subpart apply to me? 63.3300 Which of my emission sources are affected by this subpart? 63.3310 What definitions are used in this subpart? 63.3320 What emission standards must I meet? 63.3321 What operating limits must I meet? 63.3321 (a) 63.3330 When must I comply? 63.3330 (a) 63.3340 What general requirements must I meet to comply with the standards? 63.3350 If I use a control device to comply with the emission standards what monitoring must I do? 63.3350 (a) 63.3350 (b) 63.3350 (e) 63.3350 (f) 63.3360 What performance tests must I conduct? 63.3360(a) 63.3360(e), except (3)(ii) 63.3360(f) 63.3360(g) 63.3370 How do I demonstrate compliance with the emission standards? 63.3370(a)(4) 63.3370(j), except (4)(ii), (iii), and (iv) 63.3370(k)(1), except (v) and (vi) 63.3370(k)(3)(i) 63.3400 What notifications and reports must I submit? 63.3400(a) 63.3400(b)(1) (Initial notification previously submitted) 63.3400(c), except (2)(vi) 63.3400(d) 63.3400(e) 63.3400(f) 63.3400(g) 63.3410 What records must I keep? 63.3400(a)(1)(ii)(v) 63.3400(a)(2) 63.3420 What authorities may be delegated to the States? Table 1 to Subpart JJJJ of Part 63 - Operating Limits if Using Add-On Control Devices and Capture System Table 1, Items (1) and (3) Appendix A to JJJJ of Part 63 - Applicability of 40 CFR 63 General Provisions to Subpart JJJJ * (Permitting Note: These applicability references are based upon current operations as reflected in the Title V permit renewal application dated 01/06/06, additional information response dated 3/28/06, and air construction permit application dated 7/13/06. Any change in operations may change the applicable provisions.) [Rules 62-204.800(11) and 62-213.400, F.A.C.; 40 CFR 63, Subparts A and JJJJ] Comments: B.4. Visible Emission (VE) Limitations - No visible emissions (defined as ≤5 percent opacity) are allowed from the incinerator, except that visible emissions not exceeding 20 percent opacity are allowed for up to three minutes in any one hour period. [Rule 62-296.401(1)(a), F.A.C.] Comments: B.5. Testing Requirements - In order to demonstrate compliance with condition Nos. B.1. through B.4.: (a) The permittee shall test the incinerator for visible emissions within 8 to 12 months prior to expiration of the permit. (b) The permittee shall test the incinerator for VOC emissions, including the destruction efficiency, within 365 to 425 days after the effective date of this permit, again within 31 to 33 months after the effective date of the permit, and again within 8 to 10 months prior to submittal of the Title V permit renewal application. (c) The permittee shall demonstrate the capture efficiency for the coating line concurrently with the destruction efficiency test by either: 1) show the enclosures continue to meet the requirements given in Procedure T for a Permanent Total Enclosure (EPA Method 204, Criteria for and verification of a Permanent or Temporary Total Enclosure) or 2) conduct a capture efficiency test for a temporary total enclosure pursuant to Rule 62-297.450, F.A.C. [Rules 62-297.310(7), 62-297.450(1)(a), and 62-297.440(7), F.A.C.] Comments: B.6. VOC Emissions Testing - VOC emissions testing at the incinerator inlet and outlet shall be conducted using EPA Method 25, or Attachment 3 of EPA 450/2-78-041, or alternate sampling procedures approved in writing by the Department (i.e., ASP No. 96-I-01, attached). When conducting a compliance test, a sample of each coating shall be taken and an EPA Method 24 test performed. The coating sample must be at least 1 liter and be representative of the coating as applied during the test. Data provided from the coating formulator may be submitted in lieu of the Method 24 test if the certification form in EPA 450/3-84-019 is properly completed for each affected coating. [Rules 62-4.070(3), 62-296.500(2)(b), and 62-297.401, F.A.C.] Comments: B.7. Operating Rate During Testing - Compliance testing shall occur, when the incinerator are operating within 90-100% of the maximum VOC loading rate allowed by this permit (256 lbs. VOC input/hour), if feasible. If it is impracticable to test at this rate, an incinerator may be tested at less than 90% of its maximum VOC loading rate. In this case, subsequent operation is limited to 110 percent of the test load until a new test is conducted. Once the unit is so limited, operation at higher capacities is allowed for no more than 15 consecutive days for the purpose of additional compliance testing to regain the authority to operate at a higher rate, not to exceed the maximum rate allowed by this permit (256 lbs. VOC input/hour). Testing at conditions that are not representative of normal operating conditions may invalidate the test. [Rule 62-297.310(2), F.A.C.] Comments: B.8. Visible Emissions Testing - VE testing shall be conducted on the incinerator using DEP Method 9, be a minimum of 60 minutes in duration, and be conducted concurrently with one of the VOC compliance tests. The minimum requirements for stationary point source emission test procedures shall be in accordance with Chapter 62-297, F.A.C. [Rule 62-297.310(4)(a)2, F.A.C.] Comments: B.9. Compliance Test Notification - The permittee shall notify the Air Program of the PCDEM at least 15 days prior to the date on which each formal compliance test is to begin (except for the capture efficiency test, see specific condition B.10.) of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner. [Rule 62-297.310(7)(a)9, F.A.C.] Comments: B.10. Capture Efficiency Test Notification - Should a capture efficiency test using a temporary total enclosure be required, the permittee shall notify the Air Programs of the Department’s Southwest District and the Air Program of the PCDEM 30 days prior to performing any capture efficiency test. [Rule 62-297.450(4)(d), F.A.C.] Comments: B.11. Modification Notification and Testing - A modification, as defined in Rule 62-210.200, is prohibited without prior approval by the Department, however if any other physical or operational change is made to the control system, the owner or operator shall notify the Air Programs of the Department’s Southwest District and the Air Program of the PCDEM of the change within 10 working days after making such change. The Department shall require the owner or operator of the affected activity, process, or emissions unit to conduct a new capture efficiency test and/or stack test if the Department has reason to believe (based on engineering calculations or empirical evidence) that a physical or operational change to the capture system has decreased the overall emissions reduction efficiency of the system. [Rule 62-297.450(4)(c), F.A.C.] Comments: B.12. Test Report Requirements - The owner or operator of an emissions unit for which a compliance test is required shall file a report with the Air Program of the PCDEM on the results of each such test. The required test report shall be filed with the Air Program of the PCDEM as soon as practical but not later than 45 days after the last sampling run of each test is completed. The test report shall provide, at minimum, the information required in Rule 62-297.310(8), F.A.C. In addition the report shall include the following: (a) overall VOC destruction efficiency and VOC capture efficiency results; (b) utilization rates of the coating(s) during the tests, in gallons per hour; (c) VOC loading rate to the incinerator during the test, in lbs./hour; (d) inlet and outlet VOC concentration of the incinerator and supporting calculations; (e) results of the Method 24 tests, or a certification by the coating manufacturer of the composition of the coating if it is supported by actual batch formulations; (f) incinerator operating parameters such as temperature and flow rates; (g) EPA audit results, if applicable; (h) a copy of the daily log for each test day (see condition B.14.); and (i) a copy of the monthly log for the month the test was conducted (see condition B.14.) Failure to submit the above data or the actual operating conditions may invalidate the test. [Rules 62-4.070(3) & 62-297.310(8), F.A.C.] Comments: B.13. Compliance Assurance Monitoring (CAM) - This emissions unit is subject to the CAM requirements contained in the attached Appendix CAM. Failure to adhere to the monitoring requirements specified does not necessarily indicate an exceedance of a specific emissions limitation, however, it may constitute good reason to require compliance testing pursuant to Rule 62-297.310(7)(b), F.A.C. [40 CFR 64; and Rules 62-204.800 and 62-213.440(1)(b)1.a., F.A.C.] Comments: Schneller, Inc. APPENDIX CAM Inspection note: this is a modified verision of the CAM Plan for inspection purposes. (05/15/06 ver) Compliance Assurance Monitoring Requirements 40 CFR 64.7 Operation of Approved Monitoring: 5. Commencement of Operation - The owner or operator shall conduct the monitoring required under this appendix upon the effective date of this Title V permit. [40 CFR 64.7(a)] Comments: 6. Proper Maintenance - At all times, the owner or operator shall maintain the monitoring, including but not limited to, maintaining necessary parts for routine repairs of the monitoring equipment. [40 CFR 64.7(b)] Comments: 7. Continued Operation - Except for, as applicable, monitoring malfunctions, associated repairs, and required quality assurance or control activities (including, as applicable, calibration checks and required zero and span adjustments), the owner or operator shall conduct all monitoring in continuous operation (or shall collect data at all required intervals) at all times that the pollutant-specific emissions unit is operating. Data recorded during monitoring malfunctions, associated repairs, and required quality assurance or control activities shall not be used for purposes of this part, including data averages and calculations, or fulfilling a minimum data availability requirement, if applicable. The owner or operator shall use all the data collected during all other periods in assessing the operation of the control device and associated control system. A monitoring malfunction is any sudden, infrequent, not reasonably preventable failure of the monitoring to provide valid data. Monitoring failures that are caused in part by poor maintenance or careless operation are not malfunctions. [40 CFR 64.7(c)] Comments: 8. Response to Excursions or Exceedances: (a) Upon detecting an excursion or exceedance, the owner or operator shall restore operation of the pollutant-specific emissions unit (including the control device and associated capture system) to its normal or usual manner of operation as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions. The response shall include minimizing the period of any startup, shutdown or malfunction and taking any necessary corrective actions to restore normal operation and prevent the likely recurrence of the cause of an excursion or exceedance (other than those caused by excused startup or shutdown conditions, if allowed by this permit). Such actions may include initial inspection and evaluation, recording that operations returned to normal without operator action (such as through response by a computerized distribution control system), or any necessary follow-up actions to return operation to within the indicator range, designated condition, or below the applicable emission limitation or standard, as applicable. (b) Determination of whether the owner or operator has used acceptable procedures in response to an excursion or exceedance will be based on information available, which may include but is not limited to, monitoring results, review of operation and maintenance procedures and records, and inspection of the control device, associated capture system, and the process. [40 CFR 64.7(d)(1) & (2)] Comments: 9. Documentation of need for improved monitoring - If the owner or operator identifies a failure to achieve compliance with an emission limitation or standard for which the approved monitoring did not provide an indication of an excursion or exceedance while providing valid data, or the results of compliance or performance testing document a need to modify the existing indicator ranges or designated conditions, the owner or operator shall promptly notify the permitting authority and, if necessary, submit a proposed modification to the Title V permit to address the necessary monitoring changes. Such a modification may include, but is not limited to, reestablishing indicator ranges or designated conditions, modifying the frequency of conducting monitoring and collecting data, or the monitoring of additional parameters. [40 CFR 64.7(e)] Comments: 40 CFR 64.8 Quality Improvement Plan (QIP) Requirements. 10. Based on the results of a determination made under CAM Condition 8.a., above, the permitting authority may require the owner or operator to develop and implement a QIP. Consistent with CAM Condition 4., an accumulation of exceedances or excursions exceeding 5 percent duration of a pollutant-specific emissions unit's operating time for a reporting period, may require the implementation of a QIP. The threshold may be set at a higher or lower percent or may rely on other criteria for purposes of indicating whether a pollutant-specific emissions unit is being maintained and operated in a manner consistent with good air pollution control practices. [40 CFR 64.8(a)] Comments: 11. Elements of a QIP: (a) The owner or operator shall maintain a written QIP, if required, and have it available for inspection. (b) The plan initially shall include procedures for evaluating the control performance problems and, based on the results of the evaluation procedures, the owner or operator shall modify the plan to include procedures for conducting one or more of the following actions, as appropriate: (1) Improved preventive maintenance practices. (2) Process operation changes. (3) Appropriate improvements to control methods. (4) Other steps appropriate to correct control performance. (5) More frequent or improved monitoring (only in conjunction with one or more steps under CAM Condition 11.b(1) through (4), above). [40 CFR 64.8(b)] Comments: 12. If a QIP is required, the owner or operator shall develop and implement a QIP as expeditiously as practicable and shall notify the permitting authority if the period for completing the improvements contained in the QIP exceeds 180 days from the date on which the need to implement the QIP was determined. [40 CFR 64.8(c)] Comments: 13. Following implementation of a QIP, upon any subsequent determination pursuant to CAM Condition 8.b., the permitting authority may require that an owner or operator make reasonable changes to the QIP if the QIP is found to have: (a) Failed to address the cause of the control device performance problems; or (b) Failed to provide adequate procedures for correcting control device performance problems as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions. [40 CFR 64.8(d)] Comments: 14. Implementation of a QIP shall not excuse the owner or operator of a source from compliance with any existing emission limitation or standard, or any existing monitoring, testing, reporting or recordkeeping requirement that may apply under federal, state, or local law, or any other applicable requirements under the Act. [40 CFR 64.8(e)] Comments: 40 CFR 64.9 Reporting And Recordkeeping Requirements. 15. General reporting requirements. (a) Commencing from the effective date of this permit, the owner or operator shall submit monitoring reports semi-annually to the permitting authority in accordance with Rule 62-213.440(1)(b)3.a., F.A.C. (b) A report for monitoring under this part shall include, at a minimum, the information required under Rule 62-213.440(1)(b)3.a., F.A.C., and the following information, as applicable: (1) Summary information on the number, duration and cause (including unknown cause, if applicable) of excursions or exceedances, as applicable, and the corrective actions taken; (2) Summary information on the number, duration and cause (including unknown cause, if applicable) for monitor downtime incidents (other than downtime associated with zero and span or other daily calibration checks, if applicable); and (3) A description of the actions taken to implement a QIP during the reporting period as specified in CAM Conditions 10. through 14. Upon completion of a QIP, the owner or operator shall include in the next summary report documentation that the implementation of the plan has been completed and reduced the likelihood of similar levels of excursions or exceedances occurring. [40 CFR 64.9(a)] Comments: 16. General recordkeeping requirements: (a) The owner or operator shall comply with the recordkeeping requirements specified in Rule 62-213.440(1)(b)2., F.A.C. The owner or operator shall maintain records of monitoring data, monitor performance data, corrective actions taken, any written quality improvement plan required pursuant to CAM Conditions 10. through 14. and any activities undertaken to implement a quality improvement plan, and other supporting information required to be maintained under this part (such as data used to document the adequacy of monitoring, or records of monitoring maintenance or corrective actions). (b) Instead of paper records, the owner or operator may maintain records on alternative media, such as microfilm, computer files, magnetic tape disks, or microfiche, provided that the use of such alternative media allows for expeditious inspection and review, and does not conflict with other applicable recordkeeping requirements. [40 CFR 64.9(b)] Comments: 40 CFR 64.10 Savings Provisions. 17. It should be noted that nothing in this appendix shall: (a) Excuse the owner or operator of a source from compliance with any existing emission limitation or standard, or any existing monitoring, testing, reporting or recordkeeping requirement that may apply under federal, state, or local law, or any other applicable requirements under the Act. The requirements of this appendix shall not be used to justify the approval of monitoring less stringent than the monitoring which is required under separate legal authority and are not intended to establish minimum requirements for the purpose of determining the monitoring to be imposed under separate authority under the Act, including monitoring in permits issued pursuant to Title I of the Act. The purpose of this part is to require, as part of the issuance of a permit under Title V of the Act, improved or new monitoring at those emissions units where monitoring requirements do not exist or are inadequate to meet the requirements of this part. (b) Restrict or abrogate the authority of the Administrator or the permitting authority to impose additional or more stringent monitoring, recordkeeping, testing, or reporting requirements on any owner or operator of a source under any provision of the Act, including but not limited to sections 114(a)(1) and 504(b), or state law, as applicable. (c) Restrict or abrogate the authority of the Administrator or permitting authority to take any enforcement action under the Act for any violation of an applicable requirement or of any person to take action under section 304 of the Act. [40 CFR 64.10] Comments: B.14. VOC Containing Material Usage Records - Records shall be kept of usage of all VOC containing materials to document compliance with the limitations of condition Nos. B.1. and B.2. The records shall include, at a minimum, the following: Daily record the following: (a) facility name, and date; (b) Emission Unit No. and description; (c) applicable rule, i.e., Rule 62-296.504, F.A.C.; (d) substrate type coated; (e) “As Applied” coatings and clean up solvents that were used, and the amount of each used in gallons; (f) VOC content, “As Applied”, of each coating used, in lbs VOC/gal of coating and lbs VOC/gal of solids, the VOC content of each clean up solvent used, in lbs VOC/gal of solvent, and the resultant daily average lbs VOC/gal of solids after controls, based on the latest approved test results; (g) hours of operation; (h) hourly VOC input (daily average) to the incinerator (lbs/hr); (i) hourly VOC output (daily average) from the incinerator (lbs/hr); and (j) resultant lbs VOC/gal of solids after control for each coating. Monthly, record the following: (k) facility name, month, and year; and (l) calculated VOC emissions for the month (lbs) and for the most recent consecutive 12-month period (tons). Records of all calculations used to determine VOC emissions, and supporting documentation ("As Supplied", "As Applied" sheets, MSD sheets, EPA data sheets, purchase orders, etc.) shall be kept for each coating and solvent which includes sufficient information to determine VOC emissions. Daily records shall be completed within five business days and monthly records shall be completed by the end of the following month. The above records shall be maintained for five years and made available to the Department and the Air Program of the PCDEM upon request. [Rules 62-213.440(1)(b)2.b., 62-296.500(2)(b), and 62-4.070(3), F.A.C.; Pinellas Co. Code, Section 58-90] Comments: B.15. Operation and Maintenance (O & M) Plan - Not federally enforceable. The attached O & M Plan, (or the plan as revised with prior approval of the Air Program of the PCDEM, shall be followed for the thermal incinerator. The O & M documentation logs that are a part of the plan shall be maintained for a minimum of two years. At a minimum the plan shall include the following: (a) operating parameters of the pollution control device; (b) time table for routine maintenance of the pollution control device as specified by the manufacturer; (c) time table of routine weekly, bi-weekly, or monthly observations of the pollution control device; (d) list of the type and quantity of the required spare parts for the pollution control device which are stored on the premises; and (e) a record log which indicates at a minimum: 1. when maintenance and observations were performed; 2. what maintenance and observations were performed; 3. who performed said maintenance and observations; and 4. acceptable parameter ranges for each operational check. [Pinellas County Code, Section 58-128] Comments: STANDARDIZED PERMIT CONDITIONS 40 CFR 63 (NESHAP) Subpart JJJJ – National Emission Standards for Hazardous Air Pollutants: Paper and Other Web Coating (also includes applicable provisions of 40 CFR 63 Subpart A – General Provisions to 40 CFR 63 NESHAPs) Department of Environmental Protection Bureau of Air Regulation Permit Writers Tools Standardized Conditions (Last Updated 08/25/06) (Source for Subpart JJJJ: Federal Register dated 12/04/02) NOTE: This appendix was created for Schneller, Inc., Permit No. 1030118-011-AV (Title V Air Operation Permit Renewal). Cover page, headers and footers were added to Standardized Conditions referenced above by the FDEP Southwest District Air Permitting Section on September 7, 2006. Sec. 63.3320 What emission standards must I meet? (a) If you own or operate any affected source that is subject to the requirements of this subpart, you must comply with these requirements on and after the compliance dates as specified in Sec. 63.3330. (b) You must limit organic HAP emissions to the level specified in paragraph (b)(1), (2), (3), or (4) of this section. (1) No more than 5 percent of the organic HAP applied for each month (95 percent reduction) at existing affected sources, and no more than 2 percent of the organic HAP applied for each month (98 percent reduction) at new affected sources; or (2) No more than 4 percent of the mass of coating materials applied for each month at existing affected sources, and no more than 1.6 percent of the mass of coating materials applied for each month at new affected sources; or (3) No more than 20 percent of the mass of coating solids applied for each month at existing affected sources, and no more than 8 percent of the coating solids applied for each month at new affected sources. (4) If you use an oxidizer to control organic HAP emissions, operate the oxidizer such that an outlet organic HAP concentration of no greater than 20 parts per million by volume (ppmv) by compound on a dry basis is achieved and the efficiency of the capture system is 100 percent. (c) You must demonstrate compliance with this subpart by following the procedures in Sec. 63.3370. Comments: Sec. 63.3321 What operating limits must I meet? (a) For any web coating line or group of web coating lines for which you use add-on control devices, unless you use a solvent recovery system and conduct a liquid-liquid material balance, you must meet the operating limits specified in Table 1 to this subpart or according to paragraph (b) of this section. These operating limits apply to emission capture systems and control devices, and you must establish the operating limits during the performance test according to the requirements in Sec. 63.3360(e)(3). You must meet the operating limits at all times after you establish them. (b) If you use an add-on control device other than those listed in Table 1 to this subpart or wish to monitor an alternative parameter and comply with a different operating limit, you must apply to the Administrator for approval of alternative monitoring under Sec. 63.8(f). Comments: Sec. 63.3330 When must I comply? (a) If you own or operate an existing affected source subject to the provisions of this subpart, you must comply by the compliance date. The compliance date for existing affected sources in this subpart is December 5, 2005. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). (b) If you own or operate a new affected source subject to the provisions of this subpart, your compliance date is immediately upon start-up of the new affected source or by December 4, 2002, whichever is later. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). (c) If you own or operate a reconstructed affected source subject to the provisions of this subpart, your compliance date is immediately upon startup of the affected source or by December 4, 2002, whichever is later. Existing affected sources which have undergone reconstruction as defined in Sec. 63.2 are subject to the requirements for new affected sources. The costs associated with the purchase and installation of air pollution control equipment are not considered in determining whether the existing affected source has been reconstructed. Additionally, the costs of retrofitting and replacing of equipment that is installed specifically to comply with this subpart are not considered reconstruction costs. You must complete any performance test required in Sec. 63.3360 within the time limits specified in Sec. 63.7(a)(2). Comments: Sec. 63.3340 What general requirements must I meet to comply with the standards? Table 2 to this subpart specifies the provisions of subpart A of this part that apply if you are subject to this subpart, such as startup, shutdown, and malfunction plans (SSMP) in Sec. 63.6(e)(3) for affected sources using a control device to comply with the emission standards. Comments: Sec. 63.3350 If I use a control device to comply with the emission standards, what monitoring must I do? (a) A summary of monitoring you must do follows: If you operate a web coating line, and have the following: Then you must: (1) Intermittently-controlled work stations ..... (2) Solvent recovery unit ................................ (3) Control Device........................................ (4) Capture system........................................... Record parameters related to possible exhaust flow bypass of control device and to coating use (§ 63.3350(c)). Operate continuous emission monitoring system and perform quarterly audits or determine volatile matter recovered and conduct a liquid-liquid material balance (§ 63.3350(d)). Operate continuous parameter monitoring system (§ 63.3350(e)). Monitor capture system operating parameter (§ 63.3350(f)). (b) Following the date on which the initial performance test of a control device is completed to demonstrate continuing compliance with the standards, you must monitor and inspect each capture system and each control device used to comply with Sec. 63.3320. You must install and operate the monitoring equipment as specified in paragraphs (c) and (f) of this section. (c) Bypass and coating use monitoring. If you own or operate web coating lines with intermittently-controlled work stations, you must monitor bypasses of the control device and the mass of each coating material applied at the work station during any such bypass. If using a control device for complying with the requirements of this subpart, you must demonstrate that any coating material applied on a never-controlled work station or an intermittently-controlled work station operated in bypass mode is allowed in your compliance demonstration according to Sec. 63.3370(n) and (o). The bypass monitoring must be conducted using at least one of the procedures in paragraphs (c)(1) through (4) of this section for each work station and associated dryer. (1) Flow control position indicator. Install, calibrate, maintain, and operate according to the manufacturer's specifications a flow control position indicator that provides a record indicating whether the exhaust stream from the dryer was directed to the control device or was diverted from the control device. The time and flow control position must be recorded at least once per hour as well as every time the flow direction is changed. A flow control position indicator must be installed at the entrance to any bypass line that could divert the exhaust stream away from the control device to the atmosphere. (2) Car-seal or lock-and-key valve closures. Secure any bypass line valve in the closed position with a car-seal or a lock-and-key type configuration. A visual inspection of the seal or closure mechanism must be performed at least once every month to ensure that the valve or damper is maintained in the closed position, and the exhaust stream is not diverted through the bypass line. (3) Valve closure continuous monitoring. Ensure that any bypass line valve or damper is in the closed position through continuous monitoring of valve position when the emission source is in operation and is using a control device for compliance with the requirements of this subpart. The monitoring system must be inspected at least once every month to verify that the monitor will indicate valve position. (4) Automatic shutdown system. Use an automatic shutdown system in which the web coating line is stopped when flow is diverted away from the control device to any bypass line when the control device is in operation. The automatic system must be inspected at least once every month to verify that it will detect diversions of flow and would shut down operations in the event of such a diversion. (d) Solvent recovery unit. If you own or operate a solvent recovery unit to comply with Sec. 63.3320, you must meet the requirements in either paragraph (d)(1) or (2) of this section depending on how control efficiency is determined. (1) Continuous emission monitoring system (CEMS). If you are demonstrating compliance with the emission standards in Sec. 63.3320 through continuous emission monitoring of a control device, you must install, calibrate, operate, and maintain the CEMS according to paragraphs (d)(1)(i) through (iii) of this section. (i) Measure the total organic volatile matter mass flow rate at both the control device inlet and the outlet such that the reduction efficiency can be determined. Each continuous emission monitor must comply with performance specification 6, 8, or 9 of 40 CFR part 60, appendix B, as appropriate. (ii) You must follow the quality assurance procedures in procedure 1, appendix F of 40 CFR part 60. In conducting the quarterly audits of the monitors as required by procedure 1, appendix F, you must use compounds representative of the gaseous emission stream being controlled. (iii) You must have valid data from at least 90 percent of the hours during which the process is operated. (2) Liquid-liquid material balance. If you are demonstrating compliance with the emission standards in Sec. 63.3320 through liquid-liquid material balance, you must install, calibrate, maintain, and operate according to the manufacturer's specifications a device that indicates the cumulative amount of volatile matter recovered by the solvent recovery device on a monthly basis. The device must be certified by the manufacturer to be accurate to within +/-2.0 percent by mass. (e) Continuous parameter monitoring system (CPMS). If you are using a control device to comply with the emission standards in Sec. 63.3320, you must install, operate, and maintain each CPMS specified in paragraphs (e)(9) and (10) and (f) of this section according to the requirements in paragraphs (e)(1) through (8) of this section. You must install, operate, and maintain each CPMS specified in paragraph (c) of this section according to paragraphs (e)(5) through (7) of this section. (1) Each CPMS must complete a minimum of one cycle of operation for each successive 15-minute period. You must have a minimum of four equally spaced successive cycles of CPMS operation to have a valid hour of data. (2) You must have valid data from at least 90 percent of the hours during which the process operated. (3) You must determine the hourly average of all recorded readings according to paragraphs (e)(3)(i) and (ii) of this section. (i) To calculate a valid hourly value, you must have at least three of four equally spaced data values from that hour from a continuous monitoring system (CMS) that is not out-of-control. (ii) Provided all of the readings recorded in accordance with paragraph (e)(3) of this section clearly demonstrate continuous compliance with the standard that applies to you, then you are not required to determine the hourly average of all recorded readings. (4) You must determine the rolling 3-hour average of all recorded readings for each operating period. To calculate the average for each 3-hour averaging period, you must have at least two of three of the hourly averages for that period using only average values that are based on valid data (i.e., not from out-of-control periods). (5) You must record the results of each inspection, calibration, and validation check of the CPMS. (6) At all times, you must maintain the monitoring system in proper working order including, but not limited to, maintaining necessary parts for routine repairs of the monitoring equipment. (7) Except for monitoring malfunctions, associated repairs, or required quality assurance or control activities (including calibration checks or required zero and span adjustments), you must conduct all monitoring at all times that the unit is operating. Data recorded during monitoring malfunctions, associated repairs, out-of-control periods, or required quality assurance or control activities shall not be used for purposes of calculating the emissions concentrations and percent reductions specified in Sec. 63.3370. You must use all the valid data collected during all other periods in assessing compliance of the control device and associated control system. A monitoring malfunction is any sudden, infrequent, not reasonably preventable failure of the monitoring system to provide valid data. Monitoring failures that are caused in part by poor maintenance or careless operation are not malfunctions. (8) Any averaging period for which you do not have valid monitoring data and such data are required constitutes a deviation, and you must notify the Administrator in accordance with Sec. 63.3400(c). (9) Oxidizer. If you are using an oxidizer to comply with the emission standards, you must comply with paragraphs (e)(9)(i) through (iii) of this section. (i) Install, calibrate, maintain, and operate temperature monitoring equipment according to the manufacturer's specifications. The calibration of the chart recorder, data logger, or temperature indicator must be verified every 3 months or the chart recorder, data logger, or temperature indicator must be replaced. You must replace the equipment whether you choose not to perform the calibration or the equipment cannot be calibrated properly. (ii) For an oxidizer other than a catalytic oxidizer, install, calibrate, operate, and maintain a temperature monitoring device equipped with a continuous recorder. The device must have an accuracy of +/-1 percent of the temperature being monitored in degrees Celsius, or +/-1[deg] Celsius, whichever is greater. The thermocouple or temperature sensor must be installed in the combustion chamber at a location in the combustion zone. (iii) For a catalytic oxidizer, install, calibrate, operate, and maintain a temperature monitoring device equipped with a continuous recorder. The device must be capable of monitoring temperature with an accuracy of +/-1 percent of the temperature being monitored in degrees Celsius or +/- 1 degree Celsius, whichever is greater. The thermocouple or temperature sensor must be installed in the vent stream at the nearest feasible point to the inlet and outlet of the catalyst bed. Calculate the temperature rise across the catalyst. (10) Other types of control devices. If you use a control device other than an oxidizer or wish to monitor an alternative parameter and comply with a different operating limit, you must apply to the Administrator for approval of an alternative monitoring method under Sec. 63.8(f). (f) Capture system monitoring. If you are complying with the emission standards in Sec. 63.3320 through the use of a capture system and control device for one or more web coating lines, you must develop a site-specific monitoring plan containing the information specified in paragraphs (f)(1) and (2) of this section for these capture systems. You must monitor the capture system in accordance with paragraph (f)(3) of this section. You must make the monitoring plan available for inspection by the permitting authority upon request. (1) The monitoring plan must: (i) Identify the operating parameter to be monitored to ensure that the capture efficiency determined during the initial compliance test is maintained; and (ii) Explain why this parameter is appropriate for demonstrating ongoing compliance; and (iii) Identify the specific monitoring procedures. (2) The monitoring plan must specify the operating parameter value or range of values that demonstrate compliance with the emission standards in Sec. 63.3320. The specified operating parameter value or range of values must represent the conditions present when the capture system is being properly operated and maintained. (3) You must conduct all capture system monitoring in accordance with the plan. (4) Any deviation from the operating parameter value or range of values which are monitored according to the plan will be considered a deviation from the operating limit. (5) You must review and update the capture system monitoring plan at least annually. Comments: Sec. 63.3360 What performance tests must I conduct? (a) The performance test methods you must conduct are as follows: If you control organic HAP on any individual web coating line or any group of web coating lines by: You must: (1) Limiting organic HAP or volatile matter content of coatings. Determine the organic HAP or volatile matter and coating solids content of coating materials according to procedures in § 63.3360(c) and (d). If applicable, determine the mass of volatile matter retained in the coated web or otherwise not emitted to the atmosphere according to § 63.3360(g). (2) Using a capture and control system. Conduct a performance test for each capture and control system to determine: the destruction or removal efficiency of each control device other than solvent recovery according to § 63.3360(e), and the capture efficiency of each capture system according to § 63.3360(f). If applicable, determine the mass of volatile matter retained in the coated web or otherwise not emitted to the atmosphere according to § 63.3360(g). (b) If you are using a control device to comply with the emission standards in Sec. 63.3320, you are not required to conduct a performance test to demonstrate compliance if one or more of the criteria in paragraphs (b)(1) through (3) of this section are met. (1) The control device is equipped with continuous emission monitors for determining inlet and outlet total organic volatile matter concentration and capture efficiency has been determined in accordance with the requirements of this subpart such that an overall organic HAP control efficiency can be calculated, and the continuous emission monitors are used to demonstrate continuous compliance in accordance with Sec. 63.3350; or (2) You have met the requirements of Sec. 63.7(h) (for waiver of performance testing; or (3) The control device is a solvent recovery system and you comply by means of a monthly liquid-liquid material balance. (c) Organic HAP content. If you determine compliance with the emission standards in Sec. 63.3320 by means other than determining the overall organic HAP control efficiency of a control device, you must determine the organic HAP mass fraction of each coating material ``as-purchased'' by following one of the procedures in paragraphs (c)(1) through (3) of this section, and determine the organic HAP mass fraction of each coating material ``as-applied'' by following the procedures in paragraph (c)(4) of this section. If the organic HAP content values are not determined using the procedures in paragraphs (c)(1) through (3) of this section, the owner or operator must submit an alternative test method for determining their values for approval by the Administrator in accordance with Sec. 63.7(f). The recovery efficiency of the test method must be determined for all of the target organic HAP and a correction factor, if necessary, must be determined and applied. (1) Method 311. You may test the coating material in accordance with Method 311 of appendix A of this part. The Method 311 determination may be performed by the manufacturer of the coating material and the results provided to the owner or operator. The organic HAP content must be calculated according to the criteria and procedures in paragraphs (c)(1)(i) through (iii) of this section. (i) Include each organic HAP determined to be present at greater than or equal to 0.1 mass percent for Occupational Safety and Health Administration (OSHA)-defined carcinogens as specified in 29 CFR 1910.1200(d)(4) and greater than or equal to 1.0 mass percent for other organic HAP compounds. (ii) Express the mass fraction of each organic HAP you include according to paragraph (c)(1)(i) of this section as a value truncated to four places after the decimal point (for example, 0.3791). (iii) Calculate the total mass fraction of organic HAP in the tested material by summing the counted individual organic HAP mass fractions and truncating the result to three places after the decimal point (for example, 0.763). (2) Method 24. For coatings, determine the volatile organic content as mass fraction of nonaqueous volatile matter and use it as a substitute for organic HAP using Method 24 of 40 CFR part 60, appendix A. The Method 24 determination may be performed by the manufacturer of the coating and the results provided to you. (3) Formulation data. You may use formulation data to determine the organic HAP mass fraction of a coating material. Formulation data may be provided to the owner or operator by the manufacturer of the material. In the event of an inconsistency between Method 311 (appendix A of 40 CFR part 63) test data and a facility's formulation data, and the Method 311 test value is higher, the Method 311 data will govern. Formulation data may be used provided that the information represents all organic HAP present at a level equal to or greater than 0.1 percent for OSHA-defined carcinogens as specified in 29 CFR 1910.1200(d)(4) and equal to or greater than 1.0 percent for other organic HAP compounds in any raw material used. (4) As-applied organic HAP mass fraction. If the as-purchased coating material is applied to the web without any solvent or other material added, then the as-applied organic HAP mass fraction is equal to the as-purchased organic HAP mass fraction. Otherwise, the as-applied organic HAP mass fraction must be calculated using Equation 1a of Sec. 63.3370. (d) Volatile organic and coating solids content. If you determine compliance with the emission standards in Sec. 63.3320 by means other than determining the overall organic HAP control efficiency of a control device and you choose to use the volatile organic content as a surrogate for the organic HAP content of coatings, you must determine the as-purchased volatile organic content and coating solids content of each coating material applied by following the procedures in paragraph (d)(1) or (2) of this section, and the as-applied volatile organic content and coating solids content of each coating material by following the procedures in paragraph (d)(3) of this section. (1) Method 24. You may determine the volatile organic and coating solids mass fraction of each coating applied using Method 24 (40 CFR part 60, appendix A.) The Method 24 determination may be performed by the manufacturer of the material and the results provided to you. If these values cannot be determined using Method 24, you must submit an alternative technique for determining their values for approval by the Administrator. (2) Formulation data. You may determine the volatile organic content and coating solids content of a coating material based on formulation data and may rely on volatile organic content data provided by the manufacturer of the material. In the event of any inconsistency between the formulation data and the results of Method 24 of 40 CFR part 60, appendix A, and the Method 24 results are higher, the results of Method 24 will govern. (3) As-applied volatile organic content and coating solids content. If the as-purchased coating material is applied to the web without any solvent or other material added, then the as-applied volatile organic content is equal to the as-purchased volatile content and the as-applied coating solids content is equal to the as-purchased coating solids content. Otherwise, the as-applied volatile organic content must be calculated using Equation 1b of Sec. 63.3370 and the as-applied coating solids content must be calculated using Equation 2 of Sec. 63.3370. (e) Control device efficiency. If you are using an add-on control device other than solvent recovery, such as an oxidizer, to comply with the emission standards in Sec. 63.3320, you must conduct a performance test to establish the destruction or removal efficiency of the control device according to the methods and procedures in paragraphs (e)(1) and (2) of this section. During the performance test, you must establish the operating limits required by Sec. 63.3321 according to paragraph (e)(3) of this section. (1) An initial performance test to establish the destruction or removal efficiency of the control device must be conducted such that control device inlet and outlet testing is conducted simultaneously, and the data are reduced in accordance with the test methods and procedures in paragraphs (e)(1)(i) through (ix) of this section. You must conduct three test runs as specified in Sec. 63.7(e)(3), and each test run must last at least 1 hour. (i) Method 1 or 1A of 40 CFR part 60, appendix A, must be used for sample and velocity traverses to determine sampling locations. (ii) Method 2, 2A, 2C, 2D, 2F, or 2G of 40 CFR part 60, appendix A, must be used to determine gas volumetric flow rate. (iii) Method 3, 3A, or 3B of 40 CFR part 60, appendix A, must be used for gas analysis to determine dry molecular weight. You may also use as an alternative to Method 3B the manual method for measuring the oxygen, carbon dioxide, and carbon monoxide content of exhaust gas in ANSI/ASME PTC 19.10-1981, ``Flue and Exhaust Gas Analyses [Part 10, Instruments and Apparatus],'' (incorporated by reference, see Sec. 63.14). (iv) Method 4 of 40 CFR part 60, appendix A, must be used to determine stack gas moisture. (v) The gas volumetric flow rate, dry molecular weight, and stack gas moisture must be determined during each test run specified in paragraph (f)(1)(vii) of this section. (vi) Method 25 or 25A of 40 CFR part 60, appendix A, must be used to determine total gaseous non-methane organic matter concentration. Use the same test method for both the inlet and outlet measurements which must be conducted simultaneously. You must submit notice of the intended test method to the Administrator for approval along with notification of the performance test required under Sec. 63.7(b). You must use Method 25A if any of the conditions described in paragraphs (e)(1)(vi)(A) through (D) of this section apply to the control device. (A) The control device is not an oxidizer. (B) The control device is an oxidizer but an exhaust gas volatile organic matter concentration of 50 ppmv or less is required to comply with the emission standards in Sec. 63.3320; or (C) The control device is an oxidizer but the volatile organic matter concentration at the inlet to the control system and the required level of control are such that they result in exhaust gas volatile organic matter concentrations of 50 ppmv or less; or (D) The control device is an oxidizer but because of the high efficiency of the control device the anticipated volatile organic matter concentration at the control device exhaust is 50 ppmv or less, regardless of inlet concentration. (vii) Except as provided in Sec. 63.7(e)(3), each performance test must consist of three separate runs with each run conducted for at least 1 hour under the conditions that exist when the affected source is operating under normal operating conditions. For the purpose of determining volatile organic compound concentrations and mass flow rates, the average of the results of all the runs will apply. (viii) Volatile organic matter mass flow rates must be determined for each run specified in paragraph (e)(1)(vii) of this section using Equation 1 of this section: Where: Mf = Total organic volatile matter mass flow rate, kilograms (kg)/hour (h). Qsd = Volumetric flow rate of gases entering or exiting the control device, as determined according to Sec. 63.3360(e)(1)(ii), dry standard cubic meters (dscm)/h. Cc = Concentration of organic compounds as carbon, ppmv. 12.0 = Molecular weight of carbon. 0.0416 = Conversion factor for molar volume, kg-moles per cubic meter (mol/m\3\) (@ 293 Kelvin (K) and 760 millimeters of mercury (mmHg)). (ix) For each run, emission control device destruction or removal efficiency must be determined using Equation 2 of this section: Where: E = Organic volatile matter control efficiency of the control device, percent. Mfi = Organic volatile matter mass flow rate at the inlet to the control device, kg/h. Mfo = Organic volatile matter mass flow rate at the outlet of the control device, kg/h. (x) The control device destruction or removal efficiency is determined as the average of the efficiencies determined in the test runs and calculated in Equation 2 of this section. (2) You must record such process information as may be necessary to determine the conditions in existence at the time of the performance test. Operations during periods of startup, shutdown, and malfunction will not constitute representative conditions for the purpose of a performance test. (3) Operating limits. If you are using one or more add-on control device other than a solvent recovery system for which you conduct a liquid-liquid material balance to comply with the emission standards in Sec. 63.3320, you must establish the applicable operating limits required by Sec. 63.3321. These operating limits apply to each add-on emission control device, and you must establish the operating limits during the performance test required by paragraph (e) of this section according to the requirements in paragraphs (e)(3)(i) and (ii) of this section. (i) Thermal oxidizer. If your add-on control device is a thermal oxidizer, establish the operating limits according to paragraphs (e)(3)(i)(A) and (B) of this section. (A) During the performance test, you must monitor and record the combustion temperature at least once every 15 minutes during each of the three test runs. You must monitor the temperature in the firebox of the thermal oxidizer or immediately downstream of the firebox before any substantial heat exchange occurs. (B) Use the data collected during the performance test to calculate and record the average combustion temperature maintained during the performance test. This average combustion temperature is the minimum operating limit for your thermal oxidizer. (ii) Catalytic oxidizer. If your add-on control device is a catalytic oxidizer, establish the operating limits according to paragraphs (e)(3)(ii)(A) and (B) or paragraphs (e)(3)(ii)(C) and (D) of this section. (A) During the performance test, you must monitor and record the temperature just before the catalyst bed and the temperature difference across the catalyst bed at least once every 15 minutes during each of the three test runs. (B) Use the data collected during the performance test to calculate and record the average temperature just before the catalyst bed and the average temperature difference across the catalyst bed maintained during the performance test. These are the minimum operating limits for your catalytic oxidizer. (C) As an alternative to monitoring the temperature difference across the catalyst bed, you may monitor the temperature at the inlet to the catalyst bed and implement a site-specific inspection and maintenance plan for your catalytic oxidizer as specified in paragraph (e)(3)(ii)(D) of this section. During the performance test, you must monitor and record the temperature just before the catalyst bed at least once every 15 minutes during each of the three test runs. Use the data collected during the performance test to calculate and record the average temperature just before the catalyst bed during the performance test. This is the minimum operating limit for your catalytic oxidizer. (D) You must develop and implement an inspection and maintenance plan for your catalytic oxidizer(s) for which you elect to monitor according to paragraph (e)(3)(ii)(C) of this section. The plan must address, at a minimum, the elements specified in paragraphs (e)(3)(ii)(D)(1) through (3) of this section. (1) Annual sampling and analysis of the catalyst activity (i.e., conversion efficiency) following the manufacturer's or catalyst supplier's recommended procedures, (2) Monthly inspection of the oxidizer system including the burner assembly and fuel supply lines for problems, and (3) Annual internal and monthly external visual inspection of the catalyst bed to check for channeling, abrasion, and settling. If problems are found, you must take corrective action consistent with the manufacturer's recommendations and conduct a new performance test to determine destruction efficiency in accordance with this section. (f) Capture efficiency. If you demonstrate compliance by meeting the requirements of Sec. 63.3370(e), (f), (g), (h), (i)(2), (k), (n)(2) or (3), or (p), you must determine capture efficiency using the procedures in paragraph (f)(1), (2), or (3) of this section, as applicable. (1) You may assume your capture efficiency equals 100 percent if your capture system is a permanent total enclosure (PTE). You must confirm that your capture system is a PTE by demonstrating that it meets the requirements of section 6 of EPA Method 204 of 40 CFR part 51, appendix M, and that all exhaust gases from the enclosure are delivered to a control device. (2) You may determine capture efficiency according to the protocols for testing with temporary total enclosures that are specified in Methods 204 and 204A through F of 40 CFR part 51, appendix M. You may exclude never-controlled work stations from such capture efficiency determinations. (3) You may use any capture efficiency protocol and test methods that satisfy the criteria of either the Data Quality Objective or the Lower Confidence Limit approach as described in appendix A of subpart KK of this part. You may exclude never-controlled work stations from such capture efficiency determinations. (g) Volatile matter retained in the coated web or otherwise not emitted to the atmosphere. You may choose to take into account the mass of volatile matter retained in the coated web after curing or drying or otherwise not emitted to the atmosphere when determining compliance with the emission standards in Sec. 63.3320. If you choose this option, you must develop a testing protocol to determine the mass of volatile matter retained in the coated web or otherwise not emitted to the atmosphere and submit this protocol to the Administrator for approval. You must submit this protocol with your site-specific test plan under Sec. 63.7(f). If you intend to take into account the mass of volatile matter retained in the coated web after curing or drying or otherwise not emitted to the atmosphere and demonstrate compliance according to Sec. 63.3370(c)(3), (c)(4), (c)(5), or (d), then the test protocol you submit must determine the mass of organic HAP retained in the coated web or otherwise not emitted to the atmosphere. Otherwise, compliance must be shown using the volatile organic matter content as a surrogate for the HAP content of the coatings. (h) Control devices in series. If you use multiple control devices in series to comply with the emission standards in Sec. 63.3320, the performance test must include, at a minimum, the inlet to the first control device in the series, the outlet of the last control device in the series, and all intermediate streams (e.g., gaseous exhaust to the atmosphere or a liquid stream from a recovery device) that are not subsequently treated by any of the control devices in the series. Comments: Sec. 63.3370 How do I demonstrate compliance with the emission standards? (a) A summary of how you must demonstrate compliance follows: If you choose to demonstrate compliance by: Then you must demonstrate that: To Accomplish this: (1) Use of ‘‘as-purchased’’ compliant coating materials. (i) Each coating material used at an existing affected source does not exceed 0.04 kg organic HAP per kg coating material, and each coating material used at a new affected source does not exceed 0.016 kg organic HAP per kg coating material as-purchased; or. Follow the procedures set out in § 63.3370(b). (ii) Each coating material used at an existing affected source does not exceed 0.2 kg organic HAP per kg coating solids, and each coating material used at a new affected source does not exceed 0.08 kg organic HAP per kg coating solids as-purchased. Follow the procedures set out in § 63.3370(b). (2) Use of ‘‘as-applied’’ compliant coating materials. (i) Each coating material used at an existing affected source does not exceed 0.04 kg organic HAP per kg coating material, and each coating material used at a new affected source does not exceed 0.016 kg organic HAP per kg coating material as-applied; or. Follow the procedures set out in § 63.3370(c)(1). Use either Equation 1a or b of § 63.3370 to determine compliance with § 63.3320(b)(2) in accordance with § 63.3370(c)(5)(i). (ii) Each coating material used at an existing affected source does not exceed 0.2 kg organic HAP per kg coating solids, and each coating material used at a new affected source does not exceed 0.08 kg organic HAP per kg coating solids as-applied; or. Follow the procedures set out in § 63.3370(c)(2). Use Equations 2 and 3 of § 63.3370 to determine compliance with § 63.3320(b)(3) in accordance with § 63.3370(c)(5)(i). (iii) Monthly average of all coating materials used at an existing affected source does not exceed 0.04 kg organic HAP per kg coating material, and monthly average of all coating materials used at a new affected source does not exceed 0.016 kg organic HAP per kg coating material as-applied on a monthly average basis; or. Follow the procedures set out in § 63.3370(c)(3). Use Equation 4 of § 63.3370 to determine compliance with § 63.3320(b)(2) in accordance with § 63.3370(c)(5)(ii). (iv) Monthly average of all coating materials used at an existing affected source does not exceed 0.2 kg organic HAP per kg coating solids, and monthly average of all coating materials used at a new affected source does not exceed 0.08 kg organic HAP per kg coating solids as-applied on a monthly average basis. Follow the procedures set out in § 63.3370(c)(4). Use Equation 5 of § 63.3370 to determine compliance with § 63.3320(b)(3) in accordance with § 63.3370(c)(5)(ii). (3) Tracking total monthly organic HAP applied Total monthly organic HAP applied does not exceed the calculated limit based on emission limitations. Follow the procedures set out in § 63.3370(d). Show that total monthly HAP applied (Equation 6 of § 63.3370) is less than the calculated equivalent allowable organic HAP (Equation 13a or b of § 63.3370). (4) Use of a capture system and control device (i) Overall organic HAP control efficiency is equal to 95 percent at an existing affected source and 98 percent at a new affected source on a monthly basis; or oxidizer outlet organic HAP concentration is no greater than 20 ppmv by compound and capture efficiency is 100 percent; or operating parameters are continuously monitored; or. Follow the procedures set out in § 63.3370(e) to determine compliance with § 63.3320(b)(1) according to § 63.3370(i) if using a solvent recovery device, or § 63.3370(j) if using a control device and CPMS, or § 63.3370(k) if using an oxidizer. (ii) Overall organic HAP emission rate does not exceed 0.2 kg organic HAP per kg coating solids for an existing affected source or 0.08 kg organic HAP per kg coating solids for a new affected source on a monthly average as-applied basis;. Follow the procedures set out in § 63.3370(f) to determine compliance with § 63.3320(b)(3) according to § 63.3370(i) if using a solvent recovery device, or § 63.3370(k) if using an oxidizer. (iii) Overall organic HAP emission rate does not exceed 0.04 kg organic HAP per kg coating material for an existing affected source or 0.016 kg organic HAP per kg coating material for a new affected source on a monthly average as-applied basis; or. Follow the procedures set out in § 63.3370(g) to determine compliance with § 63.3320(b)(2) according to § 63.3370(i) if using a solvent recovery device, or § 63.3370(k) if using an oxidizer. (iv) Overall organic HAP emission rate does not exceed the calculated limit based on emission limitations. Follow the procedures set out in § 63.3370(h). Show that the monthly organic HAP emission rate is less than the calculated equivalent allowable organic HAP emission rate (Equation 13a or b of § 63.3370). Calculate the monthly organic HAP emission rate according to § 63.3370(i) if using a solvent recovery device, or § 63.3370(k) if using an oxidizer. (5) Use of multiple capture and/or control devices. i) Overall organic HAP control efficiency is equal to 95 percent at an existing affected source and 98 percent at a new affected source on a monthly basis; or. Follow the procedures set out in § 63.3370(e) to determine compliance with § 63.3320(b)(1) according to § 63.3370(e)(1) or (2). (ii) Average equivalent organic HAP emission rate does not exceed 0.2 kg organic HAP per kg coating solids for an existing affected source or 0.08 kg organic HAP per kg coating solids for a new affected source on a monthly average as-applied basis; or. Follow the procedures set out in § 63.3370(f) to determine compliance with § 63.3320(b)(3) according to § 63.3370(n). (iii) Average equivalent organic HAP emission rate does not exceed 0.04 kg organic HAP per kg coating material for an existing affected source or 0.016 kg organic HAP per kg coating material for a new affected source on a monthly average as-applied basis; or. Follow the procedures set out in § 63.3370(g) to determine compliance with § 63.3320(b)(2) according to § 63.3370(n). (iv) Average equivalent organic HAP emission rate does not exceed the calculated limit based on emission limitations. Follow the procedures set out in § 63.3370(h). Show that the monthly organic HAP emission rate is less than the calculated equivalent allowable organic HAP emission rate (Equation 13a or b of § 63.3370) according to § 63.3370(n). (6) Use of a combination of compliant coatings and control devices. (i) Average equivalent organic HAP emission rate does not exceed 0.2 kg organic HAP per kg coating solids for an existing affected source or 0.08 kg organic HAP per kg coating solids for a new affected source on a monthly average as-applied basis; or. Follow the procedures set out in § 63.3370(f) to determine compliance with § 63.3320(b)(3) according to § 63.3370(n). (ii) Average equivalent organic HAP emission rate does not exceed 0.04 kg organic HAP per kg coating material for an existing affected source or 0.016 kg organic HAP per kg coating material for a new affected source on a monthly average as-appliedbasis; or. Follow the procedures set out in § 63.3370(g) to determine compliance with § 63.3320(b)(2) according to § 63.3370(n). (iii) Average equivalent organic HAP emission rate does not exceed the calculated limit based on emission limitations. Follow the procedures set out in § 63.3370(h). Show that the monthly organic HAP emission rate is less than the calculated equivalent allowable organic HAP emission rate (Equation 13a or b of § 63.3370) according to § 63.3370(n). (b) As-purchased ``compliant'' coating materials. (1) If you comply by using coating materials that individually meet the emission standards in Sec. 63.3320(b)(2) or (3), you must demonstrate that each coating material applied during the month at an existing affected source contains no more than 0.04 mass fraction organic HAP or 0.2 kg organic HAP per kg coating solids, and that each coating material applied during the month at a new affected source contains no more than 0.016 mass fraction organic HAP or 0.08 kg organic HAP per kg coating solids on an as-purchased basis as determined in accordance with Sec. 63.3360(c). (2) You are in compliance with emission standards in Sec. 63.3320(b)(2) and (3) if each coating material applied at an existing affected source is applied as-purchased and contains no more than 0.04 kg organic HAP per kg coating material or 0.2 kg organic HAP per kg coating solids, and each coating material applied at a new affected source is applied as-purchased and contains no more than 0.016 kg organic HAP per kg coating material or 0.08 kg organic HAP per kg coating solids. (c) As-applied ``compliant'' coating materials. If you comply by using coating materials that meet the emission standards in Sec. 63.3320(b)(2) or (3) as-applied, you must demonstrate compliance by following one of the procedures in paragraphs (c)(1) through (4) of this section. Compliance is determined in accordance with paragraph (c)(5) of this section. (1) Each coating material as-applied meets the mass fraction of coating material standard (Sec. 63.3320(b)(2)). You must demonstrate that each coating material applied at an existing affected source during the month contains no more than 0.04 kg organic HAP per kg coating material applied, and each coating material applied at a new affected source contains no more than 0.016 kg organic HAP per kg coating material applied as determined in accordance with paragraphs (c)(1)(i) and (ii) of this section. You must calculate the as-applied organic HAP content of as-purchased coating materials which are reduced, thinned, or diluted prior to application. (i) Determine the organic HAP content or volatile organic content of each coating material applied on an as-purchased basis in accordance with Sec. 63.3360(c). (ii) Calculate the as-applied organic HAP content of each coating material using Equation 1a of this section: Where: Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Chi = Organic HAP content of coating material, i, as-purchased, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = number of different materials added to the coating material. Chij = Organic HAP content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. or calculate the as-applied volatile organic content of each coating material using Equation 1b of this section: Where: Cavi = Monthly average, as-applied, volatile organic content of coating material, i, expressed as a mass fraction, kg/kg. Cvi = Volatile organic content of coating material, i, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Cvij = Volatile organic content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. (2) Each coating material as-applied meets the mass fraction of coating solids standard (Sec. 63.3320(b)(3)). You must demonstrate that each coating material applied at an existing affected source contains no more than 0.20 kg of organic HAP per kg of coating solids applied and each coating material applied at a new affected source contains no more than 0.08 kg of organic HAP per kg of coating solids applied. You must demonstrate compliance in accordance with paragraphs (c)(2)(i) and (ii) of this section. (i) Determine the as-applied coating solids content of each coating material following the procedure in Sec. 63.3360(d). You must calculate the as-applied coating solids content of coating materials which are reduced, thinned, or diluted prior to application, using Equation 2 of this section: Where: Csi = Coating solids content of coating material, i, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Csij = Coating solids content of material, j, added to as-purchased coating material, i, expressed as a mass-fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. (ii) Calculate the as-applied organic HAP to coating solids ratio using Equation 3 of this section: Where: Hsi = As-applied, organic HAP to coating solids ratio of coating material, i. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Casi = Monthly average, as-applied, coating solids content of coating material, i, expressed as a mass fraction, kg/kg. (3) Monthly average organic HAP content of all coating materials as-applied is less than the mass percent limit (Sec. 63.3320(b)(2)). Demonstrate that the monthly average as-applied organic HAP content of all coating materials applied at an existing affected source is less than 0.04 kg organic HAP per kg of coating material applied, and all coating materials applied at a new affected source are less than 0.016 kg organic HAP per kg of coating material applied, as determined by Equation 4 of this section: Where: HL = Monthly average, as-applied, organic HAP content of all coating materials applied, expressed as kg organic HAP per kg of coating material applied, kg/kg. p = Number of different coating materials applied in a month. Chi = Organic HAP content of coating material, i, as-purchased, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Chij = Organic HAP content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in Sec. 63.3370. (4) Monthly average organic HAP content of all coating materials as-applied is less than the mass fraction of coating solids limit (Sec. 63.3320(b)(3)). Demonstrate that the monthly average as-applied organic HAP content on the basis of coating solids applied of all coating materials applied at an existing affected source is less than 0.20 kg organic HAP per kg coating solids applied, and all coating materials applied at a new affected source are less than 0.08 kg organic HAP per kg coating solids applied, as determined by Equation 5 of this section: Where: Hs = Monthly average, as-applied, organic HAP to coating solids ratio, kg organic HAP/kg coating solids applied. p = Number of different coating materials applied in a month. Chi = Organic HAP content of coating material, i, as-purchased, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Chij = Organic HAP content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in Sec. 63.3370. Csi = Coating solids content of coating material, i, expressed as a mass fraction, kg/kg. Csij = Coating solids content of material, j, added to as-purchased coating material, i, expressed as a mass-fraction, kg/kg. (5) The affected source is in compliance with emission standards in Sec. 63.3320(b)(2) or (3) if: (i) The organic HAP content of each coating material as-applied at an existing affected source is no more than 0.04 kg organic HAP per kg coating material or 0.2 kg organic HAP per kg coating solids, and the organic HAP content of each coating material as-applied at a new affected source contains no more than 0.016 kg organic HAP per kg coating material or 0.08 kg organic HAP per kg coating solids; or (ii) The monthly average organic HAP content of all as-applied coating materials at an existing affected source are no more than 0.04 kg organic HAP per kg coating material or 0.2 kg organic HAP per kg coating solids, and the monthly average organic HAP content of all as-applied coating materials at a new affected source is no more than 0.016 kg organic HAP per kg coating material or 0.08 kg organic HAP per kg coating solids. (d) Monthly allowable organic HAP applied. Demonstrate that the total monthly organic HAP applied as determined by Equation 6 of this section is less than the calculated equivalent allowable organic HAP as determined by Equation 13a or b in paragraph (l) of this section: Where: Hm = Total monthly organic HAP applied, kg. p = Number of different coating materials applied in a month. Chi = Organic HAP content of coating material, i, as-purchased, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Chij = Organic HAP content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in Sec. 63.3370. (e) Capture and control to reduce emissions to no more than allowable limit (Sec. 63.3320(b)(1)). Operate a capture system and control device and demonstrate an overall organic HAP control efficiency of at least 95 percent at an existing affected source and at least 98 percent at a new affected source for each month, or operate a capture system and oxidizer so that an outlet organic HAP concentration of no greater than 20 ppmv by compound on a dry basis is achieved as long as the capture efficiency is 100 percent as detailed in Sec. 63.3320(b)(4). Unless one of the cases described in paragraph (e)(1), (2), or (3) of this section applies to the affected source, you must either demonstrate compliance in accordance with the procedure in paragraph (i) of this section when emissions from the affected source are controlled by a solvent recovery device, or the procedure in paragraph (k) of this section when emissions are controlled by an oxidizer or demonstrate compliance for a web coating line by operating each capture system and each control device and continuous parameter monitoring according to the procedures in paragraph (j) of this section. (1) If the affected source has only always-controlled work stations and operates more than one capture system or more than one control device, you must demonstrate compliance in accordance with the provisions of either paragraph (n) or (p) of this section. (2) If the affected source operates one or more never-controlled work stations or one or more intermittently-controlled work stations, you must demonstrate compliance in accordance with the provisions of paragraph (n) of this section. (3) An alternative method of demonstrating compliance with Sec. 63.3320(b)(1) is the installation of a PTE around the web coating line that achieves 100 percent capture efficiency and ventilation of all organic HAP emissions from the total enclosure to an oxidizer with an outlet organic HAP concentration of no greater than 20 ppmv by compound on a dry basis. If this method is selected, you must demonstrate compliance by following the procedures in paragraphs (e)(3)(i) and (ii) of this section. Compliance is determined according to paragraph (e)(3)(iii) of this section. (i) Demonstrate that a total enclosure is installed. An enclosure that meets the requirements in Sec. 63.3360(f)(1) will be considered a total enclosure. (ii) Determine the organic HAP concentration at the outlet of your total enclosure using the procedures in paragraph (e)(3)(ii)(A) or (B) of this section. (A) Determine the control device efficiency using Equation 2 of Sec. 63.3360 and the applicable test methods and procedures specified in Sec. 63.3360(e). (B) Use a CEMS to determine the organic HAP emission rate according to paragraphs (i)(2)(i) through (x) of this section. (iii) You are in compliance if the installation of a total enclosure is demonstrated and the organic HAP concentration at the outlet of the incinerator is demonstrated to be no greater than 20 ppmv by compound on a dry basis. (f) Capture and control to achieve mass fraction of coating solids applied limit (Sec. 63.3320(b)(3)). Operate a capture system and control device and limit the organic HAP emission rate from an existing affected source to no more than 0.20 kg organic HAP emitted per kg coating solids applied, and from a new affected source to no more than 0.08 kg organic HAP emitted per kg coating solids applied as determined on a monthly average as-applied basis. If the affected source operates more than one capture system, more than one control device, one or more never-controlled work stations, or one or more intermittently-controlled work stations, then you must demonstrate compliance in accordance with the provisions of paragraph (n) of this section. Otherwise, you must demonstrate compliance following the procedure in paragraph (i) of this section when emissions from the affected source are controlled by a solvent recovery device or the procedure in paragraph (k) of this section when emissions are controlled by an oxidizer. (g) Capture and control to achieve mass fraction limit (Sec. 63.3320(b)(2)). Operate a capture system and control device and limit the organic HAP emission rate to no more than 0.04 kg organic HAP emitted per kg coating material applied at an existing affected source, and no more than 0.016 kg organic HAP emitted per kg coating material applied at a new affected source as determined on a monthly average as-applied basis. If the affected source operates more than one capture system, more than one control device, one or more never-controlled work stations, or one or more intermittently-controlled work stations, then you must demonstrate compliance in accordance with the provisions of paragraph (n) of this section. Otherwise, you must demonstrate compliance following the procedure in paragraph (i) of this section when emissions from the affected source are controlled by a solvent recovery device or the procedure in paragraph (k) of this section when emissions are controlled by an oxidizer. (h) Capture and control to achieve allowable emission rate. Operate a capture system and control device and limit the monthly organic HAP emissions to less than the allowable emissions as calculated in accordance with paragraph (l) of this section. If the affected source operates more than one capture system, more than one control device, one or more never-controlled work stations, or one or more intermittently-controlled work stations, then you must demonstrate compliance in accordance with the provisions of paragraph (n) of this section. Otherwise, the owner or operator must demonstrate compliance following the procedure in paragraph (i) of this section when emissions from the affected source are controlled by a solvent recovery device or the procedure in paragraph (k) of this section when emissions are controlled by an oxidizer. (i) Solvent recovery device compliance demonstration. If you use a solvent recovery device to control emissions, you must show compliance by following the procedures in either paragraph (i)(1) or (2) of this section: (1) Liquid-liquid material balance. Perform a monthly liquid-liquid material balance as specified in paragraphs (i)(1)(i) through (v) of this section and use the applicable equations in paragraphs (i)(1)(vi) through (ix) of this section to convert the data to units of the selected compliance option in paragraphs (e) through (h) of this section. Compliance is determined in accordance with paragraph (i)(1)(x) of this section. (i) Determine the mass of each coating material applied on the web coating line or group of web coating lines controlled by a common solvent recovery device during the month. (ii) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied, organic HAP emission rate based on coating material applied, or emission of less than the calculated allowable organic HAP, determine the organic HAP content of each coating material as-applied during the month following the procedure in Sec. 63.3360(c). (iii) Determine the volatile organic content of each coating material as applied during the month following the procedure in Sec. 63.3360(d). (iv) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied or emission of less than the calculated allowable organic HAP, determine the coating solids content of each coating material applied during the month following the procedure in Sec. 63.3360(d). (v) Determine and monitor the amount of volatile organic matter recovered for the month according to the procedures in Sec. 63.3350(d). (vi) Recovery efficiency. Calculate the volatile organic matter collection and recovery efficiency using Equation 7 of this section: Where: Rv = Organic volatile matter collection and recovery efficiency, percent. Mvr = Mass of volatile matter recovered in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in Sec. 63.3370. p = Number of different coating materials applied in a month. Cvi = Volatile organic content of coating material, i, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Cvij = Volatile organic content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. (vii) Organic HAP emitted. Calculate the organic HAP emitted during the month using Equation 8 of this section: Where: He = Total monthly organic HAP emitted, kg. Rv = Organic volatile matter collection and recovery efficiency, percent. p = Number of different coating materials applied in a month. Chi = Organic HAP content of coating material, i, as-purchased, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Chij = Organic HAP content of material, j, added to as-purchased coating material, i, expressed as a mass fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in Sec. 63.3370. (viii) Organic HAP emission rate based on coating solids applied. Calculate the organic HAP emission rate based on coating solids applied using Equation 9 of this section: Where: L = Mass organic HAP emitted per mass of coating solids applied, kg/kg. He = Total monthly organic HAP emitted, kg. p = Number of different coating materials applied in a month. Csi = Coating solids content of coating material, i, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Csij = Coating solids content of material, j, added to as-purchased coating material, i, expressed as a mass-fraction, kg/kg. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. (ix) Organic HAP emission rate based on coating materials applied. Calculate the organic HAP emission rate based on coating material applied using Equation 10 of this section: Where: S = Mass organic HAP emitted per mass of material applied, kg/kg. He = Total monthly organic HAP emitted, kg. p = Number of different coating materials applied in a month. Mi = Mass of as-purchased coating material, i, applied in a month, kg. q = Number of different materials added to the coating material. Mij = Mass of material, j, added to as-purchased coating material, i, in a month, kg. (x) You are in compliance with the emission standards in Sec. 63.3320(b) if: (A) The volatile organic matter collection and recovery efficiency is 95 percent or greater at an existing affected source and 98 percent or greater at a new affected source; or (B) The organic HAP emission rate based on coating solids applied is no more than 0.20 kg organic HAP per kg coating solids applied at an existing affected source and no more than 0.08 kg organic HAP per kg coating solids applied at a new affected source; or (C) The organic HAP emission rate based on coating material applied is no more than 0.04 kg organic HAP per kg coating material applied at an existing affected source and no more than 0.016 kg organic HAP per kg coating material applied at a new affected source; or (D) The organic HAP emitted during the month is less than the calculated allowable organic HAP as determined using paragraph (l) of this section. (2) Continuous emission monitoring of capture system and control device performance. Demonstrate initial compliance through a performance test on capture efficiency and continuing compliance through continuous emission monitors and continuous monitoring of capture system operating parameters following the procedures in paragraphs (i)(2)(i) through (vii) of this section. Use the applicable equations specified in paragraphs (i)(2)(viii) through (x) of this section to convert the monitoring and other data into units of the selected compliance option in paragraphs (e) through (h) of this section. Compliance is determined in accordance with paragraph (i)(2)(xi) of this section. (i) Control device efficiency. Continuously monitor the gas stream entering and exiting the control device to determine the total organic volatile matter mass flow rate (e.g., by determining the concentration of the vent gas in grams per cubic meter and the volumetric flow rate in cubic meters per second such that the total organic volatile matter mass flow rate in grams per second can be calculated) such that the control device efficiency of the control device can be calculated for each month using Equation 2 of Sec. 63.3360. (ii) Capture efficiency monitoring. Whenever a web coating line is operated, continuously monitor the operating parameters established in accordance with Sec. 63.3350(f) to ensure capture efficiency. (iii) Determine the percent capture efficiency in accordance with Sec. 63.3360(f). (iv) Control efficiency. Calculate the overall organic HAP control efficiency achieved for each month using Equation 11 of this section: Where: R = Overall organic HAP control efficiency, percent. E = Organic volatile matter control efficiency of the control device, percent. CE = Organic volatile matter capture efficiency of the capture system, percent. (v) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied, organic HAP emission rate based on coating materials applied, or emission of less than the calculated allowable organic HAP, determine the mass of each coating material applied on the web coating line or group of web coating lines controlled by a common control device during the month. (vi) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied, organic HAP emission rate based on coating material applied, or emission of less than the calculated allowable organic HAP, determine the organic HAP content of each coating material as-applied during the month following the procedure in Sec. 63.3360(c). (vii) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied or emission of less than the calculated allowable organic HAP, determine the coating solids content of each coating material as-applied during the month following the procedure in Sec. 63.3360(d). (viii) Organic HAP emitted. Calculate the organic HAP emitted during the month for each month using Equation 12 of this section: Where: He = Total monthly organic HAP emitted, kg. R = Overall organic HAP control efficiency, percent. p = Number of different coating materials applied in a month. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Mi = Mass of as-purchased coating material, i, applied in a month, kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in this section. (ix) Organic HAP emission rate based on coating solids applied. Calculate the organic HAP emission rate based on coating solids applied using Equation 9 of this section. (x) Organic HAP emission rate based on coating materials applied. Calculate the organic HAP emission rate based on coating material applied using Equation 10 of this section. (xi) Compare actual performance to the performance required by compliance option. The affected source is in compliance with the emission standards in Sec. 63.3320(b) for each month if the capture system is operated such that the average capture system operating parameter is greater than or less than (as appropriate) the operating parameter value established in accordance with Sec. 63.3350(f); and (A) The organic volatile matter collection and recovery efficiency is 95 percent or greater at an existing affected source and 98 percent or greater at a new affected source; or (B) The organic HAP emission rate based on coating solids applied is no more than 0.20 kg organic HAP per kg coating solids applied at an existing affected source and no more than 0.08 kg organic HAP per kg coating solids applied at a new affected source; or (C) The organic HAP emission rate based on coating material applied is no more than 0.04 kg organic HAP per kg coating material applied at an existing affected source and no more than 0.016 kg organic HAP per kg coating material applied at a new affected source; or (D) The organic HAP emitted during the month is less than the calculated allowable organic HAP as determined using paragraph (l) of this section. (j) Capture and control system compliance demonstration procedures using a CPMS. If you use an add-on control device, you must demonstrate initial compliance for each capture system and each control device through performance tests and demonstrate continuing compliance through continuous monitoring of capture system and control device operating parameters as specified in paragraphs (j)(1) through (3) of this section. Compliance is determined in accordance with paragraph (j)(4) of this section. (1) Determine the control device destruction or removal efficiency using the applicable test methods and procedures in Sec. 63.3360(e). (2) Determine the emission capture efficiency in accordance with Sec. 63.3360(f). (3) Whenever a web coating line is operated, continuously monitor the operating parameters established according to Sec. 63.3350(e) and (f). (4) You are in compliance with the emission standards in Sec. 63.3320(b) if the control device is operated such that the average operating parameter value is greater than or less than (as appropriate) the operating parameter value established in accordance with Sec. 63.3360(e) for each 3-hour period, and the capture system operating parameter is operated at an average value greater than or less than (as appropriate) the operating parameter value established in accordance with Sec. 63.3350(f); and (i) The overall organic HAP control efficiency is 95 percent or greater at an existing affected source and 98 percent or greater at a new affected source; or (ii) The organic HAP emission rate based on coating solids applied is no more than 0.20 kg organic HAP per kg coating solids applied at an existing affected source and no more than 0.08 kg organic HAP per kg coating solids applied at a new affected source; or (iii) The organic HAP emission rate based on coating material applied is no more than 0.04 kg organic HAP per kg coating material applied at an existing affected source and no more than 0.016 kg organic HAP per kg coating material applied at a new affected source; or (iv) The organic HAP emitted during the month is less than the calculated allowable organic HAP as determined using paragraph (l) of this section. (k) Oxidizer compliance demonstration procedures. If you use an oxidizer to control emissions, you must show compliance by following the procedures in paragraph (k)(1) of this section. Use the applicable equations specified in paragraph (k)(2) of this section to convert the monitoring and other data into units of the selected compliance option in paragraph (e) through (h) of this section. Compliance is determined in accordance with paragraph (k)(3) of this section. (1) Demonstrate initial compliance through performance tests of capture efficiency and control device efficiency and continuing compliance through continuous monitoring of capture system and control device operating parameters as specified in paragraphs (k)(1)(i) through (vi) of this section: (i) Determine the oxidizer destruction efficiency using the procedure in Sec. 63.3360(e). (ii) Determine the capture system capture efficiency in accordance with Sec. 63.3360(f). (iii) Capture and control efficiency monitoring. Whenever a web coating line is operated, continuously monitor the operating parameters established in accordance with Sec. 63.3350(e) and (f) to ensure capture and control efficiency. (iv) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied, organic HAP emission rate based on coating materials applied, or emission of less than the calculated allowable organic HAP, determine the mass of each coating material applied on the web coating line or group of web coating lines controlled by a common oxidizer during the month. (v) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied, organic HAP emission rate based on coating material applied, or emission of less than the calculated allowable organic HAP, determine the organic HAP content of each coating material as-applied during the month following the procedure in Sec. 63.3360(c). (vi) If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied or emission of less than the calculated allowable organic HAP, determine the coating solids content of each coating material applied during the month following the procedure in Sec. 63.3360(d). (2) Convert the information obtained under paragraph (p)(1) of this section into the units of the selected compliance option using the calculation procedures specified in paragraphs (k)(2)(i) through (iv) of this section. (i) Control efficiency. Calculate the overall organic HAP control efficiency achieved using Equation 11 of this section. (ii) Organic HAP emitted. Calculate the organic HAP emitted during the month using Equation 12 of this section. (iii) Organic HAP emission rate based on coating solids applied. Calculate the organic HAP emission rate based on coating solids applied for each month using Equation 9 of this section. (iv) Organic HAP based on coating materials applied. Calculate the organic HAP emission rate based on coating material applied using Equation 10 of this section. (3) You are in compliance with the emission standards in Sec. 63.3320(b) if the oxidizer is operated such that the average operating parameter value is greater than the operating parameter value established in accordance with Sec. 63.3360(e) for each 3-hour period, and the capture system operating parameter is operated at an average value greater than or less than (as appropriate) the operating parameter value established in accordance with Sec. 63.3350(f); and (i) The overall organic HAP control efficiency is 95 percent or greater at an existing affected source and 98 percent or greater at a new affected source; or (ii) The organic HAP emission rate based on coating solids applied is no more than 0.20 kg organic HAP per kg coating solids applied at an existing affected source and no more than 0.08 kg organic HAP per kg coating solids applied at a new affected source; or (iii) The organic HAP emission rate based on coating material applied is no more than 0.04 kg organic HAP per kg coating material applied at an existing affected source and no more than 0.016 kg organic HAP per kg coating material applied at a new affected source; or (iv) The organic HAP emitted during the month is less than the calculated allowable organic HAP as determined using paragraph (l) of this section. (l) Monthly allowable organic HAP emissions. This paragraph provides the procedures and calculations for determining monthly allowable organic HAP emissions for use in demonstrating compliance in accordance with paragraph (d), (h), (i)(1)(x)(D), (i)(2)(xi)(D), or (k)(3)(iv) of this section. You will need to determine the amount of coating material applied at greater than or equal to 20 mass percent coating solids and the amount of coating material applied at less than 20 mass percent coating solids. The allowable organic HAP limit is then calculated based on coating material applied at greater than or equal to 20 mass percent coating solids complying with 0.2 kg organic HAP per kg coating solids at an existing affected source or 0.08 kg organic HAP per kg coating solids at a new affected source, and coating material applied at less than 20 mass percent coating solids complying with 4 mass percent organic HAP at an existing affected source and 1.6 mass-percent organic HAP at a new affected source as follows: (1) Determine the as-purchased mass of each coating material applied each month. (2) Determine the as-purchased coating solids content of each coating material applied each month in accordance with Sec. 63.3360(d)(1). (3) Determine the as-purchased mass fraction of each coating material which was applied at 20 mass percent or greater coating solids content on an as-applied basis. (4) Determine the total mass of each solvent, diluent, thinner, or reducer added to coating materials which were applied at less than 20 mass percent coating solids content on an as-applied basis each month. (5) Calculate the monthly allowable organic HAP emissions using Equation 13a of this section for an existing affected source: Where: Ha = Monthly allowable organic HAP emissions, kg. p = Number of different coating materials applied in a month. Mi = mass of as-purchased coating material, i, applied in a month, kg. Gi = Mass fraction of each coating material, i, which was applied at 20 mass percent or greater coating solids content, on an as-applied basis, kg/kg. Csi = Coating solids content of coating material, i, expressed as a mass fraction, kg/kg. q = Number of different materials added to the coating material. MLj = Mass of non-coating-solids-containing coating material, j, added to coating-solids-containing coating materials which were applied at less than 20 mass percent coating solids content, on an as-applied basis, in a month, kg. or Equation 13b of this section for a new affected source: Where: Ha = Monthly allowable organic HAP emissions, kg. p = Number of different coating materials applied in a month. Mi = Mass of as-purchased coating material, i, applied in a month, kg. Gi = Mass fraction of each coating material, i, which was applied at 20 mass percent or greater coating solids content, on an as-applied basis, kg/kg. Csi = Coating solids content of coating material, i, expressed as a mass fraction, kg/kg. q = Number of different materials added to the coating material. MLj = Mass of non-coating-solids-containing coating material, j, added to coating-solids-containing coating materials which were applied at less than 20 mass percent coating solids content, on an as-applied basis, in a month, kg. (n) Combinations of capture and control. If you operate more than one capture system, more than one control device, one or more never-controlled work stations, or one or more intermittently-controlled work stations, you must calculate organic HAP emissions according to the procedures in paragraphs (n)(1) through (4) of this section, and use the calculation procedures specified in paragraph (n)(5) of this section to convert the monitoring and other data into units of the selected control option in paragraphs (e) through (h) of this section. Use the procedures specified in paragraph (n)(6) of this section to demonstrate compliance. (1) Solvent recovery system using liquid-liquid material balance compliance demonstration. If you choose to comply by means of a liquid-liquid material balance for each solvent recovery system used to control one or more web coating lines, you must determine the organic HAP emissions for those web coating lines controlled by that solvent recovery system either: (i) In accordance with paragraphs (i)(1)(i) through (iii) and (v) through (vii) of this section, if the web coating lines controlled by that solvent recovery system have only always-controlled work stations; or (ii) In accordance with paragraphs (i)(1)(ii), (iii), (v), and (vi) and (o) of this section, if the web coating lines controlled by that solvent recovery system have one or more never-controlled or intermittently-controlled work stations. (2) Solvent recovery system using performance test compliance demonstration and CEMS. To demonstrate compliance through an initial test of capture efficiency, continuous monitoring of a capture system operating parameter, and a CEMS on each solvent recovery system used to control one or more web coating lines, you must: (i) For each capture system delivering emissions to that solvent recovery system, monitor the operating parameter established in accordance with Sec. 63.3350(f) to ensure capture system efficiency; and (ii) Determine the organic HAP emissions for those web coating lines served by each capture system delivering emissions to that solvent recovery system either: (A) In accordance with paragraphs (i)(2)(i) through (iii), (v), (vi), and (viii) of this section, if the web coating lines served by that capture and control system have only always-controlled work stations; or (B) In accordance with paragraphs (i)(2)(i) through (iii), (vi), and (o) of this section, if the web coating lines served by that capture and control system have one or more never-controlled or intermittently-controlled work stations. (3) Oxidizer. To demonstrate compliance through performance tests of capture efficiency and control device efficiency, continuous monitoring of capture system, and CPMS for control device operating parameters for each oxidizer used to control emissions from one or more web coating lines, you must: (i) Monitor the operating parameter in accordance with Sec. 63.3350(e) to ensure control device efficiency; and (ii) For each capture system delivering emissions to that oxidizer, monitor the operating parameter established in accordance with Sec. 63.3350(f) to ensure capture efficiency; and (iii) Determine the organic HAP emissions for those web coating lines served by each capture system delivering emissions to that oxidizer either: (A) In accordance with paragraphs (k)(1)(i) through (vi) of this section, if the web coating lines served by that capture and control system have only always-controlled work stations; or (B) In accordance with paragraphs (k)(1)(i) through (iii), (v), and (o) of this section, if the web coating lines served by that capture and control system have one or more never-controlled or intermittently-controlled work stations. (4) Uncontrolled coating lines. If you own or operate one or more uncontrolled web coating lines, you must determine the organic HAP applied on those web coating lines using Equation 6 of this section. The organic HAP emitted from an uncontrolled web coating line is equal to the organic HAP applied on that web coating line. (5) Convert the information obtained under paragraphs (n)(1) through (4) of this section into the units of the selected compliance option using the calculation procedures specified in paragraphs (n)(5)(i) through (iv) of this section. (i) Organic HAP emitted. Calculate the organic HAP emissions for the affected source for the month by summing all organic HAP emissions calculated according to paragraphs (n)(1), (2)(ii), (3)(iii), and (4) of this section. (ii) Coating solids applied. If demonstrating compliance on the basis of organic HAP emission rate based on coating solids applied or emission of less than the calculated allowable organic HAP, the owner or operator must determine the coating solids content of each coating material applied during the month following the procedure in Sec. 63.3360(d). (iii) Organic HAP emission rate based on coating solids applied. Calculate the organic HAP emission rate based on coating solids applied for each month using Equation 9 of this section. (iv) Organic HAP based on materials applied. Calculate the organic HAP emission rate based on material applied using Equation 10 of this section. (6) Compliance. The affected source is in compliance with the emission standards in Sec. 63.3320(b) for the month if all operating parameters required to be monitored under paragraphs (n)(1) through (3) of this section were maintained at the values established under Sec. Sec. 63.3350 and 63.3360; and (i) The total mass of organic HAP emitted by the affected source based on coating solids applied is no more than 0.20 kg organic HAP per kg coating solids applied at an existing affected source and no more than 0.08 kg organic HAP per kg coating solids applied at a new affected source; or (ii) The total mass of organic HAP emitted by the affected source based on material applied is no more than 0.04 kg organic HAP per kg material applied at an existing affected source and no more than 0.016 kg organic HAP per kg material applied at a new affected source; or (iii) The total mass of organic HAP emitted by the affected source during the month is less than the calculated allowable organic HAP as determined using paragraph (l) of this section; or (iv) The total mass of organic HAP emitted by the affected source was not more than 5 percent of the total mass of organic HAP applied for the month at an existing affected source and no more than 2 percent of the total mass of organic HAP applied for the month at a new affected source. The total mass of organic HAP applied by the affected source in the month must be determined using Equation 6 of this section. (o) Intermittently-controlled and never-controlled work stations. If you have been expressly referenced to this paragraph by paragraphs (n)(1)(ii), (n)(2)(ii)(B), or (n)(3)(iii)(B) of this section for calculation procedures to determine organic HAP emissions for your intermittently-controlled and never-controlled work stations, you must: (1) Determine the sum of the mass of all coating materials as-applied on intermittently-controlled work stations operating in bypass mode and the mass of all coating materials as-applied on never-controlled work stations during the month. (2) Determine the sum of the mass of all coating materials as-applied on intermittently-controlled work stations operating in a controlled mode and the mass of all coating materials applied on always-controlled work stations during the month. (3) Liquid-liquid material balance compliance demonstration. For each web coating line or group of web coating lines for which you use the provisions of paragraph (n)(1)(ii) of this section, you must calculate the organic HAP emitted during the month using Equation 14 of this section: Where: He = Total monthly organic HAP emitted, kg. p = Number of different coating materials applied in a month. Mci = Sum of the mass of coating material, i, as-applied on intermittently-controlled work stations operating in controlled mode and the mass of coating material, i, as-applied on always-controlled work stations, in a month, kg. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Rv = Organic volatile matter collection and recovery efficiency, percent. MBi = Sum of the mass of coating material, i, as-applied on intermittently-controlled work stations operating in bypass mode and the mass of coating material, i, as-applied on never-controlled work stations, in a month, kg. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in this section. (4) Performance test to determine capture efficiency and control device efficiency. For each web coating line or group of web coating lines for which you use the provisions of paragraph (n)(2)(ii)(B) or (n)(3)(iii)(B) of this section, you must calculate the organic HAP emitted during the month using Equation 15 of this section: Where: He = Total monthly organic HAP emitted, kg. p = Number of different coating materials applied in a month. Mci = Sum of the mass of coating material, i, as-applied on intermittently-controlled work stations operating in controlled mode and the mass of coating material, i, as-applied on always-controlled work stations, in a month, kg. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. R = Overall organic HAP control efficiency, percent. MBi = Sum of the mass of coating material, i, as-applied on intermittently-controlled work stations operating in bypass mode and the mass of coating material, i, as-applied on never-controlled work stations, in a month, kg. Cahi = Monthly average, as-applied, organic HAP content of coating material, i, expressed as a mass fraction, kg/kg. Mvret = Mass of volatile matter retained in the coated web after curing or drying, or otherwise not emitted to the atmosphere, kg. The value of this term will be zero in all cases except where you choose to take into account the volatile matter retained in the coated web or otherwise not emitted to the atmosphere for the compliance demonstration procedures in this section. (p) Always-controlled work stations with more than one capture and control system. If you operate more than one capture system or more than one control device and only have always-controlled work stations, then you are in compliance with the emission standards in Sec. 63.3320(b)(1) for the month if for each web coating line or group of web coating lines controlled by a common control device: (1) The volatile matter collection and recovery efficiency as determined by paragraphs (i)(1)(i), (iii), (v), and (vi) of this section is at least 95 percent at an existing affected source and at least 98 percent at a new affected source; or (2) The overall organic HAP control efficiency as determined by paragraphs (i)(2)(i) through (iv) of this section for each web coating line or group of web coating lines served by that control device and a common capture system is at least 95 percent at an existing affected source and at least 98 percent at a new affected source; or (3) The overall organic HAP control efficiency as determined by paragraphs (k)(1)(i) through (iii) and (k)(2)(i) of this section for each web coating line or group of web coating lines served by that control device and a common capture system is at least 95 percent at an existing affected source and at least 98 percent at a new affected source. Comments: Sec. 63.3400 What notifications and reports must I submit? (a) Each owner or operator of an affected source subject to this subpart must submit the reports specified in paragraphs (b) through (g) of this section to the Administrator: (b) You must submit an initial notification as required by Sec. 63.9(b). (1) Initial notification for existing affected sources must be submitted no later than 1 year before the compliance date specified in Sec. 63.3330(a). (2) Initial notification for new and reconstructed affected sources must be submitted as required by Sec. 63.9(b). (3) For the purpose of this subpart, a title V or part 70 permit application may be used in lieu of the initial notification required under Sec. 63.9(b), provided the same information is contained in the permit application as required by Sec. 63.9(b) and the State to which the permit application has been submitted has an approved operating permit program under part 70 of this chapter and has received delegation of authority from the EPA to implement and enforce this subpart. (4) If you are using a permit application in lieu of an initial notification in accordance with paragraph (b)(3) of this section, the permit application must be submitted by the same due date specified for the initial notification. (c) You must submit a semiannual compliance report according to paragraphs (c)(1) and (2) of this section. (1) Compliance report dates. (i) The first compliance report must cover the period beginning on the compliance date that is specified for your affected source in Sec. 63.3330 and ending on June 30 or December 31, whichever date is the first date following the end of the calendar half immediately following the compliance date that is specified for your affected source in Sec. 63.3330. (ii) The first compliance report must be postmarked or delivered no later than July 31 or January 31, whichever date follows the end of the calendar half immediately following the compliance date that is specified for your affected source in Sec. 63.3330. (iii) Each subsequent compliance report must cover the semiannual reporting period from January 1 through June 30 or the semiannual reporting period from July 1 through December 31. (iv) Each subsequent compliance report must be postmarked or delivered no later than July 31 or January 31, whichever date is the first date following the end of the semiannual reporting period. (v) For each affected source that is subject to permitting regulations pursuant to 40 CFR part 70 or 40 CFR part 71, and the permitting authority has established dates for submitting semiannual reports pursuant to Sec. 70.6(a)(3)(iii)(A) or Sec. 71.6(a)(3)(iii)(A), you may submit the first and subsequent compliance reports according to the dates the permitting authority has established instead of according to the dates in paragraphs (c)(1)(i) through (iv) of this section. (2) The compliance report must contain the information in paragraphs (c)(2)(i) through (vi) of this section: (i) Company name and address. (ii) Statement by a responsible official with that official's name, title, and signature certifying the accuracy of the content of the report. (iii) Date of report and beginning and ending dates of the reporting period. (iv) If there are no deviations from any emission limitations (emission limit or operating limit) that apply to you, a statement that there were no deviations from the emission limitations during the reporting period, and that no CMS was inoperative, inactive, malfunctioning, out-of-control, repaired, or adjusted. (v) For each deviation from an emission limitation (emission limit or operating limit) that applies to you and that occurs at an affected source where you are not using a CEMS to comply with the emission limitations in this subpart, the compliance report must contain the information in paragraphs (c)(2)(i) through (iii) of this section, and: (A) The total operating time of each affected source during the reporting period. (B) Information on the number, duration, and cause of deviations (including unknown cause), if applicable, and the corrective action taken. (C) Information on the number, duration, and cause for CPMS downtime incidents, if applicable, other than downtime associated with zero and span and other calibration checks. (vi) For each deviation from an emission limit occurring at an affected source where you are using a CEMS to comply with the emission limit in this subpart, you must include the information in paragraphs (c)(2)(i) through (iii) and (vi)(A) through (J) of this section. (A) The date and time that each malfunction started and stopped. (B) The date and time that each CEMS and CPMS, if applicable, was inoperative except for zero (low-level) and high-level checks. (C) The date and time that each CEMS and CPMS, if applicable, was out-of-control, including the information in Sec. 63.8(c)(8). (D) The date and time that each deviation started and stopped, and whether each deviation occurred during a period of startup, shutdown, or malfunction or during another period. (E) A summary of the total duration (in hours) of each deviation during the reporting period and the total duration of each deviation as a percent of the total source operating time during that reporting period. (F) A breakdown of the total duration of the deviations during the reporting period into those that are due to startup, shutdown, control equipment problems, process problems, other known causes, and other unknown causes. (G) A summary of the total duration (in hours) of CEMS and CPMS downtime during the reporting period and the total duration of CEMS and CPMS downtime as a percent of the total source operating time during that reporting period. (H) A breakdown of the total duration of CEMS and CPMS downtime during the reporting period into periods that are due to monitoring equipment malfunctions, nonmonitoring equipment malfunctions, quality assurance/quality control calibrations, other known causes, and other unknown causes. (I) The date of the latest CEMS and CPMS certification or audit. (J) A description of any changes in CEMS, CPMS, or controls since the last reporting period. (d) You must submit a Notification of Performance Tests as specified in Sec. Sec. 63.7 and 63.9(e) if you are complying with the emission standard using a control device and you are required to conduct a performance test of the control device. This notification and the site-specific test plan required under Sec. 63.7(c)(2) must identify the operating parameters to be monitored to ensure that the capture efficiency of the capture system and the control efficiency of the control device determined during the performance test are maintained. Unless EPA objects to the parameter or requests changes, you may consider the parameter approved. (e) You must submit a Notification of Compliance Status as specified in Sec. 63.9(h). (f) You must submit performance test reports as specified in Sec. 63.10(d)(2) if you are using a control device to comply with the emission standard and you have not obtained a waiver from the performance test requirement or you are not exempted from this requirement by Sec. 63.3360(b). The performance test reports must be submitted as part of the notification of compliance status required in Sec. 63.3400(e). (g) You must submit startup, shutdown, and malfunction reports as specified in Sec. 63.10(d)(5), except that the provisions in subpart A of this part pertaining to startups, shutdowns, and malfunctions do not apply unless a control device is used to comply with this subpart. (1) If actions taken by an owner or operator during a startup, shutdown, or malfunction of an affected source (including actions taken to correct a malfunction) are not consistent with the procedures specified in the affected source's SSMP required by Sec. 63.6(e)(3), the owner or operator must state such information in the report. The startup, shutdown, or malfunction report must consist of a letter containing the name, title, and signature of the responsible official who is certifying its accuracy and must be submitted to the Administrator. (2) Separate startup, shutdown, and malfunction reports are not required if the information is included in the report specified in paragraph (c)(2)(vi) of this section. Comments: Sec. 63.3410 What records must I keep? (a) Each owner or operator of an affected source subject to this subpart must maintain the records specified in paragraphs (a)(1) and (2) of this section on a monthly basis in accordance with the requirements of Sec. 63.10(b)(1): (1) Records specified in Sec. 63.10(b)(2) of all measurements needed to demonstrate compliance with this standard, including: (i) Continuous emission monitor data in accordance with the requirements of Sec. 63.3350(d); (ii) Control device and capture system operating parameter data in accordance with the requirements of Sec. 63.3350(c), (e), and (f); (iii) Organic HAP content data for the purpose of demonstrating compliance in accordance with the requirements of Sec. 63.3360(c); (iv) Volatile matter and coating solids content data for the purpose of demonstrating compliance in accordance with the requirements of Sec. 63.3360(d); (v) Overall control efficiency determination using capture efficiency and control device destruction or removal efficiency test results in accordance with the requirements of Sec. 63.3360(e) and (f); and (vi) Material usage, organic HAP usage, volatile matter usage, and coating solids usage and compliance demonstrations using these data in accordance with the requirements of Sec. 63.3370(b), (c), and (d). (2) Records specified in Sec. 63.10(c) for each CMS operated by the owner or operator in accordance with the requirements of Sec. 63.3350(b). (b) Each owner or operator of an affected source subject to this subpart must maintain records of all liquid-liquid material balances performed in accordance with the requirements of Sec. 63.3370. The records must be maintained in accordance with the requirements of Sec. 63.10(b). Tables to Subpart JJJJ of Part 63 Table 1 to Subpart JJJJ of Part 63. Operating Limits if Using Add-On Control Devices and Capture System For the following Device: You must meet the following operating limit And you must demonstrate continuous compliance with operating limits by: 1. Thermal Oxidizer a. The average combustion temperature in any 3-hour period must not fall below the combustion temperature limit established according to § 63.3360(e)(3)(i). i. Collecting the combustion temperature data according to § 63.3350(e)(9); ii. Reducing the data to 3-hour block averages; and iii. Maintain the 3-hour average combustion temperature at or above the temperature limit. 3. Emission Capture System Submit monitoring plan to the Administrator that identifies operating parameters to be monitored according to § 63.3350(f). Conduct monitoring according to the plan (§ 63.3350(f)(3)). |
|  |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating. Yes No Comments: The Rotogravure Printing Press, Emission Unit 004, has been dismantled and removed from the premises. |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: |
| Inspector(s): Jose Rodriguez, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? |  | ARMS? |  |

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030118 003 66750.doc

| AIRS ID 1030118 | OWNER Schneller, LLC | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report |  |
| DONE N/A | Statement of compliance |  |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs |  |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) |  |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jose Rodriguez		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.