| 1030180 75734 |  |
| --- | --- |
| FACILITY: Interprint, Inc. | PERMIT ID: 928 |
| Web Plant (Plant B) | DISTRICT: Southwest |
| ADDRESS: 12030 31st Court North | CONTACT PHONE: |
| Pinellas Park, FL | 727-572-7785 |
| ARMS NO: 1030180 001 | PERMIT NO: | Expiration Date: 11/4/2013 Renewal Date: 9/5/2013 |
|  | 1030180-007-AO & 1030180-008-AC |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Lithographic printer: Two Harris heat set web lithographic presses (Model Nos. M 110B and M 300M; Two natural gas fired drying ovens; with emissions from the drying ovens are controlled by a Langbein & Englebrecht (L & E), Model No. TR 592, RTO |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | February 15, 2011 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review | ( | Yes |  | No |
|  | Comments: The file was reviewed prior to inspection |  |  |  |  |
| 2. | Introduction and Entry | ( | Yes |  | No |
|  | Comments: I met on site with Matt Allen and Scott Morten |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Scott Morten? | ( | Yes |  | No |
|  | Comments: Yes, he is still the owner The Responsible Official/Authorized Representative’s e-mail is: |
| 4. | Is the facility contact still: Scott Morten? | ( | Yes |  | No |
|  | Comments: yes, but Matt Allen keeps the records and msd sheets. The facility contact’s e-mail is: |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: Permit (1030180-007-AO) authorizes the continued operation permit (1030180-008-AC) authorizes the decrease in permitted emission limitations from 99.9 to 90.0 tons per any 12 consecutive month period of VOCs; from 24.9 to 20.0 tons per any 12 consecutive month period of total HAPs; and from 9.9 to 9.0 tons per any 12 consecutive month period of any individual HAP. It removes the daily recordkeeping requirements. It also removes the 5% visible emission limitation on the regenerative thermal oxidizer and associated testing requirements. These permits were issued simultaneously on 11/4/08 This permit or a copy thereof shall be kept at the work site of the permitted activity. [General Condition 12.] Comments: The facility ( did □ did not have a copy of the permit on-site. Mr. Allen maintains the permit copies in the front office. Operating and Emission Limitations 4. Volatile Organic Compound (VOC) and Hazardous Air Pollutant (HAP) Emission Limitations - Facility-wide emissions of VOCs and HAPs, as defined in Rule 62-210.200, F.A.C., shall not exceed the following: a. Total VOC emissions shall not exceed 90.0 tons in any consecutive 12-month period. b. Total HAP emissions shall not exceed 20.0 tons in any consecutive 12- month period. c. The highest individual HAP emissions shall not exceed 9.0 tons in any consecutive 12-month period. [Rule 62-210.200, F.A.C. (“Potential to Emit”); Construction Permit 1030180-008-AC] Comments: The highest reported emissions were 2.158 tons VOC, 0.33 tons total HAPS, and 0.08 tons individual HAPS for the month of August 2010, the 12-month period VOC total was 26.09 Tons. The reviewed records for the months of December 2010 through January 2011. 5. General Standards: Objectionable Odor - The permittee shall not cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An "Objectionable Odor" is defined as any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. If the Department or the Pinellas County Department of Environmental Management (PCDEM) receive a valid odor complaint from either location, the Department reserves the right to require additional odor control measures/work practices be implemented. [Rules 62-210.200 and 62-296.320(2), F.A.C.; Pinellas County Code, Section 58-178] Comments: There were no objectionable odors outside the building. The Harris press M 300 was in operation and the RTO was on line. The operations of the presses are maintained inside the building and no odors were detected outside or downwind of the RTO. 6. General Standards: Volatile Organic Compound Emissions and/or Organic Solvent Emissions - The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The following procedures shall be utilized to minimize pollutant emissions: a. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions and spills of solvent materials. b. All VOC/OS from washings (equipment clean-up) shall be directed into containers that prevent evaporation into the atmosphere. c. Tightly cover or close all VOC containers when they are not in use. d. Prevent excessive air turbulence across exposed VOCs. e. Immediately confine and clean up VOC spills and make sure wastes are placed in closed containers for reuse, recycling or proper disposal. [Rules 62-4.070(3) and 62-296.320(1), F.A.C.; Construction Permit 1030180-005-AC] Comments: the equipment was in good condition and no leaks observed around the printing presses, the facility press areas were clean, no spills of fluids from washing or solutions tanks, all working areas are well maintained. The containers were closed and tank tops were closed. There were no exposed solutions to the atmosphere. 7. General Standards: Visible Emissions - Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). [Rule 62-296.320(4)(b)1., F.A.C.] Comments: The RTO was in operation. There were no visible emissions from the stack as was observed during survey outside the building. 8. General Standards: Unconfined Particulate Matter (PM) - All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. [Rule 62-296.320(4)(c), F.A.C.] Comments: there were no activities being performed at this facility that would create unconfined emission. No PM emissions were observed. 9. Excess Emissions - Excess emissions which are caused entirely or in part by poor maintenance, poor operation, or any other equipment or process failure which may reasonably be prevented during startup, shutdown, or malfunction shall be prohibited. [Rule 62-210.700(4), F.A.C.] Comments: there were no excess emissions resulting from operation or maintenance issues. The RTO, is operated on the VOC from the presses and is monitored by a consultant company which keeps in check at all times during the operation and calibrates to prevent operation failure. 10. Modification - Unless otherwise exempt by rule, the permittee shall not initiate any construction, reconstruction, or modification at the facility and shall not install/modify any pollution control device at the facility without obtaining prior authorization from the Department. Modification is defined as: Any physical change or changes in the method of operations or addition to a facility that would result in an increase in the actual emissions of any air pollutant subject to air regulations, including any not previously emitted, from any emission unit or facility. [Rules 62-210.200 (“Modification”) and 62-210.300(1)(a), F.A.C.] Comments: There have been no modifications of equipment or additional equipment or changes to the presses, inks or solutions used in the operations at this facility. 11. Special Compliance Tests - When the Department or PCDEM, after investigation, has good reason (such as complaints, increased visible emissions, or questionable maintenance of control equipment) to believe that any applicable emission standard contained in a Department rule or in a permit issued pursuant to those rules is being violated, it may require the owner or operator of the emissions unit to conduct compliance tests which identify the nature and quantity of pollutant emissions from the emission unit and to provide a report on the results of said tests to the Department and/or PCDEM. [Rule 62-297.310(7)(b), F.A.C.] Comments: There are no special compliance tests required by the departments for this emission unit. 12. VOC/HAP Monthly Records – In order to demonstrate compliance with the VOC and HAPs limitations of Specific Condition No. 4, the permittee shall maintain monthly VOC and HAP records/logs which at a minimum shall contain the following: VOC Records: a. Facility name, facility ID No., 1030180, Emission Unit No. 001, Heat Set Web Lithographic Printing Facility, and month/year; b. total quantity of each VOC containing materials (i.e. inks, coatings, thinners, solvents, etc.) used for the entire facility for the month; c. VOC content of each VOC containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the entire facility during the month; d. calculated (based upon material VOC content) monthly total VOC emissions (pounds or tons per month) for the entire facility; e. cumulative total of the VOC emissions for the most recent 12 consecutive month period (tons per 12 consecutive month period) for the entire facility; HAP Records: f. facility name, facility ID No., 1030180, Emission Unit No. 001, Heat Set Web Lithographic Printing Facility and month/year; g. total quantity of each HAP containing material (i.e. inks, coatings, thinners, solvents, etc.) used for the entire facility for the month; h. HAP content of each HAP containing material (i.e., inks, coatings, thinners, solvents, etc.) used for the entire facility during the month; i. calculated (based upon material HAP content) monthly HAP emissions for each individual HAP and for total HAPs (pounds or tons per month) for the entire facility; and j. cumulative total of the HAP emissions for each individual HAP and for total HAPs for the most recent 12 consecutive month period (tons per 12 consecutive month period) for the entire facility. (Permitting Note: The RTO destruction efficiency shall not be used in the recordkeeping to show compliance with the emission limits of Specific Condition No. 4.) [Rule 62-4.070(3), F.A.C.; Construction Permit 1030180-005-AC] Comments: The records meet the requirements of a-j above for facility and permit number ID , material content, HAP and VOC amounts, totals and 12 month rolling totals. See copies of records attached. 13. Documentation – Supporting documentation (e.g., MSDS sheets, “As Supplied” sheets, “As Applied” sheets, purchase orders, inventory records, production records, etc.) for the records required by Specific Condition No. 12, which shall include sufficient information to determine VOC and HAP emissions, shall be kept at the facility. At the permittee’s option, “quantity purchased” may be reported to satisfy the requirement of “quantity used”, provided no materials are used which are not purchased. [Rule 62-4.070(3), F.A.C.] Comments: Mr. Allen maintains the up to date MSD sheets are contained in binders in the facility work area. The inks, thinners, blanket washes and solvents msds sheets are kept for all the products used for the presses operations. I requested a copy of the HWO colortrac LTSS process yellow ink 6-2655 and listed as I003 in the records. 14. Records Completion and Retention - Monthly records required by Specific Condition No. 12 shall be completed by the 10th day of the following month. Records shall be maintained on-site or electronically available on-site for a minimum of the most recent three (3) year period and made available to the Department and the Air Quality Division of the Pinellas County Department of Environmental Management (PCDEM), upon request. [Rule 62-4.070(3), F.A.C.] Comments: Mr. Allen maintains the records for the facility back to 2004 on site. The most recent are kept in his desk and the other copies are kept in binders in another cabinet in the main office. The current year’s copies are also kept in the personal computer in the front office. 15. Plant Operation Problems - If the permittee is temporarily unable to comply with any of the conditions of the permit due to breakdown of equipment or destruction by hazard of fire, wind or by other cause, the permittee shall immediately notify the Air Quality Division of the PCDEM. Notification shall include pertinent information as to the cause of the problem, and what steps are being taken to correct the problem and to prevent its recurrence, and where applicable, the owner's intent toward reconstruction of destroyed facilities. Such notification does not release the permittee from any liability for failure to comply with Department rules. [Rule 62-4.130, F.A.C.; Construction Permit 1030180-005-AC] Comments: There have been no upset conditions fires, storm damage or other issues that resulted in the facility being unable to comply with the permit conditions. 16. Plant Operation Problems Notification - For purposes of notification to the Department pursuant to Rule 62-4.130, F.A.C., Plant Operation-Problems, “immediately” shall mean the same day, if during a workday (i.e., 8:00 a.m. - 5:00 p.m.), or the first business day after the incident, excluding weekends and holidays. [Rule 62-4.070(3), F.A.C.; Construction Permit 1030180-005-AC] Comments: There has been no notification to the Department at this time. The facility has not experienced any plant operation upsets. 17. Annual Operating Report (AOR) - On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. Note, the annual operating report for calendar year 2008 shall be submitted on or before May 1, 2009. If the report is be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, a hardcopy may be sent to the to the Air Compliance section of the Pinellas County Department of Environmental Management. If only a hardcopy is sent, send the report to the Air Compliance section of the Pinellas County Department of Environmental Management. [Rule 62-210.370(3), F.A.C.] Comments: Mr. Allen stated that the 2009 AOR was submitted on time and as required, and the 2010 AOR report has been completed and submitted by the consultant Dean Barcenas, and should be received by the Department in the near future. 18. Operation Permit Renewal Application - A completed application for renewal of the operation permit shall be submitted to the Air Permitting Section of the Department’s Southwest District Office with a copy to the Pinellas County Department of Environmental Management no later than 60 days prior to the expiration date of the operation permit… [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit is no expiring at this time this is not applicable. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: There have been no changes to the equipment at this time. |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; □ P2 Manual; □ P2 Checklist Have any emissions reductions occurred □ Yes / No □ Chemical Substitution; □ Equipment Changes; □ Process Changes □ Chemical/Material Reuse; □ On-site Recycling; Other: Comments: The facility is certified to use recycled paper for the presses. They used recycled paper 1% of the time and are using TRI, SFP, PAPER, due to customer demand is low. He sends out 250 lbs of paper goes to Tampa company for being recycled and the aluminum printer plates are sent to recyclers. Mr. Morten had replaced the fluorescent tube that does not have ballast has circuit board and has lower wattage with reflectors, 3 years ago. |
| Closing Conference: I informed Mr. Allen that the facility appears to be in compliance at this time. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: February 17, 2011 |
| ACCESS? |  | ARMS? |  |

No Photos camera would not operate.