| 1030223 001 70973 |
| --- |
| FACILITY: Catalina Yachts, Morgan Division | PERMIT ID: 26 |
|  | DISTRICT: Southwest |
| ADDRESS: 7200 Bryan Dairy Road | CONTACT PHONE: |
| Largo, FL | 727-544 6681 |
| ARMS NO: 1030223 001 | PERMIT NO: | Expiration Date: 4/1/2009 Renewal Date: 10/3/2008 *AV (1030223-011-AV) has not been issued by FDEP. It is still in review[jm] |
|  | 1030223-007-AV & 1030223-010-AC |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Fiberglass Boat Manufacturing |
| CMS INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | February 8, 2010 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The Responsible Official/Authorized Representative’s e-mail is: mike@catalinayachts.com |
| 4. | Is the facility contact still: Michael Quinn? |  | Yes |  | No |
|  | Comments: The facility contact’s e-mail is: mike@catalinayachts.com |
| IN | MNC | SNC | B. Specific Conditions: |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Inspection note: There are two current permits (10-0223-010-AC and 1030223-007-AV). Permit 1030223-007-AV is still effective until the final renewal permit (1030223-011-AV) is issued. Permit 103-0223-10-AC allows for establishment of a dedicated varnish room and allows for lamination and gelcoating activities associated with the manufacture of dinghies and other small parts in the previous small storage building. Unless otherwise noted, the conditions are from permit 1030223-007-AV. Section II. Facility-wide Conditions. This permit or a copy thereof shall be kept at the work site of the permitted activity. [APPENDIX TV-4, TITLE V CONDITION 12(12)] Comments: reviewed on-site permit 2. General Pollutant Emission Limiting Standards. Objectionable Odor Prohibited. No person shall cause, suffer, allow, or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. [Rule 62-296.320(2), F.A.C., Pinellas County Code, Section 58-178; AC52-262880] Comments: An upwind/downwind survey of the facility was conducted. The observed parameters were: Downwind odor detected- None ; Wind direction – E/10 mph Upwind odor detected-None No odors detected around the perimeter of the facility. All doors of the lamination bay were closed. All 11 ventilation fans were operating including the 4 fans on the north side, the 4 fans on the south and the 3 operating on the roof. 3. General Particulate Emission Limiting Standards. General Visible Emissions Standard. Except for emissions units that are subject to a particulate matter or opacity limit set forth or established by rule and reflected by conditions in this permit, no person shall cause, let, permit, suffer or allow to be discharged into the atmosphere the emissions of air pollutants from any activity, the density of which is equal to or greater than that designated as Number 1 on the Ringelmann Chart (20 percent opacity). EPA Method 9 is the method of compliance pursuant to Chapter 62-297, F.A.C. [Rules 62-296.320(4)(b)1. & 4., F.A.C.] Comments: No particulate emissions observed 4. Prevention of Accidental Releases (Section 112(r) of CAA). If required by 40 CFR 68, the permittee shall submit to the implementing agency: A. A risk management plan (RMP) when, and if, such requirement becomes applicable; and B. Certification forms and/or RMPs according to the promulgated rule schedule. [40 CFR 68] Comments: Does not apply to this condition 5. Insignificant Emissions Units and/or Activities. Appendix I-1: List of Insignificant Emissions Units and/or Activities, is a part of this permit. [Rules 62-213.440(1), 62-213.430(6) and 62-4.040(1)(b), F.A.C.] Comments: there are no insignificant emission units as a part of this permit 6. General Pollutant Emission Limiting Standards. Volatile Organic Compounds (VOC) Emissions or Organic Solvents (OS) Emissions. The permittee shall allow no person to store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The permittee shall comply with the following: Each building's fans and/or ventilation systems shall be operating whenever usage of materials containing VOC/OS's occurs and shall remain operating for at least 1 hour after the usage has been completed. The capture rate of miscellaneous other VOC/OS emissions clean-up shall not be less than 40%. Compliance with the 40% capture rate shall be considered satisfied by complying with Attachment C – Standard Operating Procedures for Clean-up Solvent Usage. NOTE – When determining the miscellaneous solvent emission rate(s), the percent of solids in the recovered solvents shall be documented and accounted for in the emission calculations. Attachment C Catalina Yachts, Morgan Division Standard Operating Procedures for Cleanup Solvent Usage The cleanup solvents at Catalina Yachts, Morgan Division are used for a variety of different operations. The solvents are used for brush and roller cleaning, spray gun cleaning, tool cleaning, and product wipe down. The following procedures will be utilized to ensure at least a 40% initial solvent capture efficiency. 1. The brushes and rollers are soaked in a closed solvent container until clean. The solvent is re-used several times until it is no longer usable as a cleaning agent. The spent solvent is then place in drums to be recycled. The approximate capture efficiency of this operation is roughly 90%. 2. The gel-coat and chopper spray guns are soaked in a closed solvent container for initially cleaning. Then some solvent is sprayed through the guns into a closed capture container. This spent solvent is also stored for recycling. The capture efficiency of this operation is around 50%. 3. Solvent is also used to clean boats prior to shipping. Solvent dampened rags and brushes are used in this cleaning process. The solvent is stored in closed safety cans during this process. The solvent capture rate of this operation is unknown, but assumed small. 4. All solvents shall be kept in closed containers. All solvent dampened rass shall be stored in closed containers. The net overall initial solvent capture rate from these operations should be at least 40% All materials containing VOC/OS's shall be stored in closed original containers and/or in small automatic closing safety cans. Clean-up solvent washings shall be directed into containers that prevent evaporation into the atmosphere. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive emissions, and spills of materials containing VOC/OS's. Work practice controls shall include limiting the amount of clean-up solvents issued to employees and employees shall use gloves whenever handling resins. Immediately attend to all spills of materials containing VOC/OS's as appropriate. [Rule 62-296.320(1)(a), F.A.C. and Construction Permit AC52-262880] from 1030223-010-AC Comments: An inspection of each work/lamination station (8 in operation during the inspection) revealed that: Based on observation, brushes and rollers are soaked in closed solvent Based on observation and interview of workers, the gel-coat and chopper spray guns are soaked in a closed solvent container Based on observation, solvent is used to clean boats prior to shipping All solvents observed, MMA, resin and gelcoat are stored in closed containers Some of the solvent materials are stored in small safety cans Spray equipment, rollers observed did not leak Mr. Quinn stated that solvent clean-up is performed with gloves Further stated, the procedure is to immediately attend to all spills based on the O&M Plan 7. Emissions of Unconfined Particulate Matter. Pursuant to Rules 62-296.320(4)(c)1., 3., & 4., F.A.C., reasonable precautions to prevent emissions of unconfined particulate matter at this facility include the following requirements (see Condition No. 57 of Appendix TV-4, Title V Conditions): A. The north wall of the grinding building shall contain a filter with the exhaust fan. B. Frequent cleanings and sweeping of floors, equipment, and finished products. C. Supervisory inspections during operation(s) to ensure that all activities are being conducted in a manner to minimize emissions. D. Application of water to paved and unpaved areas accommodating vehicular traffic, as necessary. E. Enclosure or covering of activities or equipment where necessary. As an indicator that adequate control measures/practices are adequate, visible emissions from the property line, exhaust fans, doors, and vents shall not exceed 5% opacity. If this level is exceeded, it shall not be considered a violation in and of itself, but may allow the Department to require additional controls or work practices. [Rule 62-296.320(4)(c)2., F.A.C. and AC52-262880] Comments: No unconfined emissions 9. Statement of Compliance. The annual statement of compliance pursuant to Rule 62-213.440(3)(a)2., F.A.C., shall be submitted to this office and the EPA within 60 (sixty) days after the end of the calendar year using DEP Form No. 62-213.900(7), F.A.C. [Rules 62-213.440(3) and 62-213.900, F.A.C.] {Permitting Note: This condition implements the requirements of Rules 62-213.440(3)(a)2. and 3., F.A.C. (see Condition No. 51 of Appendix TV-4, Title V Conditions)} Comments: The latest Annual Statement of Compliance was submitted on 2/23/09 Essential Potential to Emit (PTE) Parameters A.2. The permittee shall comply with the following: A. Emissions of total HAP's shall not exceed 240 tons per any consecutive 12 month period. B. Emissions of total volatile organic compounds (VOC's), which includes chemicals such as Styrene and Methyl Methacrylate, shall not exceed 240 tons per any consecutive 12 month period. [Rules 62-4.160(2) and 62-210.200(PTE), F.A.C.; 1030223-005-AC] Comments: Highest 12-mo totals HAP (Nov, 09’) = 4.73 tons/yr. Highest VOC emissions = 11.96 tons/yr. Highest MMA emissions = 0.45 tons/yr Recordkeeping and Reporting Requirements A.3. A monthly log based on the tracking of individual HAP's associated with monomer usage, total HAP's and/or VOC containing material used in association with manufacturing activities shall be kept for this facility to document compliance with the emission limitations of Condition No. A.2. Note, if any month results in total HAP's and/or total VOC's emissions being within 10% of its associated allowable emission limit as shown in Condition No. A.2., the logs required below shall be then kept daily. The daily logs shall include a cumulative total to demonstrate compliance with Condition No. A.2. At a minimum, the logs shall contain the following: A. Facility Name, Date, and Emission Unit ID (1030223 001). B. Identify and quantify each resin, coating, solvent, chemical, etc. used at the facility that contains HAP's and/or VOC's. At the permittee's option, "purchases" may be used where "usage" is specified, except when daily recordkeeping is required. If this option is utilized, no materials may be used which is not purchased. C. The total tons of each individual HAP (i.e., Styrene in monomer usage) emissions for the month. D. The total HAP emissions for the month in tons. E. The total VOC emissions for the month in tons. F. The total HAP emissions, in tons, for the most recent consecutive 12 month period. G. The total VOC emissions, in tons, for the most recent consecutive 12 month period. H. Record the method of application (where applicable) for each material used (see Table below). I. Emissions of Styrene, Methyl methacrylate (MMA), and other volatile organic compounds (VOCs) shall be determined as follows until notified by the Department or the Pinellas County Department of Environmental Management. Note, Styrene and MMA are each considered a VOC and HAP. 1. Styrene emissions shall be determined using the following equation: where: Ms = amount of styrene containing material used (in tons) EF = emission factor (lb/ton) for styrene monomer content (from table below) The applicable styrene emission factor shall be obtained (interpolated/extrapolated, if applicable) from the following table, in conjunction with the percent of available non-vapor suppressed (NVS) styrene monomer in the resin/gelcoat: % Monomer Resin** Hand (Non-Spray) Layup Resin** Mechanical Atomized Spray Layup Resin Mechanical Nonatomized* Spray Layup Gel Coat** Mechanical Atomized Spray Layup Gelcoat Mechanical Nonatomized* Spray Layup 18 39 51 39 138 67 19 41 54 41 148 70 20 43 58 43 158 79 21 45 61 45 168 88 22 48 64 47 178 97 23 50 68 49 189 106 24 52 71 51 200 115 25 55 75 54 211 124 26 57 78 56 221 133 27 59 82 58 233 142 28 62 86 60 244 151 29 64 90 62 256 160 30 67 94 64 269 169 31 69 97 66 281 178 32 71 102 68 295 187 33 74 105 71 308 196 34 77 112 74 322 205 35 80 118 77 336 214 36 83 127 80 354 223 37 86 136 83 371 232 38 90 146 86 390 241 39 92 156 89 408 250 40 95 166 93 427 259 41 98 176 96 446 268 42 100 187 99 466 278 43 112 192 102 477 287 44 117 202 105 495 296 45 122 212 108 513 305 46 127 221 111 532 314 47 133 232 115 551 323 48 138 242 118 571 332 49 143 252 121 590 341 50 148 263 124 609 350 * Nonatomized means any application technology in which the resin is not broken into droplets or an aerosol as it travels from the application equipment to the surface of the part. Nonatomized resin application technology includes, but is not limited to, flowcoaters, chopper flowcoaters, and pressure fed resin rollers. In addition, the device must be operated according to the manufacturer’s directions, including instructions to prevent the operation of the device at excessive spray pressures. ** The emission factors in these columns are based on a weighted average using the following assumptions: - Using the Unified Emission Factors - 20% by weight of the facility's usage of resins and gelcoats are for reinforced plastic composites production for items such as hatches and doors, but not for hulls and decks. - Using the National Marine Manufacturer Association's Factors – 80% by weight of the facility's usage of resins and gelcoats are for items such as decks and hulls. 2. MMA emissions shall be determined by the following equations: where: Mmma = amount of MMA containing material used (in tons) Cmma = MMA content (percent/100) 3. Other VOC emissions shall be determined by the following equation for each material. These values shall be used in conjunction with the above Styrene and MMA emissions to determine total VOC: where: Mvoc = amount of VOC containing material used (in tons) Cvoc = VOC content (percent/100) J. Each log, where applicable, shall have attached the documentation for all chemicals captured for disposal or recycle. Documentation of each chemical captured shall use a mass balance method to determine usage/emissions (amount used minus amount collected for disposal or recycle). K. When determining the VOC emissions and HAP emission rates, the percent of solids in the recovered materials shall be documented and accounted for in the emission calculations, if applicable. L. The monthly logs shall be completed by the end of the following month. Daily logs (if required) shall be completed within 3 business days. Supporting documentation (MSDS sheets, purchase orders, etc.) shall be kept for each material, which includes sufficient information to determine VOC emissions and HAP emissions. M. The total HAP and total VOC emission summary, calculations, and records used to determine emissions shall be recorded in a permanent form suitable for inspection by the Department or PCDEM upon request. N. The logs/records shall be kept at the facility for a minimum of 5 years and made available to the Department and PCDEM upon request. [Rule 62-213.440(1)(b), F.A.C.] Comments: The facility meets A-N of this condition MACT - 40 CFR 63, Subparts A and VVVV, Requirements A.4. This emission unit is subject to and shall comply with the applicable provisions* of the MACT standards of 40 CFR 63, Subparts A and VVVV (incorporated into Attachment B, which is a part of this permit). Note, these requirements are for only Open Molding Resin and Gel Coat Operations using Emissions Averaging Option and/or Compliant Materials Option. Requirements relating to add-on-control devices have been deleted, since this emission unit does not utilize add-on-control devices. Additionally, when demonstrating compliance with 40 CFR 63, Subpart VVVV, either the Emissions Averaging Option or the Compliant Materials Option may be used, but each time a compliance option is used, it must be used for a minimum of 12 consecutive months before switching to the other option. *An applicability reference table is included as an attachment to this permit (Attachment A). The table is based upon information provided in an email from Catalina Yachts, dated October 17, 2008. Therefore, any change in operations may change the applicable provisions and in some cases, may require a construction permit. [Rule 62-204.800(11)(b)59., F.A.C.] from 1030223-010-AC Comments: The facility meets the requirements of 40 CFR 62 subpart A and VVVV by demonstrating compliance using the emissions averaging option. See the latest SAMS and monthly report Attachment A- Applicability Table 40 CFR 63, Subpart VVVV National Emission Standards for Hazardous Air Pollutants for Boat Manufacturing Section Applies Y/N § 63.5680 What is the purpose of this subpart? Y § 63.5683 Does this subpart apply to me? Y § 63.5686 How do I demonstrate that my facility is not a major source? § 63.5689 What parts of my facility are covered by this subpart? The affected source (the portion of your boat manufacturing facility covered by this subpart) is the combination of all of the boat manufacturing operations listed in paragraphs (a) through (f) of this section. Y (a) Open molding resin and gel coat operations (including pigmented gel coat, clear gel coat, production resin, tooling gel coat, and tooling resin). Y (b) Closed molding resin operations. Y (c) Resin and gel coat mixing operations. Y (d) Resin and gel coat application equipment cleaning operations. Y (e) Carpet and fabric adhesive operations. Y (f) Aluminum hull and deck coating operations, including solvent wipedown operations and paint spray gun cleaning operations, on aluminum recreational boats. N § 63.5692 How do I know if my boat manufacturing facility is a new source or an existing source? Y (a) A boat manufacturing facility is a new source if it meets the criteria in paragraphs (a)(1) through (3) of this section. N (1) You commence construction of the affected source after July 14, 2000. N (2) It is a major source. N (3) It is a completely new boat manufacturing affected source where no other boat manufacturing affected source existed prior to the construction of the new source. N (b) For the purposes of this subpart, an existing source is any source that is not a new source. Y § 63.5695 When must I comply with this subpart? Y Standards for Open Molding Resin and Gel Coat Operations Y § 63.5698 What emission limit must I meet for open molding resin and gel coat operations? Y (a) You must limit organic HAP emissions from the five open molding operations listed in paragraphs (a)(1) through (5) of this section to the emission limit specified in paragraph (b) of this section. Operations listed in paragraph (d) are exempt from this limit. Y (1) Production resin. Y (2) Pigmented gel coat. Y (3) Clear gel coat. Y (4) Tooling resin. Y (5) Tooling gel coat. Y (b) You must limit organic HAP emissions from open molding operations to the limit specified by equation 1 of this section, based on a 12-month rolling average. Y (c) The open molding emission limit is the same for both new and existing sources. Y (d) The materials specified in paragraphs (d)(1) through (3) of this section are exempt from the open molding emission limit specified in paragraph (b) of this section. Y (1) Production resins (including skin coat resins) that must meet specifications for use in military vessels or must be approved by the U.S. Coast Guard for use in the construction of lifeboats, rescue boats, and other life-saving appliances approved under 46 CFR subchapter Q or the construction of small passenger vessels regulated by 46 CFR subchapter T. Production resins for which this exemption is used must be applied with nonatomizing (non-spray) resin application equipment. You must keep a record of the resins for which you are using this exemption. N (2) Pigmented, clear, and tooling gel coat used for part or mold repair and touch up. The total gel coat materials included in this exemption must not exceed 1 percent by weight of all gel coat used at your facility on a 12-month rolling-average basis. You must keep a record of the amount of gel coats used per month for which you are using this exemption and copies of calculations showing that the exempt amount does not exceed 1 percent of all gel coat used. Y applicable but the source does not utilize this exemption (3) Pure, 100 percent vinylester resin used for skin coats. This exemption does not apply to blends of vinylester and polyester resins used for skin coats. The total resin materials included in the exemption cannot exceed 5 percent by weight of all resin used at your facility on a 12-month rolling-average basis. You must keep a record of the amount of 100 percent vinylester skin coat resin used per month that is eligible for this exemption and copies of calculations showing that the exempt amount does not exceed 5 percent of all resin used. Y applicable but the source does not utilize this exemption § 63.5701 What are my options for complying with the open molding emission limit? You must use one or more of the options listed in paragraphs (a) through (c) of this section to meet the emission limit in §63.5698 for the resins and gel coats used in open molding operations at your facility. Y (a) Maximum achievable control technology (MACT) model point value averaging (emissions averaging) option. (1) Demonstrate that emissions from the open molding resin and gel coat operations that you average meet the emission limit in §63.5698 using the procedures described in §63.5710. Compliance with this option is based on a 12-month rolling average. Y (2) Those operations and materials not included in the emissions average must comply with either paragraph (b) or (c) of this section. N (b) Compliant materials option. Demonstrate compliance by using resins and gel coats that meet the organic HAP content requirements in Table 2 to this subpart. Compliance with this option is based on a 12-month rolling average. N (c) Add-on control option. Use an enclosure and add-on control device, and demonstrate that the resulting emissions meet the emission limit in §63.5698. Compliance with this option is based on control device performance testing and control device monitoring. N § 63.5704 What are the general requirements for complying with the open molding emission limit? Y (a) Emissions averaging option. For those open molding operations and materials complying using the emissions averaging option, you must demonstrate compliance by performing the steps in paragraphs (a)(1) through (5) of this section. Y (1) Use the methods specified in §63.5758 to determine the organic HAP content of resins and gel coats. Y (2) Complete the calculations described in §63.5710 to show that the organic HAP emissions do not exceed the limit specified in §63.5698. Y (3) Keep records as specified in paragraphs (a)(3)(i) through (iv) of this section for each resin and gel coat. Y (i) Hazardous air pollutant content. Y (ii) Amount of material used per month. Y (iii) Application method used for production resin and tooling resin. This record is not required if all production resins and tooling resins are applied with nonatomized technology. Y (iv) Calculations performed to demonstrate compliance based on MACT model point values, as described in §63.5710. Y (4) Prepare and submit the implementation plan described in §63.5707 to the Administrator and keep it up to date. Y (5) Submit semiannual compliance reports to the Administrator as specified in §63.5764. Y (b) Compliant materials option. For each open molding operation complying using the compliant materials option, you must demonstrate compliance by performing the steps in paragraphs (b)(1) through (4) of this section. N (1) Use the methods specified in §63.5758 to determine the organic HAP content of resins and gel coats. N (2) Complete the calculations described in §63.5713 to show that the weighted-average organic HAP content does not exceed the limit specified in Table 2 to this subpart. N (3) Keep records as specified in paragraphs (b)(3)(i) through (iv) of this section for each resin and gel coat. N (i) Hazardous air pollutant content. N (ii) Application method for production resin and tooling resin. This record is not required if all production resins and tooling resins are applied with nonatomized technology. N (iii) Amount of material used per month. This record is not required for an operation if all materials used for that operation comply with the organic HAP content requirements. N (iv) Calculations performed, if required, to demonstrate compliance based on weighted-average organic HAP content as described in §63.5713. N (4) Submit semiannual compliance reports to the Administrator as specified in §63.5764. N (c) Add-on control option. If you are using an add-on control device, you must demonstrate compliance by performing the steps in paragraphs (c)(1) through (5) of this section. N (1) Conduct a performance test of the control device as specified in §§63.5719 and 63.5722 to demonstrate initial compliance. N (2) Use the performance test results to determine control device parameters to monitor after the performance test as specified in §63.5725. N (3) Comply with the operating limits specified in §63.5715 and the control device and emission capture system monitoring requirements specified in §63.5725 to demonstrate continuous compliance. N (4) Keep the records specified in §63.5767. N (5) Submit to the Administrator the notifications and reports specified in §§63.5761 and 63.5764. N § 63.5707 What is an implementation plan for open molding operations and when do I need to prepare one? Y (a) You must prepare an implementation plan for all open molding operations for which you comply by using the emissions averaging option described in §63.5704(a). Y (b) The implementation plan must describe the steps you will take to bring the open molding operations covered by this subpart into compliance. For each operation included in the emissions average, your implementation plan must include the elements listed in paragraphs (b)(1) through (3) of this section. Y (1) A description of each operation included in the average. Y (2) The maximum organic HAP content of the materials used, the application method used (if any atomized resin application methods are used in the average), and any other methods used to control emissions. Y (3) Calculations showing that the operations covered by the plan will comply with the open molding emission limit specified in §63.5698. Y (c) You must submit the implementation plan to the Administrator with the notification of compliance status specified in §63.5761. Y (d) You must keep the implementation plan on site and provide it to the Administrator when asked. Y (e) If you revise the implementation plan, you must submit the revised plan with your next semiannual compliance report specified in §63.5764. Y § 63.5710 How do I demonstrate compliance using emissions averaging? Y (a) Compliance using the emissions averaging option is demonstrated on a 12-month rolling-average basis and is determined at the end of every month (12 times per year). The first 12-month rolling-average period begins on the compliance date specified in §63.5695. Y (b) At the end of the twelfth month after your compliance date and at the end of every subsequent month, use equation 1 of this section to demonstrate that the organic HAP emissions from those operations included in the average do not exceed the emission limit in §63.5698 calculated for the same 12-month period. (Include terms in equation 1 of §63.5698 and equation 1 of this section for only those operations and materials included in the average.) Y (c) At the end of every month, use equation 2 of this section to compute the weighted-average MACT model point value for each open molding resin and gel coat operation included in the average. Y § 63.5713 How do I demonstrate compliance using compliant materials? N § 63.5714 How do I demonstrate compliance if I use filled resins? N § 63.5715 Demonstrating Compliance for Open Molding Operations Controlled by Add-On Control Devices N § 63.5716 When must I conduct a performance test? N § 63.5719 How do I conduct a performance test? N § 63.5722 How do I use the performance test data to demonstrate initial compliance? N § 63.5725 What are the requirements for monitoring and demonstrating continuous compliance? N Standards for Closed Molding Resin Operations Y § 63.5728 What standards must I meet for closed molding resin operations? Standards for Resin and Gel Coat Mixing Operations Y § 63.5731 What standards must I meet for resin and gel coat mixing operations? (a) All resin and gel coat mixing containers with a capacity equal to or greater than 208 liters, including those used for on-site mixing of putties and polyputties, must have a cover with no visible gaps in place at all times. Y (b) The work practice standard in paragraph (a) of this section does not apply when material is being manually added to or removed from a container, or when mixing or pumping equipment is being placed in or removed from a container. Y (c) To demonstrate compliance with the work practice standard in paragraph (a) of this section, you must visually inspect all mixing containers subject to this standard at least once per month. The inspection should ensure that all containers have covers with no visible gaps between the cover and the container, or between the cover and equipment passing through the cover. Y (d) You must keep records of which mixing containers are subject to this standard and the results of the inspections, including a description of any repairs or corrective actions taken. Y Standards for Resin and Gel Coat Application Equipment Cleaning Operations Y § 63.5734 What standards must I meet for resin and gel coat application equipment cleaning operations? (a) For routine flushing of resin and gel coat application equipment (e.g., spray guns, flowcoaters, brushes, rollers, and squeegees), you must use a cleaning solvent that contains no more than 5 percent organic HAP by weight. For removing cured resin or gel coat from application equipment, no organic HAP content limit applies. Y (b) You must store organic HAP-containing solvents used for removing cured resin or gel coat in containers with covers. The covers must have no visible gaps and must be in place at all times, except when equipment to be cleaned is placed in or removed from the container. On containers with a capacity greater than 7.6 liters, the distance from the top of the container to the solvent surface must be no less than 0.75 times the diameter of the container. Containers that store organic HAP-containing solvents used for removing cured resin or gel coat are exempt from the requirements of 40 CFR part 63, subpart T. Cured resin or gel coat means resin or gel coat that has changed from a liquid to a solid. Y § 63.5737 How do I demonstrate compliance with the resin and gel coat application equipment cleaning standards? Y (a) Determine and record the organic HAP content of the cleaning solvents subject to the standards specified in §63.5734 using the methods specified in §63.5758. Y (b) If you recycle cleaning solvents on site, you may use documentation from the solvent manufacturer or supplier or a measurement of the organic HAP content of the cleaning solvent as originally obtained from the solvent supplier for demonstrating compliance, subject to the conditions in §63.5758 for demonstrating compliance with organic HAP content limits. Y (c) At least once per month, you must visually inspect any containers holding organic HAP-containing solvents used for removing cured resin and gel coat to ensure that the containers have covers with no visible gaps. Keep records of the monthly inspections and any repairs made to the covers. Y Standards for Carpet and Fabric Adhesive Operations Y § 63.5740 What emission limit must I meet for carpet and fabric adhesive operations? Standards for Aluminum Recreational Boat Surface Coating Operations N § 63.5743 What standards must I meet for aluminum recreational boat surface coating operations? § 63.5746 How do I demonstrate compliance with the emission limits for aluminum wipedown solvents and aluminum coatings? N § 63.5749 How do I calculate the organic HAP content of aluminum wipedown solvents? N § 63.5752 How do I calculate the organic HAP content of aluminum recreational boat surface coatings? N § 63.5753 How do I calculate the combined organic HAP content of aluminum wipedown solvents and aluminum recreational boat surface coatings? N § 63.5755 How do I demonstrate compliance with the aluminum recreational boat surface coating spray gun cleaning work practice standards? N § 63.5758 Methods for Determining Hazardous Air Pollutant Content How do I determine the organic HAP content of materials? Y (a) Determine the organic HAP content for each material used. To determine the organic HAP content for each material used in your open molding resin and gel coat operations, carpet and fabric adhesive operations, or aluminum recreational boat surface coating operations, you must use one of the options in paragraphs (a)(1) through (6) of this section. Y (1) Method 311 (appendix A to 40 CFR part 63). You may use Method 311 for determining the mass fraction of organic HAP. Use the procedures specified in paragraphs (a)(1)(i) and (ii) of this section when determining organic HAP content by Method 311. N (i) Include in the organic HAP total each organic HAP that is measured to be present at 0.1 percent by mass or more for Occupational Safety and Health Administration (OSHA)-defined carcinogens as specified in 29 CFR 1910.1200(d)(4) and at 1.0 percent by mass or more for other compounds. For example, if toluene (not an OSHA carcinogen) is measured to be 0.5 percent of the material by mass, you do not need to include it in the organic HAP total. Express the mass fraction of each organic HAP you measure as a value truncated to four places after the decimal point (for example, 0.1234). N (ii) Calculate the total organic HAP content in the test material by adding up the individual organic HAP contents and truncating the result to three places after the decimal point (for example, 0.123). N (2) Method 24 (appendix A to 40 CFR part 60). You may use Method 24 to determine the mass fraction of non-aqueous volatile matter of aluminum coatings and use that value as a substitute for mass fraction of organic HAP. N (3) ASTM D1259–85 (Standard Test Method for Nonvolatile Content of Resins). You may use ASTM D1259–85 (available for purchase from ASTM) to measure the mass fraction of volatile matter of resins and gel coats for open molding operations and use that value as a substitute for mass fraction of organic HAP. N (4) Alternative method. You may use an alternative test method for determining mass fraction of organic HAP if you obtain prior approval by the Administrator. You must follow the procedure in §63.7(f) to submit an alternative test method for approval. N (5) Information from the supplier or manufacturer of the material. You may rely on information other than that generated by the test methods specified in paragraphs (a)(1) through (4) of this section, such as manufacturer's formulation data, according to paragraphs (a)(5)(i) through (iii) of this section. Y (i) Include in the organic HAP total each organic HAP that is present at 0.1 percent by mass or more for OSHA-defined carcinogens as specified in 29 CFR 1910.1200(d)(4) and at 1.0 percent by mass or more for other compounds. For example, if toluene (not an OSHA carcinogen) is 0.5 percent of the material by mass, you do not have to include it in the organic HAP total. Y (ii) If the organic HAP content is provided by the material supplier or manufacturer as a range, then you must use the upper limit of the range for determining compliance. If a separate measurement of the total organic HAP content using the methods specified in paragraphs (a)(1) through (4) of this section exceeds the upper limit of the range of the total organic HAP content provided by the material supplier or manufacturer, then you must use the measured organic HAP content to determine compliance. Y (iii) If the organic HAP content is provided as a single value, you may assume the value is a manufacturing target value and actual organic HAP content may vary from the target value. If a separate measurement of the total organic HAP content using the methods specified in paragraphs (a)(1) through (4) of this section is less than 2 percentage points higher than the value for total organic HAP content provided by the material supplier or manufacturer, then you may use the provided value to demonstrate compliance. If the measured total organic HAP content exceeds the provided value by 2 percentage points or more, then you must use the measured organic HAP content to determine compliance. Y (6) Solvent blends. Solvent blends may be listed as single components for some regulated materials in certifications provided by manufacturers or suppliers. Solvent blends may contain organic HAP which must be counted toward the total organic HAP content of the materials. When detailed organic HAP content data for solvent blends are not available, you may use the values for organic HAP content that are listed in Table 5 or 6 to this subpart. You may use Table 6 to this subpart only if the solvent blends in the materials you use do not match any of the solvent blends in Table 5 to this subpart and you know only whether the blend is either aliphatic or aromatic. However, if test results indicate higher values than those listed in Table 5 or 6 to this subpart, then the test results must be used for determining compliance. Y (b) Determine the volume fraction solids in aluminum recreational boat surface coatings. To determine the volume fraction of coating solids (liters of coating solids per liter of coating) for each aluminum recreational boat surface coating, you must use one of the methods specified in paragraphs (b)(1) through (3) of this section. If the results obtained with paragraphs (b)(2) or (3) of this section do not to agree with those obtained according to paragraph (b)(1) of this section, you must use the results obtained with paragraph (b)(1) of this section to determine compliance. N (c) Determine the density of each aluminum recreational boat wipedown solvent and surface coating. Determine the density of all aluminum recreational boat wipedown solvents, surface coatings, thinners, and other additives from test results using ASTM Method D1475–90, information from the supplier or manufacturer of the material, or reference sources providing density or specific gravity data for pure materials. If there is disagreement between ASTM Method D1475–90 test results and other information sources, you must use the test results to demonstrate compliance. N Notifications, Reports, and Records Y § 63.5761 What notifications must I submit and when? Y (a) You must submit all of the notifications in Table 7 to this subpart that apply to you by the dates in the table. The notifications are described more fully in 40 CFR part 63, subpart A, General Provisions, referenced in Table 8 to this subpart. Y (b) If you change any information submitted in any notification, you must submit the changes in writing to the Administrator within 15 calendar days after the change. Y § 63.5764 What reports must I submit and when? Y (a) You must submit the applicable reports specified in paragraphs (b) through (e) of this section. To the extent possible, you must organize each report according to the operations covered by this subpart and the compliance procedure followed for that operation. Y (b) Unless the Administrator has approved a different schedule for submission of reports under §63.10(a), you must submit each report by the dates in paragraphs (b)(1) through (5) of this section. Y (1) If your source is not controlled by an add-on control device (i.e., you are complying with organic HAP content limits, application equipment requirements, or MACT model point value averaging provisions), the first compliance report must cover the period beginning 12 months after the compliance date specified for your source in §63.5695 and ending on June 30 or December 31, whichever date is the first date following the end of the first 12-month period after the compliance date that is specified for your source in §63.5695. If your source is controlled by an add-on control device, the first compliance report must cover the period beginning on the compliance date specified for your source in §63.5695 and ending on June 30 or December 31, whichever date is the first date following the end of the first calendar half after the compliance date that is specified for your source in §63.5695. Y (2) The first compliance report must be postmarked or delivered no later than 60 calendar days after the end of the compliance reporting period specified in paragraph (b)(1) of this section. Y (3) Each subsequent compliance report must cover the applicable semiannual reporting period from January 1 through June 30 or from July 1 through December 31. Y (4) Each subsequent compliance report must be postmarked or delivered no later than 60 calendar days after the end of the semiannual reporting period. Y (5) For each affected source that is subject to permitting regulations pursuant to 40 CFR part 70 or 71, and if the permitting authority has established dates for submitting semiannual reports pursuant to 40 CFR 70.6(a)(3)(iii)(A) or 40 CFR 71.6(a)(3)(iii)(A), you may submit the first and subsequent compliance reports according to the dates the permitting authority has established instead of according to the dates in paragraphs (b)(1) through (4) of this section. Y (c) The compliance report must include the information specified in paragraphs (c)(1) through (7) of this section. Y (1) Company name and address. Y (2) A statement by a responsible official with that official's name, title, and signature, certifying the truth, accuracy, and completeness of the report. Y (3) The date of the report and the beginning and ending dates of the reporting period. Y (4) A description of any changes in the manufacturing process since the last compliance report. Y (5) A statement or table showing, for each regulated operation, the applicable organic HAP content limit, application equipment requirement, or MACT model point value averaging provision with which you are complying. The statement or table must also show the actual weighted-average organic HAP content or weighted-average MACT model point value (if applicable) for each operation during each of the rolling 12-month averaging periods that end during the reporting period. Y (6) If you were in compliance with the emission limits and work practice standards during the reporting period, you must include a statement to that effect. Y (7) If you deviated from an emission limit or work practice standard during the reporting period, you must also include the information listed in paragraphs (c)(7)(i) through (iv) of this section in the semiannual compliance report. Y (i) A description of the operation involved in the deviation. Y (ii) The quantity, organic HAP content, and application method (if relevant) of the materials involved in the deviation. Y (iii) A description of any corrective action you took to minimize the deviation and actions you have taken to prevent it from happening again. Y (iv) A statement of whether or not your facility was in compliance for the 12-month averaging period that ended at the end of the reporting period. Y (d) If your facility has an add-on control device, you must submit semiannual compliance reports and quarterly excess emission reports as specified in §63.10(e). The contents of the reports are specified in §63.10(e). N (e) If your facility has an add-on control device, you must complete a startup, shutdown, and malfunction plan as specified in §63.6(e), and you must submit the startup, shutdown, and malfunction reports specified in §63.10(e)(5). N § 63.5767 What records must I keep? Y You must keep the records specified in paragraphs (a) through (d) of this section in addition to records specified in individual sections of this subpart. Y (a) You must keep a copy of each notification and report that you submitted to comply with this subpart. Y (b) You must keep all documentation supporting any notification or report that you submitted. Y (c) If your facility is not controlled by an add-on control device (i.e., you are complying with organic HAP content limits, application equipment requirements, or MACT model point value averaging provisions), you must keep the records specified in paragraphs (c)(1) through (3) of this section. Y (d) If your facility has an add-on control device, you must keep the records specified in §63.10(b) relative to control device startup, shut down, and malfunction events; control device performance tests; and continuous monitoring system performance evaluations. N § 63.5770 In what form and for how long must I keep my records? Y (a) Your records must be readily available and in a form so they can be easily inspected and reviewed. Y (b) You must keep each record for 5 years following the date that each record is generated. Y (c) You must keep each record on site for at least 2 years after the date that each record is generated. You can keep the records offsite for the remaining 3 years. Y (d) You can keep the records on paper or an alternative media, such as microfilm, computer, computer disks, magnetic tapes, or on microfiche. Y Other Information You Need To Know Y § 63.5773 What parts of the General Provisions apply to me? Y You must comply with the requirements of the General Provisions in 40 CFR part 63, subpart A, as specified in Table 8 to this subpart. Y § 63.5776 Who implements and enforces this subpart? Y (a) If the Administrator has delegated authority to your State or local agency, the State or local agency has the authority to implement and enforce this subpart. Y (b) In delegating implementation and enforcement authority of this subpart to a State or local agency under 40 CFR part 63, subpart E, the authorities that are retained by the Administrator of the U.S. EPA and are not transferred to the State or local agency are listed in paragraphs (b)(1) through (4) of this section. Y (1) Under §63.6(g), the authority to approve alternatives to the standards listed in paragraphs (b)(1)(i) through (vii) of this section is not delegated. Y (i) §63.5698—Emission limit for open molding resin and gel coat operations. Y (ii) §63.5728—Standards for closed molding resin operations. Y (iii) §63.5731(a)—Standards for resin and gel coat mixing operations. Y (iv) §63.5734—Standards for resin and gel coat application equipment cleaning operations. Y (v) §63.5740(a)—Emission limit for carpet and fabric adhesive operations. Y (vi) §63.5743—Standards for aluminum recreational boat surface coating operations. Y (vii) §63.5746(g)—Approval of alternative means of demonstrating compliance with the emission limits for aluminum recreational boat surface coating operations. Y (2) Under §63.7(e)(2)(ii) and (f), the authority to approve alternatives to the test methods listed in paragraphs (b)(2)(i) through (iv) of this section is not delegated. N (i) §63.5719(b)—Method for determining whether an enclosure is a total enclosure. N (ii) §63.5719(c)—Methods for measuring emissions from a control device. N (iii) §63.5725(d)(1)—Performance specifications for thermal oxidizer combustion temperature monitors. N (iv) §63.5758—Method for determining hazardous air pollutant content of regulated materials. Y (3) Under §63.8(f), the authority to approve major alternatives to the monitoring requirements listed in §63.5725 is not delegated. A “major alternative” is defined in §63.90. N (4) Under §63.10(f), the authority to approve major alternatives to the reporting and recordkeeping requirements listed in §§63.5764, 63.5767, and 63.5770 is not delegated. A “major alternative” is defined in §63.90. N |
| ( |  |  | Valid Permit [Rule 62-210.300] |
|  |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No Comments: |

| ( | C. Other: |
| --- | --- |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No lower emissions due to lower production 2009 – Highest 12-mo totals HAP (Nov, 09’) = 4,73 tons/yr Highest VOC emissions = 11.96 tons/yr, Highest MMA emissions = 0.45 tons/yr 2008 – 12 mo consecutive total Styrene =13.11 tons/yr, total HAP = 13.14 tons/yr, MMA = 0.03 tons/yr, VOC = 26.33 tons/yr Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: Comments: |
| Closing Conference: RTM vacuum technology starts April, 10. The facility will test out on small parts. |
| Inspector(s): Jeffrey Morris, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: |
| ACCESS? | ( | ARMS? | ( |

| AIRS ID 1030223 | OWNER Catalina Yachts, Morgan Division | FACILITY NAME |
| --- | --- | --- |
| TITLE V | SYNTHETIC MINOR | DATE OF THIS FCE March 9, 2010 |
| TITLE V MEGA-SITE* | OTHER | DATE OF LAST FCE |

*Facility with a large number of complex emissions units.  It is more reasonable to evaluate a Title V Mega-Site once every 3 years instead of once every 2 years.

Review of All Required Reports

| PERIODIC REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Annual operating report | Received 3/15/09 Reviewed 4/15/09 |
| DONE N/A | Statement of compliance | 09’ SOCR reviewed 4/30/09 |
| DONE N/A | Annual |  |
| DONE N/A | Semi-annual | Reviewed 9/15/09 |
| DONE N/A | Quarterly |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

| CONTINUOUS EMISSION MONITOR REPORTS | COMMENTS |
| --- | --- |
| DONE N/A | Quarterly excess emissions |  |
| DONE N/A | Semi-annual |  |
| DONE N/A | RATA |  |
| DONE N/A | CGA |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Assessment of Control Device and Process Operating Conditions

| OFF-SITE ASSESSMENT | (Describe the off-site assessment in comments) |
| --- | --- |
| ON-SITE ASSESSMENT | (Document the on-site inspection below) |
| DATE OF INSPECTION | DATE OF INSPECTION REPORT | My office maintains the inspection report... |
|  |  | ...in the ARMS database through EASIIR. | ...with the paper or electronic compliance files | ...in another location (specify). |
| 2/8/10 | 3/9/10 |  |  |  |
| COMMENTS |

Review of Tests and Records

| TESTS, OBSERVATIONS AND RECORDS | COMMENTS |
| --- | --- |
| DONE N/A | Visible emission observation(s) |  |
| DONE N/A | Review of facility records and logs | Copy of the monthly totals (Nov, 09’) |
| DONE N/A | Assessment of process parameters (feed rates, process rates, raw material compositions, etc.) | Usage rate of resins and gel coat supplied |
| DONE N/A | Assessment of control equipment performance parameters (water flow rates, pressure drops, temperatures, ESP power levels, etc.) |  |
| DONE N/A | Stack test(s) |  |
| DONE N/A | Other : |  |
| DONE N/A | Other : |  |

Compliance Monitoring (CM) Information

| CM ELEMENT | My office maintains this information... |
| --- | --- |
|  | ...electronically, in the ARMS database. | ...in the permit. | ...in the inspection report. | ...in another location (specify). |
| Facility information |  |  |  |  |
| Applicable requirements |  |  |  |  |
| Inventory of emission units |  |  |  |  |
| Enforcement history |  |  |  |  |
| Compliance activities |  |  |  |  |
| Findings and recommendations |  |  |  |  |
| COMMENTS |

Other Comments

Prepared by:	   Jeffrey Morris		Date:

Reviewed by:			Date:

1.  Complete the form as much as possible during for inspection; 2.  The remainder of checklist, for activities in the FY, are filled in no later than 9/15;  3.  Between 9/15 and 9/30, complete the FCE by closing out the FCS project in ARMS.  The INSP > FCS record only accepts a completion date and a comment; it does not accept information on the lower portion of the form.  If an FCS project already exists for the fiscal year in question, enter a completion date and comment in the existing record, do not create a duplicate FCS record.