| 1030534 84744 |  |
| --- | --- |
| FACILITY: Tampa Yacht Manufacturing, LLC | PERMIT ID: 2867 |
|  | DISTRICT: Southwest |
| ADDRESS: 4350 62nd Avenue North | CONTACT PHONE: |
| Pinellas Park, FL | 727-954-3435 |
| ARMS NO: 1030534 001 | PERMIT NO: | Expiration Date: 1/8/2015 Renewal Date: 11/9/2014 |
|  | 1030534-002-AO |  |
|  |  | Test Due Date: |
| EMISSION UNIT DESCRIPTION : Fiberglass Boat Manufacturer |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
|  | March 27, 2013 |  |  | INS1 | ( | INS2 |  | INS3 |  | FUI | ( | IN |  | MNC |  | SNC |
| INSPECTION TYPE: | ( | Initial |  | Re-inspection |  | Complaint |  | Drive-by |  | Quarterly |
| ( | A. General Review: |
| 1. | Permit File Review |  | Yes |  | No |
|  | Comments: YES |  |  |  |  |
| 2. | Introduction and Entry |  | Yes |  | No |
|  | Comments: I met with Mr. Robert Stevens and Mr. Robert Brown |  |  |  |  |
| 3. | Is the Responsible Official/Authorized Representative still: Robert Stevens? |  | Yes |  | No |
|  | Comments: YES The Responsible Official/Authorized Representative’s e-mail is: robert.stevens@tampa-yacht.com |
| 4. | Is the facility contact still: Robert Brown? |  | Yes |  | No |
|  | Comments: YES The facility contact’s e-mail is: bob.brown@tampa-yacht.com |

| IN | MNC | SNC | B. Specific Conditions: |
| --- | --- | --- | --- |
| ( ( ( ( ( ( ( ( ( ( ( ( ( ( ( |  |  | Permit History/Affected Permits Inspection note: This is the initial operation permit, replacing construction permit 1030534-001-AC. This facility is considered a synthetic minor source General Conditions [62-4.160, F.A.C.] 12. This permit or a copy thereof shall be kept at the work site of the permitted activity. Comments: A copy of the permit was was not kept at the worksite. Mr. Brown maintains the permit copy in his office 8. If, for any reason, the permittee does not comply with or will be unable to comply with any condition or limitation specified in this permit, the permittee shall immediately provide the Department with the following information: A description of and cause of noncompliance; and The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result and may be subject to enforcement action by the Department for penalties or for revocation of this permit. Comments: The facility had no non compliance issues are exceedances of permit limitations. Common Conditions [Rule 62-296.320(4)(c), F.A.C.] Unless otherwise specified in the permit, the following conditions apply to all emissions units and activities at the facility. Emissions and Controls 2. Circumvention: The permittee shall not circumvent the air pollution control equipment or allow the emission of air pollutants without this equipment operating properly. [Rule 62-210.650, F.A.C.] Comments: There are no control devices associated with this source. 6. VOC or OS Emissions: No person shall store, pump, handle, process, load, unload or use in any process or installation, volatile organic compounds (VOC) or organic solvents (OS) without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. [Rule 62-296.320(1), F.A.C.] Comments: The facility maintains clean work spaces and closed containers. There were no spills observed acetone is maintained in closed drum. 7. Objectionable Odor Prohibited: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An “objectionable odor” means any odor present in the outdoor atmosphere which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-296.320(2) and 62-210.200(Definitions), F.A.C.] Comments: There was no styrene or objectionable odors outside the building. The indoor work area had a moderate styrene odor in the laminations area, during lamination processing of boat mold. (see photos). 9. Unconfined Particulate Emissions: No person shall cause, let, permit, suffer or allow the emissions of unconfined particulate matter from any activity, including vehicular movement; transportation of materials; construction, alteration, demolition or wrecking; or industrially related activities such as loading, unloading, storing or handling; without taking reasonable precautions to prevent such emissions. Any permit issued to a facility with emissions of unconfined particulate matter shall specify the reasonable precautions to be taken by that facility to control the emissions of unconfined particulate matter. Reasonable precautions include the following: Paving and maintenance of roads, parking areas and yards. Application of water or chemicals to control emissions from such activities as demolition of buildings, grading roads, construction, and land clearing. Application of asphalt, water, oil, chemicals or other dust suppressants to unpaved roads, yards, open stock piles and similar activities. Removal of particulate matter from roads and other paved areas under the control of the owner or operator of the facility to prevent reentrainment, and from buildings or work areas to prevent particulate from becoming airborne. Landscaping or planting of vegetation. Use of hoods, fans, filters, and similar equipment to contain, capture and/or vent particulate matter. Confining abrasive blasting where possible. Enclosure or covering of conveyor systems. Comments: There were no unconfined emissions at this time, the work areas were clean. No work is performed outside the building area. The clean sweeping is performed at least once a week Administrative Requirements 7 Annual Operating Report: On or before April 1 of each year, the permittee shall submit a completed DEP Form 62-210.900(5), "Annual Operating Report for Air Pollutant Emitting Facility" (AOR) for the preceding calendar year. The report may be submitted electronically in accordance with the instructions received with the AOR package sent by the Department, or a hardcopy may be sent to the Compliance Authority. [Rule 62-210.370(3), F.A.C.] Comments: The annual operating report for calendar year 201 2 was submitted on 3/13/13. 8 Operation Permit Renewal Application: A completed application for renewal of the operation permit shall be submitted to the Permitting Authority with a copy to PCDEM (Compliance Authority) no later than 60 days prior to the expiration date of the operation permit. [Rules 62-4.030, 62-4.050, 62-4.070(3), 62-4.090, 62-210.300(2), and 62-210.900, F.A.C.] Comments: The permit expires on 1/8/2015 An application is required to be submitted no later than 11/9/2014 ________ Specific Conditions A.2. Styrene Emissions Standard: Styrene emissions from the emissions unit shall not exceed 9.5 tons per any consecutive 12-month period. [Construction Permit 1030534-001-AC; Rule 62-210.200, F.A.C. – Definitions (PTE)] A.3. VOC Emissions Standard: VOC emissions from the emissions unit shall not exceed 24 tons per any consecutive 12-month period. {Permitting Note: All HAPs contained in the raw materials are VOCs; therefore, limiting VOC emission will also limit the total HAP emissions.} [Construction Permit 1030534-001-AC; Rule 62-210.200, F.A.C. – Definitions (PTE)] Comments: The highest reported 12-month period emissions were 1.67 tons VOC, and 1.03 tons Styrene, and total H APS 1.22 tons_ for the months of January 2012. Records were reviewed for the months of _ January 2012 through _ January 2013 . These rates are low and reduced up to January 2013, as the facility has not received any new contracts at this time. The facility had only one boat in manufacturing process, These rates are in compliance and do not exceed the permit limitations. Emissions and Controls A.4. Fugitive Organic Solvents, and Volatile Organic Compounds: The permittee shall not store, pump, handle, process, load, unload, or use in any process or installation, OS, or VOCs without applying known and existing vapor emission control devices or systems deemed necessary and ordered by the Department. The permittee shall comply with the following: All materials containing VOC/OS shall be stored closed containers and/or in small automatic closing safety cans. Clean-up solvent washings shall be directed into containers that prevent evaporation into the atmosphere. All equipment, pipes, hoses, lids, fittings, etc., shall be operated/maintained in such a manner as to minimize leaks, fugitive VOC/OS emissions and spills of materials containing VOC/OS. Immediately attend to all spills of materials containing VOC/OS as appropriate. [Construction Permit 1030534-001-AC; Rules 62-4.070(3) and 62-296.320(1), FAC] Comments: The facility was maintaining clean work spaces, closed containers, were located on benches there were no spills observed. There were no leaks from resin containers and equipment. A.5. Unconfined Particulates: All reasonable precautions shall be taken to prevent and control generation of unconfined emissions of particulate matter in accordance with the provisions in Rule 62-296.320, F.A.C. These provisions are applicable to any source, including but not limited to, vehicular movement, transportation of materials, construction, alteration, demolition or wrecking, or industrial related activities such as loading, unloading, storing and handling. Reasonable precautions to prevent emissions of unconfined particulate matter from trimming and other similar activities such as: cutting, shaping, and sanding operations performed by hand tools and tabletop equipment shall, in general, be controlled by portable "shop-vac" vacuum collectors and normal "good housekeeping" procedures. [Construction Permit 1030534-001-AC; Rules 62-4.070(3) and 62-296.320(4)(c), F.A.C.] Comments: There were no unconfined emissions occurring, no particulate accumulation in work areas or in floors, there was no activities located adjacent to doors , no accumulation of materials and no tracking of particulate outside the building. A.6. Visible Emission Indicator: As an indicator that the precautions to control unconfined particulate emission are adequate, visible emissions from the facility should not exceed five percent (5%) opacity. If this value is exceeded it will not be considered a violation in and of itself, but may be a violation of the precautions stated above and serve as justification to the Department to require additional controls or work practices. [Construction Permit 1030534-001-AC; Rule 62-4.070(3), F.A.C.] Comments: There were no visible emissions occurring during the tour and observations of the facility building and working areas. The operations which are well within the building were not generating emissions from work activities. A.7. Objectionable Odor: No person shall cause, suffer, allow or permit the discharge of air pollutants, which cause or contribute to an objectionable odor. An objectionable odor is any odor present in the outdoor atmosphere, which by itself or in combination with other odors, is or may be harmful or injurious to human health or welfare, which unreasonably interferes with the comfortable use and enjoyment of life or property, or which creates a nuisance. [Rules 62-210.200 (Definition “Objectionable Odor”) and 62-296.320(2), F.A.C.; Pinellas Co. Code, Sec. 58-178] Comments: There were no styrene or objectionable odors outside the building off the property. The indoor work area had a moderate styrene odor in the laminations area, as the employees were in process of applying the glass and resin to a boat mold. I observed the air handlers to be in operation drawing air to stack which vents ~ 40 foot off ground. A.8. VOC/Styrene Recordkeeping: To document compliance with Specific Condition Nos. A.2. and A.3., the permittee shall maintain a monthly log tracking the usage and associated emissions of styrene and VOC containing materials used in the manufacturing process. Additionally, if any monthly result for either styrene and/or VOC emissions is within 10% of its permitted emissions limit, then daily logs shall be maintained during the following month. At a minimum, the logs shall contain the following: Facility Name, Facility Number (1030534), Emission Unit ID No. (001), Month, Year. For each type of raw material (resin, coating, solvent, chemical, etc.) used at the facility that contains Styrene and/or VOC, record the following: The type of raw material (e.g., resin) and material identification or description; The quantity (in pounds or tons) of materials used (where usage may be determined based upon the beginning and ending inventory and receipt of materials); The styrene and VOC content; The “method of application” where applicable and the emission factor (see Specific Condition No. A.9.). For the emission unit: The total quantity (in tons) of styrene emissions for the month; The total quantity (in tons) of VOC emissions (including Styrene) for the month; The total quantity (in tons) of Styrene emissions for the most recent consecutive 12 month period; The total quantity of (in tons) of VOC emissions (including Styrene) for the most recent consecutive 12 month period. Additional Information: Where applicable, each log shall have attached the documentation for all chemicals captured for disposal or recycle. Supporting documentation (MSDS sheets, purchase orders, etc.) shall be kept for each material which includes sufficient information to determine VOC emissions and Styrene emissions. All daily records required by this permit shall be completed within three business days and all monthly records shall be completed by the end of following month. All records required by this permit shall be maintained at the facility for at least three years, unless otherwise noted, and be made available to the Department and PCDEM for inspection upon request. [Rules 62-4.070(3) and 62-4.160(14)(b), F.A.C.] Comments: The record keeping is taken from Mr. Browns inventory and MSD sheets, and submitted to the Tom John Engineering consultant for addition into the spread sheets. The records are sent back to Mr. Brown to update monthly records and maintain in his personal computer. The hard copy records were reviewed for compliance of A -D and are maintained as required by above condition. A and B1-3 are covered in Section A and B of the Spreadsheet, B 4 and C are covered in Section C and D of the spreadsheets. (See copies) A.9. Emissions Calculation Methods: Emissions of Styrene and volatile organic compounds (VOCs) shall be determined as follows until notified by the Department or the Pinellas County Department of Environmental Management (PCDEM). Styrene emissions shall be determined using the following equation: Ms x EF Emissions (tons) = --------------- 2000 lb/ton where: Ms = amount of styrene containing material used (in tons) EF = emission factor (lb/ton) for styrene monomer content (from the table below) The applicable styrene emission factor shall be obtained (interpolated/extrapolated, if applicable) from the following table, in conjunction with the percent of available non-vapor suppressed (NVS) styrene monomer in the resin/gelcoat: % Monomer Resin** Hand (Non-Spray) Layup Resin** Mechanical Atomized Spray Layup Resin Mechanical Nonatomized* Spray Layup Gel Coat** Mechanical Atomized Spray Layup Gelcoat Mechanical Nonatomized* Spray Layup 18 39 51 39 138 67 19 41 54 41 148 70 20 43 58 43 158 79 21 45 61 45 168 88 22 48 64 47 178 97 23 50 68 49 189 106 24 52 71 51 200 115 25 55 75 54 211 124 26 57 78 56 221 133 27 59 82 58 233 142 28 62 86 60 244 151 29 64 90 62 256 160 30 67 94 64 269 169 31 69 97 66 281 178 32 71 102 68 295 187 33 74 105 71 308 196 34 77 112 74 322 205 35 80 118 77 336 214 36 83 127 80 354 223 37 86 136 83 371 232 38 90 146 86 390 241 39 92 156 89 408 250 40 95 166 93 427 259 41 98 176 96 446 268 42 100 187 99 466 278 43 112 192 102 477 287 44 117 202 105 495 296 45 122 212 108 513 305 46 127 221 111 532 314 47 133 232 115 551 323 48 138 242 118 571 332 49 143 252 121 590 341 50 148 263 124 609 350 * Nonatomized means any application technology in which the resin is not broken into droplets or an aerosol as it travels from the application equipment to the surface of the part. Nonatomized resin application technology includes, but is not limited to, flowcoaters, chopper flowcoaters, and pressure fed resin rollers. In addition, the device must be operated according to the manufacturer’s directions, including instructions to prevent the operation of the device at excessive spray pressures. ** The emission factors in these columns are based on a weighted average using the following assumptions: - Using the Unified Emission Factors - 20% by weight of the facility's usage of resins and gelcoats are for reinforced plastic composites production for items such as hatches and doors, but not for hulls and decks. - Using the National Marine Manufacturer Association's Factors – 80% by weight of the facility's usage of resins and gelcoats are for items such as decks and hulls. MMA emissions shall be determined by the following equation for each material. Emissions (tons) = Mmma x Cmma x 0.75 where: Mmma = amount of MMA containing material used (in tons) Cmma = MMA content (percent/100) VOC emissions shall be determined by the following equation for each material. These values shall be used in conjunction with the above Styrene and MMA emissions to determine total VOC. Emissions (tons) = Mvoc x Cvoc x 1.00 where: Mvoc = amount of VOC containing material used (in tons) Cvoc = VOC content (percent/100) [Construction Permit 1030534-001-AC; Rule 62-4.070(3), F.A.C.] Comments: The emissions are calculated following the above guidance , equations, and using the emission factors in the table listed above. The spreadsheets are calculating the emissions based on the table for they styrene and MMA content percentage with the emissions factors for the Resin Mechanical Nonatomized* Spray Layup (See spreadsheet Section B attachment). I reviewed the records with Mr. Brown and we compared the styrene content of resins with the table non atomized emission factors to insure, the consultant was using correct factors for emissions calculations. The emission factors were determined to be correct. |
| ( |  |  | Valid Permit [Rule 62-210.300] |
| ( |  |  | Changes to Facility/emission unit [Rule 62-210.300] Does the emission unit description above match what the facility is operating (Number of emission units or points, model number and serial number, etc.) Yes No |
| ( | C. Other: |
| Pollution Prevention Activities P2 Handouts Provided: P2 Brochure; P2 Manual; P2 Checklist Have any emissions reductions occurred Yes / No Chemical Substitution; Equipment Changes; Process Changes Chemical/Material Reuse; On-site Recycling; Other: addition of new product Comments: There have been one resin change to the facility product use at this time, the addition of MVR 8039 with 35 % styrene content, is an average range typical of the other resins already in use at the facility. |
| Closing Conference: I informed Mr. Brown that the facility appeared to be in compliance at this time. |
| Inspector(s): Shea Jackson, Pinellas County, Air Quality Division |
| Signature(s): Date: | Date: April 3, 2013 |
| ACCESS? | ( | ARMS? | ( |
| ESAIIR | ( |  |  |

H:\USERS\WPDOCS\Airqual\Air_Compliance\AQI\1030534 84744.doc

Tampa Yacht Manufacturing, LLC

4350 62nd Avenue North, Pinellas Park

Photo #1  Front Door	         Photo#2   Spraying fiber glass

Project Id:	84744	Permit No: 1030534-002-AO	Arms Number: 0534 001

Inspector:	Shea Jackson	Inspection Date / Time: 3/27/2013  / _______

Source (EU):	Fiberglass Boat Manufacturer

# Description:	[The front of the facility and entrance and lamination area in progress inside building]

Photo #1  Acetone		Photo#2  resin

Project Id:	84744	Permit No: 1030534-002-AO	Arms Number: 0534 001

Inspector:	Shea Jackson	Inspection Date / Time: 3/27/2013  / _______

Source (EU):	Fiberglass Boat Manufacturer

# Description:	[Drums of acetone and new resin product MVR 8039 ]

Photo #1  close containers	      Photo#2  Ventilation stack maintenance log

Project Id:	84744	Permit No: 1030534-002-AO	Arms Number: 0534 001

Inspector:	Shea Jackson	Inspection Date / Time: 3/27/2013  / _______

Source (EU):	Fiberglass Boat Manufacturer

# Description:[Facility keeping resins and solvent closed to prevent evaporation, log shows maintenance check

# of the stack ventilation system and filters ]

H:\USERS\WPDOCS\Airqual\Air_Compliance\AQI\1030534 84744.doc