1030129 002 62428

ANIMAL CREMATORY

COMPLIANCE INSPECTION CHECKLIST

INSPECTION TYPE:	ANUAL (INS1, INS2)		COMPLAINT/DISCOVERY (CI)

RE-INSPECTION (FUI)		ARMS COMPLAINT NO:

AIRS ID#: 1030129 002	DATE:    08/07/08		ARRIVE:    0945	DEPART:   1215

FACILITY NAME:    Pinellas Memorial Pet Cemetery

FACILITY LOCATION:	  6500 86th Avenue North

Pinellas Park,, FL

RESPONSIBLE OFFICIAL:  Linda Jones	PHONE:     727 544-1051

CONTACT NAME:     Linda Jones		PHONE:    727 544-1051

REMITTANCE YEAR:    2008       ENTITLEMENT PERIOD:      11/16/06		/	  	11/16/11

(effective date)	(end date)

PART I:  INSPECTION COMPLIANCE STATUS (check  only one box)

 IN COMPLIANCE         MINOR Non-COMPLIANCE 	 SIGNIFICANT Non-COMPLIANCE

PART II: TESTING/RECORDKEEPING REQUIREMENTS – Rule 62-296.401, F.A.C.

(check  appropriate box(es))

1.  Were there any objectionable odor(s) detected?-----------------------------------------------------------------------	 Yes	  No

2.  Was a visible emissions test conducted during this site visit according to EPA Method 9 (Ref.: Chapter

62-297, F.A.C.)?-----------------------------------------------------------------------------------------------------------	 Yes	  No

3.  In order to demonstrate individual source compliance, was an annual visible emissions test conducted 60

days prior to the AGP Notification form submission, and within 60 days prior to each anniversary date? (Rule

62-296.401(6)(j), F.A.C.)-------------------------------------------------------------------------------------------------	Yes	  No

4.  In order to demonstrate individual source compliance were the remaining applicable standards testing

completed  within 60 days prior to the AGP Notification form submission? (Rule 62-210.300(4), F.A.C.)	Yes	No

a)  Carbon Monoxide (CO) emissions equal to or below the requirements of 100 parts per million by

volume, dry basis, corrected to 7% O2 on an hourly average basis and tested according to EPA Method

10 (Ref.: Chapter 62-297, F.A.C.)?------------------------------------------------------------------------------------	Yes	  No

b)  Oxygen test performed according to EPA Method 3 (Ref.: Chapter 62-297, F.A.C.)?---------------------	Yes	  No

c)  Particulate matter emissions test with results equal to or below the requirements of 0.080 grains per

dry standard cubic foot (ft3)of flue gas, corrected to 7% O2 and tested according to EPA Method 5

(Ref.: Chapter62-297, F.A.C.)?------------------------------------------------------------------------------------------	Yes	  No

5.  Was all emissions testing conducted with the source operating at the manufacturers recommended

capacity?-------------------------------------------------------------------------------------------------------------------	Yes	  No

6.  Was CO & PM compliance demonstrated by submission of a test report for an identical crematory unit?	Yes	  No

7.  Was the Department notified at least 15 days prior to the date of the last formal compliance test?-----------	Yes	  No

8.  Was the required test report filed with the Department as soon as practical, but no longer than 45 days after

the test was completed?---------------------------------------------------------------------------------------------------	Yes	  No

PART III:  OPERATING/RECORDKEEPING REQUIREMENTS – Rule 62-296.401, F.A.C.

(check  appropriate box(es))

1.  Is there Continuous Emissions Monitoring System (CEMS) equipment installed on each unit to record temperatures in the 	primary and secondary chambers where there is a 1.0 second gas residence time in the secondary chamber combustion zone in 	accordance with the manufacturer’s instructions?-----------------------------------------------------------------------	Yes	  No

a)  Do temperature probes seem to be properly placed?-----------------------------------------------------------	Yes	  No

b)  Are the following records kept on file, available for inspection for at least two years following the recording of such  		     measurements, maintenance, reports and records?

1)  All measurements (including CEMS)---------------------------------------------------------------------	Yes	  No

2)  Monitoring device-------------------------------------------------------------------------------------------	Yes	  No

3)  Performance Testing Measurements	------------------------------------------------------------------	Yes	  No

4)  CEMS Performance Evaluation---------------------------------------------------------------------------	Yes	  No

5)  All CEMS or monitoring device calibration checks----------------------------------------------------	Yes	  No

6)  Adjustments--------------------------------------------------------------------------------------------------	Yes	  No

7)  Preventive maintenance performed on systems/devices-----------------------------------------------	Yes	  No

8)  Corrective maintenance performed on systems/devices-----------------------------------------------	Yes	  No

2.  Was this crematory unit constructed: (check only one  box)

a)   BEFORE  August 30, 1989? (If this box checked, continue on to #3 and skip #4)

b)   ON or AFTER  August 30, 1989? (If this box checked, skip #3 and continue on to #4)

3.  If constructed BEFORE August 30, 1989 is the:

a)  secondary chamber combustion zone providing at least a 1.0 second gas residence time @ 1600oF?	Yes	  No

b)  actual operating temperature of the secondary chamber combustion zone no less than 1400oF

throughout the combustion process in the primary chamber?------------------------------------------------	Yes	  No

c)  cremation in the primary chamber begun after the secondary chamber combustion zone temperature

is equal to or greater than 1400oF?-------------------------------------------------------------------------------	Yes	  No

d)  required monitoring equipment installed and operational, and providing continuous monitoring to

record the temperature at the point or beyond where 1.0 second gas residence time is obtained in the

secondary chamber combustion zone according to the manufacturer’s instructions?---------------------	Yes	  No

4.  If constructed ON or AFTER August 30, 1989 is the:

a)  volume in the secondary combustion zone sufficient to provide at least a 1.0 second gas residence time

@ 1800o F?----------------------------------------------------------------------------------------------------------	Yes	  No

b)  the actual operating temperature of the secondary chamber combustion zone no less than 1600oF

throughout the combustion process in the primary chamber?------------------------------------------------	Yes	  No

c)  secondary chamber combustion zone temperature equal to or greater than 1600oF before the cremation

process begins in the primary chamber?------------------------------------------------------------------------	Yes	  No

5.  Are appropriate leak-proof containers containing no more than 0.5 % (percent) by weight chlorinated

plastics used during the cremation of dead animals?--------------------------------------------------------------	 Yes	  No

a)  If the answer to question 4 above is YES, is certifying documentation from the manufacturer that they

are composed of 0.5% or less by weight chlorinated plastics kept on file at the site for the duration of

their use and for at least two years after their use?------------------------------------------------------------	 Yes	  No

b)	If plastic bags are used for the cremation of animals are they non-chlorinated and no less than 3 mils

thick?----------------------------------------------------------------------------------------------------------------	 Yes	  No

c)  Are dead animals, which have been used for medical or commercial experimentation, or other

materials, including biomedical wastes (Rule 62-210.200, F.A.C.), incinerated at this location?-----	Yes	  No

6.  During this review period, was the largest batch load cremated 500 pounds per hour or less?--------------	 Yes	  No

7.  Have all crematory operators been trained and certified by a Department-approved training program?---	Yes	  No

a)	Are copies of the training certificates all crematory operators kept on file at the facility for the duration

of the operator’s employment & for an additional two years after termination of employment?------	 Yes	  No

PART IV:  SPECIAL CONDITIONS AND PROCEDURES – Rule 62-296.401, F.A.C.

A.  New or Modified Process Equipment

1.  Since the last inspection has there been

a)  installation of any new process equipment?--------------------------------------------------------	Yes	 No

b)  alterations to existing process equipment without replacement?--------------------------------	Yes	 No

c)  replacement of existing equipment substantially different than that noted on the most

recent notification form?-------------------------------------------------------------------------------	Yes	 No

d)  If you answered YES to any of the above, did the owner submit a new and complete

notification form and appropriate fee (Rule 62-4.050, F.A.C.) to the appropriate DEP or

local program office?-----------------------------------------------------------------------------------	Yes	No

2.  If a crematory unit has been modified to the extent that a Department air construction permit

was required, have all operators been retrained to operate the modified unit?---------------------	Yes	No

3.  In the case of new or modified equipment, where a Department air construction permit was

required, has the owner submitted copies of all operator training certificates?--------------------	Yes	No

a) submitted within the 15 day required window following the training?-------------------------	Yes	No

Chris  Brodeur

_______________________________________________		___________________________________

Inspector’s Name (Please Print)				     Date of Inspection

_______________________________________________		___________________________________

Inspector’s Signature				     Approximate Date of Next Inspection

COMMENTS:  See the attached Pinellas County inspection report form for additional information

| FACILITY: Pinellas Memorial Pet Cemetery | PERMIT ID: 170 |
| --- | --- |
|  | DISTRICT: Southwest |
| ADDRESS: 6500 86th Avenue North | CONTACT PHONE: |
| Pinellas Park, FL | 727 544-1051 |
| ARMS NO: 1030129 002 | PERMIT NO: | Expiration Date: 11/16/11 Renewal Date: 10/17/11 |
|  | 1030129-005-AG |  |
|  |  | Test Date: 9/4/00 |
| EMISSION UNIT DESCRIPTION: Animal Crematory: Crawford, Model C500P, Unit No. 2 (western most unit). Maximum Batch load is 200 pounds Afterburner must operate at 1600 degrees F. |
| INSPECTION DATE: | ARMS INSPECTION TYPE: | COMPLIANCE STATUS: |
| 08/07/08 | INS2 or INS_____ | IN MNC SNC |
| Type of Inspection: Initial Re-inspection Complaint Drive-by Quarterly A. General Review: |
| 1. | Permit File Review Yes No |
| 2. | Introduction and Entry Yes No Comments: interview with operator Bill Thigpen and owner Linda Jones |
| 3. | Administrative Corrections. Within thirty (30) days of any minor changes requiring corrections to information contained in the registration form, the owner or operator shall notify the Department in writing. Such changes shall include: 1. Any change in the name, address, or phone number of the facility or authorized representative not associated with a change in ownership or with a physical relocation of the facility or any emissions units or operations comprising the facility; or 2. Any other similar minor administrative change at the facility. Is the Authorized Representative still: Linda Jones? Yes No Is the facility contact still: Linda Jones? Yes No [62-210.310(2)(d), F.A.C.] Comments: Bill Thigpen is the primary operator. |

| IN | MNC | SNC | B. Specific Conditions |
| --- | --- | --- | --- |
|  |  |  | Visible emissions - Visible emissions shall not exceed five percent (5%) opacity, six (6) minute average, except that visible emissions not exceeding fifteen percent (15%) opacity shall be allowed for up to six (6) minutes in any one (1) hour period. [Rule 62-62-296.401(6)(b)1., F.A.C.] Comments: The last annual visible emissions test, conducted on ___08/07/08___ demonstrated an opacity of __0__%. Southern Environmental was on site performing a ve test when I arrived. |
|  |  |  | Operating Temperature - Crematory units shall operate with a secondary chamber temperature of no less than : 1600 degrees Fahrenheit throughout the combustion process in the primary chamber, for construction applications received by the Department on or after August 30, 1989. Cremation in the primary chamber shall not begin unless the secondary chamber combustion zone temperature is equal to or greater than 1600 degrees Fahrenheit. [Rule 62-296.401(6)(c)1, F.A.C.], or ٱ 1400 degrees Fahrenheit throughout the combustion process in the primary chamber, for construction applications received by the Department prior to August 30, 1989. Cremation in the primary chamber shall not begin unless the secondary chamber combustion zone temperature is equal to or greater than 1400 degrees Fahrenheit. [Rule 62-62-296.401(6)(c)2, F.A.C.] Comments: Based on record reviews, the lowest operating temperature observed was __1600______ degrees Fahrenheit |
|  |  |  | Allowed Materials - Animal crematory units shall cremate only animal remains and, if applicable, the bedding associated with the animals and appropriate containers. Containers shall contain no more than 0.5 percent by weight chlorinated plastics as demonstrated by the manufacturer’s data sheet. If containers are incinerated, documentation from the manufacturers certifying that they are composed of 0.5 percent or less by weight chlorinated plastics shall be kept on-file at the site for the duration of their use and for at least two (2) years after their use. [62-296.401(6)(d), F.A.C.] Comments: There was not any documentation available as to the chemical composition of plastic bags (consisting of various garbage bags to used grocery bags) combusted with the bodies. Linda Jones will try to obtain MSDS but does not have much hope. To avoid this issue in the future, Bill Thigpen indicated that he will remove the animals from the bags before combustion. Follow up: I have spoken with P.C. Solid Waste’s Alex Crawford (on 09/10/08) regarding the issue of disposal of used garbage bags in the solid waste stream. Mr. Crawford stated that the incinerator operates @ 1200 deg. F. and therefore the disposal of these bags in the normal solid waste stream would not be cause for concern. |
|  |  |  | Equipment Maintenance - All animal crematory units shall be maintained in proper working order in accordance with the manufacturer’s specifications to ensure the integrity and efficiency of the equipment. If a crematory unit contains a defect that affects the integrity of the unit, the unit shall be taken out of service. No person shall use or permit the use of that unit until it has been repaired or adjusted. Repair records on all crematory units shall be maintained onsite for at least two (2) years. A written plan with operating procedures for startup, shutdown and malfunction of each crematory unit shall be maintained and followed during those events. Each unit’s burners shall be operated with a proper air-to-fuel ratio. If the unit so allows, the burners’ flame characteristics shall be visually checked at least once during each operating shift and adjusted when warranted by the visual checks. [62-296.401(6)(e), F.A.C.] Comments: Repair records were on premises and inspected back to 08/28/06. A written start up, shut down and malfunction (ssm) procedure does not exist. Facility allowed until close of business 08/13/08 to supply DEM with a ssm. A one page SSM was supplied on 08/18/08. |
|  |  |  | Continuous Monitoring Requirements- Each animal crematory unit shall be equipped and operated with a continuous monitor to record temperature at the point or beyond where 1.0 second gas residence time is obtained in the secondary chamber combustion zone in accordance with the manufacturer’s instructions. In addition, each crematory unit installed after February 1, 2007, shall be equipped and operated with a pollutant monitoring system to automatically control combustion based on continuous in-stack opacity measurement. Such system shall be calibrated to restrict combustion in the primary chamber whenever any opacity exceeding fifteen percent (15%) opacity is occurring. A complete file of all temperature measurements; all continuous monitoring system, monitoring device, and performance testing measurements; all continuous monitoring system performance evaluations; all continuous monitoring system or monitoring device calibration checks; and all adjustments, preventive maintenance, and corrective maintenance performed on these systems or devices, shall be recorded in a permanent legible form available for inspection. Continuous temperature monitoring documentation shall include operator name, operator indication of when cremation in the primary chamber was begun, date, time, and temperature markings. Pollutant monitoring system documentation shall include indication of when the opacity measurement system was cleaned and checked for proper operation in accordance with the manufacturer’s recommended maintenance schedule. The file shall be retained for at least two (2) years following the recording of such measurements, maintenance, reports, and records. [62-296.401(6)(h)(i), F.A.C.] Comments: Reviewed temperature charts for the months of _01/07 through 08/08. The last calibration on the temperature chart was on 08/15/07 (documented by itemized receipt)_. The temperature probe appears properly placed ( Yes or No) The facility demonstrated some confusion as to the proper documentation of the temperature charts. Inspector explained the need for precise marks where cremation begins and operator’s signature. |
|  |  |  | Test Notification - The owner or operator shall notify the Department, at least 15 days prior to the date on which each formal compliance test is to begin, of the date, time, and place of each such test, and the test contact person who will be responsible for coordinating and having such test conducted for the owner or operator. [62-297.310(7)(a)9. F.A.C.] Comments: The County was notified on ___07/23/08___, for the test that was conducted on _08/07/08_____ |
|  |  |  | Test Reports - The required test report shall be filed with the PCDEM as soon as practical but no later than 45 days after the test is completed. [Rules 62-213.440 and 62-297.310(8), F.A.C.] Comments: The last test was conducted on 08/07/08, and the test results were submitted on _not yet submitted_. |
|  |  |  | Process Rate Comments: The maximum batch load for this crematory unit is __200_____ pounds. The largest batch load cremated during this review period was __90___. |

| IN | MNC | SNC | C. Selected General Conditions and Procedures |
| --- | --- | --- | --- |
|  |  |  | Periods of Noncompliance - If, for any reason, the owner or operator of any facility operating under an air general permit pursuant to Rule 62-210.300(4)(a), F.A.C., does not comply with or will be unable to comply with any condition or limitation of the permit, the permittee shall immediately provide the Department with the following information: 1. A description of and cause of noncompliance; and 2. The period of noncompliance, including dates and times; or, if not corrected, the anticipated time the noncompliance is expected to continue, and steps being taken to reduce, eliminate, and prevent recurrence of the noncompliance. The permittee shall be responsible for any and all damages which may result. [62-210.310(3)(i), F.A.C.] Comments: |
|  |  |  | Valid Permit To avoid lapse of authority to operate, an owner or operator intending to use, or continue to use, an air general permit must submit the proper registration form and processing fee at least thirty (30) days prior to expiration of the facility’s existing air operation permit or air general permit. [62-210.310(2)(c)2., F.A.C.] Comments: The permit expires on 11/16/11. A new notification form is required to be submitted no later than 10/17/11. |
|  |  |  | Equipment Changes - The owner or operator shall maintain records of all equipment changes. In the case of installation of new process or air pollution control equipment, alteration of existing process or control equipment without replacement, or replacement of existing process or control equipment with equipment substantially different in terms of capacity, method of operation, material processed, or intended use than that noted on the most recent registration form, the owner or operator shall submit a new and complete air general permit registration form for the facility with the appropriate fee pursuant to Rule 62-4.050, F.A.C. to the Department, provided, however, that any change that would constitute a new major stationary source, major modification, or modification that would be a major modification but for the provisions of paragraph 62-212.400(2)(a), F.A.C., shall require authorization by air construction permit. [62-210.310(2)(e)., F.A.C.] Comments: no changes noted. |

D. Other:

Closing Conference Yes No Mrs. Linda Jones was apprised of the two conditions that would indicate a minor non-compliance issue with this permit. The first being the lack of MSDS sheets for the burned containers (bags). Mrs. Jones and operator Mr. Thigpen indicated that they would no longer cremate the remains inside of these containers and that the bags would be disposed of in the normal solid waste stream. The lack of a formal SSM was also addressed. Mrs. Jones stated that she would have this document drawn up and mailed to us in a timely matter.

Other Comments: As of 08/18/08 all issues regarding minor non compliance found have been resolved.

Inspector(s): Chris R. Brodeur, Pinellas County, Air Quality Division

Signature(s) Date:

CONTACT LOG? _________,    ACCESS? _________,    ARMs? ___________

H:\users\wpdocs\airqual\Air_Compliance\AQI\1030129 002 62428.doc